## Slide 1: Disregard bits in TB PPDU
Date: 2021-05-14
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Srinath Puducheri | Broadcom |  |  | 

## Slide 2: Discussion
The group decided to set all disregard bits in MU PPDU to 1.
However for TB PPDU in D0.4 those bits are not defined. Propose to define all of them to 1
From the USIG in TB PPDU spec:
From the Trigger definition spec:
The U-SIG Disregard And Validate subfield carries the value to be included in the Disregard and Validate subfields of the U-SIG field of the solicited EHT TB PPDUs. The mapping from the U-SIG Disregard And Validate subfield to bits in the U-SIG field for an EHT TB PPDU is defined in Table 9-29j4 (Mapping from Special User Info field to U-SIG-1 and U-SIG-2 fields in the EHT TB PPDU).

## Slide 3: SP #1
Do you support that all disregard bits in the USIG1/2 of the TB PPDU are set to 1?
  Note – USIG fields are copied from the trigger frame

## Slide 4: Motion #1
Move to add the following above Table 9-29j4 – The disregard bits are set to all 1s if dot11EHTBaseLineFeaturesImplementedOnly equals to true