## Slide 1: Q-D simulation & Modeling framework for sensing
Date: 2021-05-11
Authors:

## Slide 2: Outline
Abstract
The NIST Q-D Framework
Towards a sensing-enabled NIST Q-D Framework

## Slide 3: Abstract
IEEE 802.11bf PAR [1]: “This amendment defines modifications to the IEEE 802.11 medium access control layer (MAC) and to the Directional Multi Gigabit (DMG) and enhanced DMG (EDMG) PHYs to enhance Wireless Local Area Network (WLAN) sensing (SENS) operation in license-exempt frequency bands between 1 GHz and 7.125 GHz and above 45 GHz”
The NIST Quasi-Deterministic (Q-D) framework [2] is a suite of tools designed to obtain realistic DMG and EDMG performance evaluation (from the channel model to the application layer)
  In this contribution, we present our updates to the NIST Q-D framework channel software to enable the evaluation and development of sensing algorithms in the millimeter wave band.

## Slide 4: The NIST Q-D framework
Started in 2017
  Goal: Develop simulation models to evaluate DMG and EDMG end-to-end performance with high-fidelity channel and antenna models and system-level protocols.
  Publicly available using open-source ns-3 (https://github.com/wigig-tools)
5 software packages
  NIST Q-D Channel Realization Software
  NIST 802.11ay PHY
  ns-3 802.11ad/ay with Q-D channel
  Codebook Generator
  NIST Q-D Interpreter
Q-D Interpreter***
ns-3 802.11ad/ay
with Q-D channel**
Codebook Generator*
NIST Q-D Channel Realization software*
NIST 802.11ay PHY*
Channel
PHY
System-Level
Interpretation
* Matlab ** C++ *** Python
Antenna Model
Measurements

## Slide 5: The NIST Q-D framework for sensing
Overview of what is required to utilize the NIST Q-D framework in IEEE 802.11bf
In this contribution, we present our updates to the channel model
The PHY and system-level models would also need to be modified to include proposals under consideration by the group
Q-D Interpreter
ns-3 802.11ad/ay
with Q-D channel
Codebook Generator
NIST Q-D Channel Realization software
NIST 802.11ay PHY
 | NIST Q-D framework | NIST Q-D framework for sensing
Channel | Q-D methodology approach | Adapt the Q-D methodology for sensing applications
PHY | IEEE 802.11ay waveforms | Add IEEE 802.11bf waveform
System-Level | IEEE 802.11ad/ay procedures | Add IEEE 802.11bf sensing procedures
Codebook Generator | Phased-Antenna Array toolbox | ✓

## Slide 6: The NIST Q-D Channel realization software
The NIST Q-D Channel Realization software uses the Q-D methodology to generate Multi-Paths
Components (MPCs)
  Specular rays: Deterministic approach – Ray tracing (method of images)
  Diffuse components: Stochastic approach using a material library (reflectivity, number of pre-post cursors, etc.)
In [3], “A common ‘environment model/channel model’ is needed for the comparison of performance from different contributions. The environment should include:
  A few typical scenarios for WLAN sensing
    Specific configurations (size of environment, objects properties in the environment, frequency, bandwidth, antenna configuration)
  Target(s) to be sensed
    Specific configurations (location, trajectory, …) ”
We provide 8 IEEE scenarios [4] (Conference Room, Living Room, etc.)
  User can define their own scenario environment and parameters (number of nodes, reflection orders, frequency, bandwidth, etc.)
NIST Q-D channel: Raytracing performed for static environment
=> The NIST Q-D Channel realization software was modified to handle “Target(s) to be sensed”
IEEE Living Room Scenario

## Slide 7: The NIST Q-D Channel realization software for sensing
Introduced the notion of targets
  Targets are moving objects/people defined by
    Radar Cross Section (shape and dimensions)
    Physics of the targets (Reflection coefficient, rough surface parameters)
    Trajectory/Velocity
We use a two-steps modeling approach
  Ray Tracing of the targets to obtain geometrical parameters, i.e., AOA/AOD, delay (measurements independent) – Presented in this contribution
  Target model (measurements dependent)
    Loss induced by the target (MPCs gain)
    Generate a model from the measurements to the system parameters (RCS)
    Targeted to be available for D0.1 (January 2022)
  For the remaining of the contribution, we use an omnidirectional RCS
TX
RX
TG
1)
TX
RX
2)

## Slide 8: The NIST Q-D Channel realization software for sensing: Targets Ray Tracing
We considered three approaches
  Box approximation
  Polyhedrons
  Points in space
TX
RX
1)
TX
RX
3)
TX
RX
1)
TX
RX
2)
 | Pros | Cons
1) Box approximation | Simple objects to ray trace: scalable | Target could appear as invisible (Snell’s laws)
2) Polyhedrons | Include blockage | Computationally expensive
3) Points in space | Simple extension of the software | Does not include blockage
We chose the points in space approach
(a target can be made of multiple points in space)

## Slide 9: The NIST Q-D Channel realization software for sensing: Sensing targets
Sensing Receiver Signal Processing Module
NIST Q-D Channel Realization software with targets support
Interpolation
Doppler Range
Static Environment Geometry
Sensing Nodes Mobility
Targets: Mobility for every points in space and RCS
TX
RX
MPCs First Order
MPCs Second Order
Q-D Input
Q-D Output
Codebook Generator
Phased Antenna Array properties at TX and RX (number of elements, geometry, elements type, etc.)
Codebook Input
MPCs (AOA, AOD, Phase, delay and amplitude)

## Slide 10: The NIST Q-D Channel realization software for sensing: Targets Model (TBD)
TX
RX
TX
RX
TX
RX
Target model will depend on measurements: TBD
1) Ray trace Target points-in-space
2) Apply the target RCS
TG

## Slide 11: Summary
We presented the NIST Q-D framework and a first step to enable a sensing channel model at mmWave
  We focused on the channel model aspects, but each piece of the framework could be used to evaluate different aspects of IEEE 802.11bf
  [5] presents a use-case of human-target detection using the NIST Q-D framework
Next steps
  Measurements campaigns, modeling and integration to the NIST Q-D Realization Software

## Slide 12: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-2103-11-SENS-802-11-sens-sg-proposed-par.docx
[2] https://www.nist.gov/communications-technology-laboratory/wireless-networks-division/radio-resource-allocation-and
[3] https://mentor.ieee.org/802.11/dcn/20/11-20-1642-00-00bf-wlan-sensing-link-level-simulation.pptx
[4] https://mentor.ieee.org/802.11/dcn/15/11-15-1150-09-00ay-channel-models-for-ieee-802-11ay.docx
[5] https://mentor.ieee.org/802.11/dcn/21/11-21-0747-00-00bf-a-preliminary-channel-model-using-raytracing-to-detect-human-presence.pptx