## Slide 1: A-MPDU Issue For 802.11ah
Date: 2021-05-05
Authors:

## Slide 2: Abstract
The 802.11ah-2016 specification made changes to originator processing of MPDUs within an A-MPDU. The changes involve modifying the Fragment Number Field in each MPDU MAC header. It was not specified whether to make the changes before or after encryption and FCS creation, leading to a potential variety of implementations. In addition, there are no instructions for recipient processing.

## Slide 3: 802.11ah A-MPDU Originator Processing
Changes to A-MPDU originator processing were introduced for 802.11ah
  For example, in 802.11me d0.0 Section 10.25.6.7 Originator’s behavior:
    "During an accepted HT-immediate block ack agreement, the S1G originator of an A-MPDU that is not an SMPDU eliciting an NDP BlockAck frame shall set the Fragment Number subfield in the Sequence Control field of each MPDU in the A-MPDU to WinStartO + WinSizeO – 1 – SN, where SN is the value of the Sequence Number subfield in the corresponding MPDU within the A-MPDU.“

## Slide 4: Issues with the originator changes (1)
There are no instructions on when the originator modifies the fragment number (FN) field
  A literal implementation would change the FN field after encryption and after FCS creation since in the A-MPDU case aggregation occurs after these steps
  The FN field is part of the additional authentication data (AAD) so modifying it after encryption will cause decryption to fail unless the recipient masks the field out
  Modifying the FN field after FCS creation means it cannot be trusted

## Slide 5: Issues with the originator changes (2)
There are no instructions for the recipient to process the information and then reverse or ignore the changes to the FN field if necessary
There is a reference to the use of the modified FN field in the letter ballot comments on 802.11ah d1.0 (2013)
  See Comment 1219 in: https://mentor.ieee.org/802.11/dcn/13/11-13-1336-16-00ah-tgah-lb200-comments-on-d1-0.xlsx
  The comment resolution includes the sentence: "BA operation does not break because FN simply provides an offset to WinEndO helping the S1G recipient synch its BlockAck win parameters with those of the Originator.“

## Slide 6: Different 802.11ah implementations
On transmit some implementations do not modify the FN field and therefore do not expect a modified FN field on receive
On transmit other implementations modify the FN field after encryption and before FCS creation
These two implementation examples do not interoperate
No implementation appears to be using the modified FN field on the receive side

## Slide 7: Resolution Options
Remove the FN field related changes to A-MPDU originator processing introduced by 802.11ah-2016
Alternatively, specify the exact steps to be followed by the originator and recipient noting that
  The modified FN field should at least be protected by the FCS
  If WinStartO changes and some MPDUs need to be retransmitted then those MPDUs need to go through the encryption step and the FCS creation step again, depending on the design
    To avoid opening potential security holes it may be better to modify the FN field after encryption and prior to FCS creation
      The recipient would need to mask the FN field prior to decryption

## Slide 8: References