## Slide 1: Coexistence between radars and communication systems in the 60GHz band
Date: 2019-05-11
Authors:

## Slide 2: Abstract
The 60 GHz band is shared by communication systems and radar sensing systems
Each of these systems are based on different technology and are subject to different access rules
Coexistence among diverse uses is discussed in several regulatory bodies and industry forums

## Slide 3: Communication usages in the 60 GHz band
Gigabit and fast WLAN access (based on IEEE802.11ad & 11ay)
Low latency applications like AR/VR (based on IEEE802.11ad & 11ay)
Gigabit backhaul, fixed wireless access – indoor & outdoor (based on IEEE802.11ay)
Legacy mmWave point-to-point link (proprietary PHY & MAC)
Other protocols (e.g., Wireless HDMI)
and more…
Note that 11ay&bf can also be used for radar/sensing function. However, from a coexistence point of view, 11ay&bf radar behaves just like a communication 11ad/ay device.

## Slide 4: Radar usages in the 60 GHz band
Broadly speaking, mainly two types of radar: FMCW radar and 11ay/11bf based radar
Gesture recognition
Room sensing
Car in-cabin sensing (left behind child, driver sleepiness detection)
Health Application
  fall detection
  breathing/pulse tracking
Wall Penetrating Radar
and more…

## Slide 5: Communication Access
WLAN (11 access) –
  LBT (listen before talk)
    Follow NAV rules
    preamble detection
    energy detection
  TDD access
    Scheduled Access in service periods
    Used in narrow beam systems
  Channelization
    11ad/ay can set up BSS in different channels for better coexistence

## Slide 6: FMCW Radar Access
FMCW Radar is based on transmission of “sweep” CW pulse. One or more pulses form a burst, and bursts are periodically transmitted.
Radar parameters: EIRP, sweep BW, sweep/pulse duration, number of pulses in a burst and burst period are derived from the radar requirements (max range, range resolution, max doppler, doppler resolution) and HW limitations.
In general, radar transmits periodically based on the parameters.
There is no coordination of medium access
Due to the nature of FMCW signal, the impact from the collision of two FWCM radar signals is limited.

## Slide 7: Examples of FMCW Radar Pattern
.

## Slide 9: FCC existing rules for 60 GHz radars
60 GHz band (57-71 GHz) regulated as unlicensed intentional radiator through 47 CFR 15.255
- For personal radar, FCC 15.255(c)(3): “short-range devices for interactive motion sensing, the peak transmitter conducted output power shall not exceed −10 dBm and the peak EIRP level shall not exceed 10 dBm.”

## Slide 10: FCC waivers
Many waiver requests have been submitted to the FCC to permit radar operations in 60 GHz spectrum at higher power levels and aboard aircraft; several FCC Orders have been issued:
Google Soli field disturbance sensor. FCC Soli Waiver Order DA 18-1308
Leica Waiver for use on UAVs. FCC Leica Waiver Order DA 20-795
FCC recently approved several limited waivers under same technical terms as Google Soli for use in vehicles to identify children left behind in hot cars. FCC In-Vehicle Radar Waiver Order DA 21-407
DA-18-1308 Soli Waiver Order parameters were applied to subsequent Waiver Orders
“…allow the device to operate in the 57-64 GHz band at a maximum +13 dBm EIRP, +10 dBm transmitter conducted output power, and +13 dBm/MHz power spectral density”
“operate with a maximum transmit duty cycle of 10 percent in any 33 milliseconds (ms) interval”

## Slide 12: ETSI BRAN activity in the mmWave band
Band original designated 57-66 GHz, now extended to 57-71 GHz.
The group operates under the guidance of ERC Recommendation 70-03 (relating to the use of Short Range Devices)
Frequency Band |  | Power / Magnetic Field | Spectrum access and mitigation requirements | Modulation / maximum occupied bandwidth | ECC/ERC Deliverable | 
c1 | 57-71 GHz | 40 dBm e.i.r.p., 23 dBm/MHz e.i.r.p. density | Adequate spectrum sharing mechanism shall be implemented | Not specified |  | Fixed outdoor installations are not allowed.
c2 | 57-71 GHz | 40 dBm e.i.r.p., 23 dBm/MHz e.i.r.p. density and maximum transmit power of 27 dBm at the antenna port or ports | Adequate spectrum sharing mechanism shall be implemented | Not specified | ECC Report 288 | 
c3 | 57-71 GHz | 55 dBm e.i.r.p., 38 dBm/MHz e.i.r.p. density and transmit antenna gain ≥ 30 dBi | Adequate spectrum sharing mechanism shall be implemented | Not specified | ECC Report 288 | Applies only to fixed outdoor installations (note 3)
Note 3: Some CEPT Administrations, have an existing regulatory framework for the Fixed Service in 57-66 GHz and may implement a self-coordination mechanism similar to “light licensing” described in ECC Report 80

## Slide 13: non specific SRD in ERC REC 70-03
n1 | 57-64 GHz | 100 mW e.i.r.p. 10 mW output power | No requirement | Not specified |  | The frequency band is also identified in Annex 6 and within frequency bands in Annex 3
n2 | 61-61.5 GHz | 100 mW e.i.r.p. | No requirement | Not specified |  | 
These bands are covered by harmonized standard EN 305 550

## Slide 14: Radiotelemetry in ERC REC 70-03
f4 | 57-64 GHz | -41.3 dBm/MHz e.i.r.p. outside the enclosed test tank structure | No requirement | Not specified |  | For Tank Level Probing Radar (TLPR)
g3 | 57-64 GHz | * | * | Not specified | ECC/DEC/(11)02 | For Industrial Level Probing Radar (LPR). *See detailed requirements in related ECC Decision
These bands are for Level Probing Radar (LPR)
for the f4 band maximum transmission (outside the tank) is -41.3 dBm
for the g3 band maximum transmission is 35 dBm EIRP
In any case these are for indoor industrial LPR
harmonized standard is EN 302 729

## Slide 15: ETSI BRAN standard for the band
EN 302 567 – [c1] – Multiple-Gigabit radio equipment operating in the 60GHz band; Harmonised Standard for access to radio spectrum
EN 303 722 – [c2] – Wideband Data Transmission System (WDTS) for Fixed Network Radio Equipment in the 57-71 GHz band; Harmonised Standard for access to radio spectrum
EN 303 753 – [c3] – Wideband Data Transmission System (WDTS) for Fixed and Mobile Network Radio Equipment in the 57-71 GHz band; Harmonised Standard for access to radio spectrum

## Slide 16: EN 302 567 – status
Corresponds to mobile devices, no fixed indoor/outdoor access
Appropriate for 11ad devices
In development for many years
In the last stages of approval (waiting for national administrations approval, may be approved within a few months)
Coexistence Mechanism: LBT

## Slide 17: EN 303 722
Fixed indoor/outdoor access
Appropriate for TDD access in 802.11ay
Stable Draft, sent to EC consultant for editorial review
Channel Sharing Mechanism:
  Automatic Transmit Power Control
  Automatic Link Adaptation

## Slide 18: EN 303 753
Fixed and Mobile devices
In the early stages of development
Coexistence Mechanisms: not settled yet

## Slide 19: Potential coexistence issues: Impact of FMCW radar on communication links
Communication links can be affected by FMCW radar.
  Most sensitive current use case is AR/VR/XR. Large delay and delay jitter lead to negative user experience and motion sickness
Impact depends on FMCW operating parameters
  Link budget (EIRP, BW, distance, beamforming,…)
  Duty cycle limit and definition
  Activity time and pattern (e.g. burst duration and the idle period between bursts, etc.)

## Slide 20: Coexistence Concerns with Soli Waiver parameters
The FCC waiver granted to Google Soli (FMCW) introduces a 10% duty cycle limit over any 33ms period to address coexistence issues in the 60 GHz band
While this is a good step forward, there remain some coexistence concerns to be addressed
  Loophole in duty cycle definition: FMCW radar may transmit pulses for 10 µs followed by 90 µs of off time. While this complies with the 10% duty cycle requirement, the 90 µs of off time is too short for nearby 11ad/ay system to effectively utilize the channel. An FMCW radar thus could occupy the entire 7 GHz-wide band and continuously block/impact nearby 11ad/ay systems. Additional duty cycle limitation is needed to ensure that this does not occur.
  Potentially long transmission time (3.3 msec) also can impact the ability of other systems to access the channel and may impact latency (e.g., AR/VR)

## Slide 21: 60GHz Coex working group

## Slide 22: 60 GHz Coexistence Study Group for Communications and Radar
“The companies listed below share a strong interest in ensuring an environment of reasonable coexistence among all technologies reliant on 60 GHz spectrum. Together, with other interested companies, we have formed a 60 GHz Coexistence Study Group for Communications and Radar to (i) study modes of coexistence between radar and communication devices in the 60 GHz spectrum band, and (ii) work with regulatory bodies and other constituencies to encourage expanded uses of the 60 GHz unlicensed spectrum band.
Although the undersigned companies may have varying views about the merits of the pending waiver requests, we all agree that a long-term solution is needed to allow for technological innovation while ensuring reasonable coexistence of all technologies operating pursuant to the Commission’s 60 GHz unlicensed rules. To that end, we encourage the Commission to commence a comprehensive rulemaking proceeding to (i) to promote future applications, services, and devices in the 60 GHz unlicensed band, and (ii) address the range of technical and policy issues necessary to preserve reasonable coexistence between radars and field disturbance sensors, which require higher power levels than currently permitted, and other users of the 60 GHz unlicensed band.”
Source: Letter to the FCC, February 3, 2020
Latest members of CSG60 group: Google, Qualcomm, Intel, Facebook, Infineon, Socionext, Samsung, Continental, Vayyar, Texas Instruments (TI), Peraso, Acconeer

## Slide 23: Summary
There are coexistence issues in the 60GHz band between FMCW radar and WLAN communication (11ad/ay), especially for low latency applications
The FCC waiver conditions to permit higher-power sensing need to be adjusted to improve coexistence between communications and radar/sensing operations
The ”60GHz Coexistence Study Group for Communication and Radar” has been working on the issue.
  Encourage IEEE community to contribute to the coexistence discussion and formulate new coexistence rules in 60 GHz band