## Slide 1: Privacy Enhancement to avoid Element Fingerprint
Date: 2021-05-13
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Johannes Berg |  |  |  | 
Ilan Peer |  |  |  | 
Ido Ouzieli |  |  |  | 
Emily Qi |  |  |  | 
Ehud Reshef |  |  |  | 
Necati Canpolat |  |  |  | 
Daniel F Bravo |  |  |  | 
Robert Stacey |  |  |  | 
Notes: September 2012

## Slide 2: Background
Various privacy enhancements have been discussed
  PMKID [1]
  Password Identifier [2]
  “fingerprint” quasi-identifier [3-4], which is also called element fingerprint in [5]
Proposal in [3] is more general and can protect the whole (re)association request/response frame, but it needs asymmetric crypto, where trusted public key distribution is hard [2]
We demonstrate in this presentation that PMKID privacy enhancement can essentially be utilized to solve element fingerprint by protecting (re)association request/response frame without the need of asymmetric crypto

## Slide 3: Flow in [1] to avoid PMKID tracking
STA
AP
AP generates another PMKID2 attaches to the same PMKSA of previous PMKID1
STA generates another PMKID2 attaches to the same PMKSA of previous PMKID1
User MAC address 1
Use MAC address 2
Generate first-time PMKSA/PMK and PMKID1
Disconnect
Use PMKID1 to associate and avoid authentication to derive PMK again
Disconnect
Open Authentication
Use PMKID2 to associate and avoid authentication to derive PMK again
Open Authentication
Use MAC address 3

## Slide 4: Proposed Method
First, develop a standardized “private limited connection” to generate first-time PMKSA using existing authentication/association procedure
  Only standardized capability/operation element with standardized indication needs to be included in frames (ex probe/authentication/association) required to generate first-time PMKSA
  Remove all the unnecessary elements that is not required to generate first-time PMKSA
  Can use any randomized MAC address
STA
AP
User MAC address 1
Private limited connection to generate first-time PMKSA/PMK and PMKID1

## Slide 5: Proposed Method
First, develop a standardized “private limited connection” to generate first-time PMKSA using existing authentication/association procedure
Second, change MAC address and use authentication exchange (ex open) with PMKID in authentication frame to identify PMK and derive a key
  Open authentication exchange can not be tracked
  Standard KDF method (ex KDF-Hash-Length (PMK, Label, Context)) to derive key early to protect following (re)association request/response
STA
AP
User MAC address 1
Private limited connection to generate first-time PMKSA/PMK and PMKID1
User MAC address 2
Open Authentication with PMKID1

## Slide 6: Proposed Method
First, develop a standardized “private limited connection” to generate first-time PMKSA using existing authentication/association procedure
Second, change MAC address and use authentication exchange (ex open) with PMKID in authentication frame to identify PMK and derive a key
Third, use the derived key to protect the following (re)association request/response frame using existing standardized methods
STA
AP
User MAC address 1
Private limited connection to generate first-time PMKSA/PMK and PMKID1
User MAC address 2
Open Authentication with PMKID1
Protected (re)association request/response

## Slide 7: Proposed Method
First, develop a standardized “private limited connection” to generate first-time PMKSA using existing authentication/association procedure
Second, change MAC address and use authentication exchange (ex open) with PMKID in authentication frame to identify PMK and derive a key
Third, use the derived key to protect the following (re)association request/response frame using existing standardized methods
Fourth, utilize any PMKID privacy enhancement method. Repeat later.
STA
AP
User MAC address 1
Private limited connection to generate first-time PMKSA/PMK and PMKID1
User MAC address 2
Open Authentication with PMKID1
Protected (re)association request/response
AP uses PMKID privacy enhancement mechanism
STA uses PMKID privacy enhancement mechanism

## Slide 8: Benefits of the approach
Only use existing symmetric crypto
  No need for asymmetric crypto and trusted public key distribution
  Reuse most of the existing implementation
Private limited connection goes through full authentication procedure
  No problem with Rogue AP [3]
Avoid element fingerprint for the whole connection procedure
  standardized capability/operation element and standardized indication in private limited connection
  Remove all the unnecessary elements that is not required to generate first-time PMKSA
  Protect (re)association request/response frame
Leverage existing PMKSA caching and proposed PMKID change feature
  Most of the overhead absorbed by the first-time establishment of PMKSA
Can combine with SAE password identifier privacy enhancement if needed
  When private limited connection needs to be reestablished with SAE and password identifier due to PMKSA lifetime expiration

## Slide 9: Conclusion
We think element fingerprint should be a use case to be addressed in 11bi, and we prefer to utilize existing symmetric crypto
We demonstrate that existing PMKSA caching procedure can be utilized to avoid element fingerprint
  Define private limited connection to get first-time PMKSA
  Carry PMKID in authentication frame exchange (ex open)
  Use PMK of identified PMKSA to derive key and protect (re)association request/response frame
  Utilize PMKID privacy enhancement and repeat the procedure when connect with the same AP later

## Slide 10: Reference
[1] 11-20-336r2 MAC Privacy and PMKSA caching
[2] 11-21-541r0 protecting password identifiers
[3] 11-20-746r1 identifier privacy mechanism
[4] 11-19-0489r0 Client Privacy discussion
[5] Why MAC Address Randomization is not Enough: An Analysis of Wi-Fi Network Discovery Mechanisms
[6]https://www.cisco.com/c/en/us/td/docs/wireless/controller/9800/17-2/config-guide/b_wl_17_2_cg/_opportunistic_key_caching.pdf