## Slide 1: A Proposed Sensing Procedure for 802.11bf
Date: 2021-05-16
Authors:

## Slide 2: Abstract
This submission presents a sensing procedure modelled after the sounding procedure in 802.11ac and 802.11ax.

## Slide 3: Background
802.11 defines a sounding procedure for beamforming as shown in the Figure below.
The sounding procedure starts with an NDPA announcement frames sent by the beamformer and defines those STAs participating the sounding process and related parameters.
NDP Announcement
Frame
NDP
Polling for
beamforming report
Beamformer
Beamformees
Reports

## Slide 4: Sensing Procedure (I)
Sensing Initiator: Usually resides at the AP but maybe also a non-AP STA. It initiates the sensing process and determines which devices are requested to send sensing feedback.
Sensing Responder: Receives the sensing request, e.g. sensing reference sequence and sends feedback back to the sensing initiator.
AP
Sensing Initiator
Sensing
Responder
Sensing
Responder
Object

## Slide 5: Sensing Procedure (II)
Sensing Announcing (SA) frame includes the identity of devices to participate in sensing and from which measurement feedback is required. It may also include other parameters such as the type of the feedback, etc.
Sensing Reference Sequence may be LTF-like sequence
Sensing Feedback Report may be transmitted in parallel (as shown above) or serially by polling each responder
Sensing
Announcement (SA) Frame
Sensing
Reference
Sequence
Sensing
Feedback
Request
Sensing
Feedback
Report
Sensing
Feedback
Report
Initiator
Responder
Responder
Setup
Phase
Measurement
Phase
Reporting
Phase

## Slide 6: Sensing Procedure (III)
Similar to VHT and HT NDPA frames, Sensing Announcement (SA) frame can be a control frame. The format of the SA frame is TBD.
Sensing Reference Sequence frame is similar to NDP frame and may be called Sensing NDP frame. Format is TBD.
The Sensing Feedback frame can be defined as a new category (Sensing Category) of Action frame. Format is TBD.

## Slide 7: SP
Do you agree to include the sounding sequence shown in slide #5 in the TGbf SFD? Formats of individual frames and the reference sequence are TBD.

## Slide 8: References