## Slide 1
NFRP TF Random Access for Unassociated STAs and Power Saving
Date: 2021-10-30
Authors:

## Slide 2: Introduction
The efficiency of current UORA is very low:
  About 37% (Slotted ALOHA)
NFRP based random access is proposed in [1]
  By reusing the 802.11ax NFRP, the NFRP based RA can increase efficiency up to 74%
When there are many STAs attempting UORA, a lot of collisions are expected due to low efficiency
The new NFRP TF Random Access scheme can be used for various scenarios
  Unassociated STAs
    When there are many unassociated STAs, AP needs to check the population of the STAs
  Multi-link power saving
    Multi-link presence check can be used NFRP TF random access

## Slide 3: NFRP TF random access for Unassociated STAs
Since AP doesn’t know how many unassociated STAs will attempt random access, it is difficult for AP to allocate resources.

## Slide 4: NFRP TF random access for Unassociated STAs
Probe storm can be prevented using NFRP TF random access
  A specific resource can be reserved as a “System information request tone”
  Energy detection on the tone can trigger the system information transmission
    Probe storm can be prevented

## Slide 5: NFRP TF random access for Unassociated STAs – Multi-link
NFRP TF random access can be used in Multi-link

## Slide 6: NFRP TF random access for ML power saving
STAs in power saving mode needs to transmit either PS-Poll or QoS Null through the link it shall retrieve the BUs.
Tone allocation can be utilized for the presence check of STAs

## Slide 7: Conclusion
Since the current UORA has very low channel access efficiency, a new channel access scheme with better efficiency is required.
  Reusing IEEE 802.11ax NFRP random access is a good suggestion
In this presentation, possibilities of using NFRP TF Random access in various scenarios are shown.
  Unassociated STAs (Single-link, Multi-link)
  Power saving
  Probe response storm prevention
NFRP TF random access should be considered in R2 for better performance.

## Slide 8: Reference
[1] 11-20/1903r1 Random Access for 11be
[2] Draft P802.11ax_D8.0