## Slide 1: ANQP Elements Augmentation Proposal
Date: 2021-06-14
Authors:
May 2021

## Slide 2: Abstract
This submission proposes two new elements for ANQP that would be of use for WFA and WBA use cases.

## Slide 3: Comment Resolution
Comment | Proposed Change | Resolution
Modern networks allow more than one types of credentials, but may not allow all types | Specify credential types that can be advertized as allowed, along with the allowed validation method and requried lifetime for these credentials | Accept, define a new ANQP element that clarifies which credentials are accepted, along with the acceptation method.
Privacy is a primary determinator for network atatchement choice. Without knowing if the local entwork requires a real identity or accepts anonymous IDs, users are forced tor evlea more than they want or need | Define a privacy indicator element that clarifies if the network allows for anonymous connections | Accept, define a Privacy indicator element for ANQP
93
94

## Slide 4: Background – ANQP in Federations
In large federations (where multiple venues may allow for multiple sources of identities), the multi-to-multi relationship makes it difficult for the STA profile to understand the required identity and credential expectations of the venue, and how these map to the identity profile that the STA is configured to use.
This ambiguity can cause unnecessary overhead or may cause the STA to send discovery messages that may not be required by the infrastructure (and that can in turn, affect the user privacy or result in a lower user experience).
This submission proposes additional ANQP elements that can assist a STA in clarifying the required identity and credential expectations of the infrastructure.

## Slide 5: Advertising Credential Types
In a multi-to-multi environment (e.g., multiple venue members of a federation), each venue may advertise a RCOI (Roaming Consortium) that allow STAs to provide multiple identities, each with different credential type requirements (e.g., simple email, proof of residence, identity validation or other). Each venue may also accept multiple types of credentials. However, the venue may also be constrained in the type of credentials it can accept (e.g., ‘only accept credentials where the user identity can be verified’) – this is a limitation in WBA and WFA scenarios
It is useful to define the credentials types that the venue can accept, as this may be a subset of the credentials accepted by all of the RCOI members within a federation (e.g., type of credentials accepted, with type of verification accepted, credential lifetime)
The venue may also mandate that the user connects with a verifiable outer identity. In other cases, the venue requirements are satisfied with an anonymous outer identity, provided that an authentication source validates the user credentials. It may be useful to specify if the venue requires a ‘real’ outer identity or not, potentially removing the need for clients to expose their user identity where it is not needed.

## Slide 6: Credential Types ANQP-Element
Suggest insert after 9.4.5.29
Credential Types ANQP-Element
The Credential Types ANQP-element provides a STA with the information about the types of credentials accepted via that AP. One or more types of credentials are listed.
The credential types subfield includes for each type of accepted credential, the credential type (table 1), the required validation type (table 2), the minimum lifetime required for the credentials, and a privacy indicator.
Info ID
Length
Credential Types
Category group
Category type
B0
Lifetime
2
2
variable
octets:
Bits:
B7
B18
B8
B19
B22
Privacy Indicator
B23
Validation
B15
B16

## Slide 7: Credential Types ANQP-Element
The credential category subfield includes a category of credentials accepted by an AP. The list uses an augmented baseline Table 9-66. Many elements in the table already express business types that can not only be venues, but can also provide credentials commonly used for public venue authentication (the examples below, are already in Table 9-66)
Credential Category | Venue group code | Venue type code
Any | 0 | 0
Enterprise | 2 | 0
Education or Research | 3 | 0
Loyalty or Merchant | 6 | 0
Hospitality | 7 | 2
Automotive | 10 | 1
Aviation | 10 | 2

## Slide 8: Credential Types ANQP-Element
Insert after 9.4.5.29
The credential category subfield includes a category of credentials accepted by an AP. The list uses the augmented baseline Table 9-66, for businesses that are not included in the list of physical venues but provide credentials.
Credential Category | Venue group code | Venue type code
Misc entities | 12 | 12
Service Provider | 12 | 1
Cloud or Social Media Provider | 12 | 2
Cable Industry | 12 | 3
Government | 12 | 4
Reserved | 12 | 5-255

## Slide 9: Credential Types ANQP-Element
Insert after 9.4.5.29
Credential Types ANQP-Element (Cont.)
The validation method subfield lists the type of credential validation that must occur for the credentials to be deemed valid.
The weakest supported method is indicated (e.g., a validation method of 3 indicates that methods 3, 4 and 5 are accepted)
Validation method | Value | Notes
No verification | 0 | Credentials do not need to be verified
Any method allowed | 1 | Any method, from 1 to 5, is accepted
Email verification | 2 | 
SMS verification | 3 | 
Government ID | 4 | e.g., account obtained by showing a Government ID
Government issued credentials | 5 | e.g., a certificate emitted by a Government
Reserved | 6-7 | 

## Slide 10: Credential Types ANQP-Element
Suggest insert after 9.4.5.29
Credential Types ANQP-Element (Cont.)
The Lifetime subfield indicates the minimum age of the credentials to be acceptable, in units of year quarters (e.g., a value of 8 represents that the matching credentials are accepted if the account is 8 quarters or more, or 2 years, old; a value of 0 indicates that the matching credentials are accepted if they are 0 quarters or more).
When set, the Privacy indicator indicates that this network requires the user to expose a real contactable identity to the network (usually for legal purposes). The default value is 0, indicating that this network will accept anonymous roaming.

## Slide 11: Comment Resolution
Comment | Proposed Change | Resolution
Users offered the choice between 2 networks may prefer to attach to the one that provides the best SLA, or for which they have an offload agreement with. However, such indication is not provided, limiting the quality of the experience for the user | Define a settlement indicator, and an SLA indicator, that clarifies if the network will accept all roaming, offer paid services or free services only, and if the network supports a form of SLA. | Accept, define a new ANQP element that clarifies the settlement and SLA values for the network
95

## Slide 12: SLA ANQP-Element
Insert after 9.4.5.29
SLA ANQP-Element
The Service Level Agreement (SLA) ANQP-element provides STA with the information about the type of roaming supported by the local network, and the SLA offered by the AP for a given roaming type.
Info ID
Length
Primary
SLA Indicator
B0
2
2
variable
octets:
Primary Settlement Indicator
Bits:
B1
B8
B2
B3
B7
SLA Details
SLA Indicator
Settlement Indicator
Second SLA Indicator
Second
Settlement Indicator
1
SLA Indicator
Settlement Indicator
SLA Details
B4
B5
B6
(nx8)

## Slide 13: SLA ANQP-Element
Insert after 9.4.5.29
SLA ANQP-Element (Cont.)
The Settlement Indicator subfield indicates if the network will accept all roaming, offers paid services or free services. The SLA Indicator subfield indicates the SLA that the network offers for the associated settlement. When the SLA is the same for all settlement values, the Settlement and SLA values are indicated in the first half of the element (e.g., 0011 0000 indicating a Gold SLA level for everyone (paid and free services) .
The SLA Details field is an optional string that indicates the details of the SLA (e.g., minimum bandwidth, max jitter or delay, etc.) The content of this subfield is beyond the scope of this specification.
Settlement Indicator Value | Settlement
0 | All
1 | Free services
2 | Paid services
3 | Reserved
SLA Indicator Value | SLA Level
0 | No SLA
1 | Bronze
2 | Silver
3 | Gold

## Slide 14: Straw Poll
Do you support the addition of the two ANQP elements presented in this submission?
Yes
No
Abstain