## Slide 1: Non-TB and TB measurement procedure for WLAN sensing
Date: 2021-06-29
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sang Kim |  |  |  | sanggook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
June 2021

## Slide 2: Introduction
We introduced the various measurement procedures for WLAN sensing by considering roles of initiator/responder and transmitter/receiver, AP initiated and non-AP STA initiated scenarios in [1].
And, regarding on the measurement procedure, we got following agreement on the direction.
  Do you agree that NDP based measurement procedure is supported for channel measurement in the sub-7GHz band for 11bf?
    Results: 26Y/7N/17A
In this contribution, we discuss the measurement protocol that provides two feedback mechanisms, i.e., TB and non-TB which are based on the NDP transmission.

## Slide 3: Sounding protocol in WLAN
To know the channel state information in the sub-7GHz band, the sounding protocol is defined in [2, 3]
  For example, the followings are defined in 11ax for channel sounding
    The HE sounding NDP that does not include the data field is used for sounding.
    The HE sounding protocol provides two feedback mechanisms, defined as HE non-trigger-based (non-TB) sounding and HE trigger-based (TB) sounding.
      And, non-TB sounding and TB sounding can be distinguished by using a trigger frame for request of feedback frame from the STA(s).
    In addition, both methods are also defined in 11az for the ranging feedback.

## Slide 4: Non-TB and TB sounding (1/2)
Non-TB and TB sounding procedure in 11ax
  Ex. HE non-TB sounding
  Ex. HE TB sounding

## Slide 5: Non-TB and TB sounding (2/2)
Supporting in WLAN standards
  The Trigger frame defined in 11ax is used to solicit the response frames from the STA(s). In accordance with whether using the Trigger frame or not on the sounding procedure, we can distinguish the sounding as Non-TB or TB.
 | 11n | 11ac | 11ax | 11az | 11be
Non-TB | O | O | O | O | O
TB | x | x | O | O | O

## Slide 6: Sensing measurement protocol (1/3)
Similar to the existing sounding process, the sensing measurement is also performed to get the channel information through a single STA or multiple STAs.
Therefore, we can reuse the sounding protocol defined in 11ax or 11az for sensing measurement.
  In accordance with a sensing scenario or procedure, we propose to consider two measurement procedures, i.e., non-TB and TB, in WLAN sensing.

## Slide 7: Sensing measurement protocol (2/3)
  Among the various sensing scenarios, first we can consider that the sensing measurement is performed per STA separately. In this case, we can consider the use of the non-TB sounding procedure.
    Example 1 for non-TB measurement with feedback
    Example 2 for non-TB measurement without feedback

## Slide 8: Sensing measurement protocol (3/3)
  On the other hand, we can also consider the sensing measurement case that multiple STAs perform the channel measurement simultaneously.
    In this case, to get the feedback from the multiple SATs efficiently, we can reuse the TB sounding protocol for sensing.
    Example for TB measurement for sensing

## Slide 9: Summary
The current WLAN system has defined the sounding protocols for the channel measurement.
  i.e., Non-TB sounding and TB sounding
  Each sounding protocol can be applied independently according to whether the Trigger frame is used or not to request the measurement feedback.
And, since WLAN sensing is based on the conventional WLAN system, we can simply reuse these sounding protocols for the measurement procedure of sensing by considering various sensing operations.
  Based on the use of the Trigger frame for STA(s), we can define the non-TB and TB measurement procedures as described in slides 7 and 8.

## Slide 10: Straw Poll #1
Do you agree to add the following into 11bf SFD ?
  In measurement phase of sensing session, the NDP can be used for the channel measurement (e.g. CSI) between sensing transmitter and sensing receiver(s) in sub 7Ghz band.
    NDP format for sensing is TBD.
  Y/N/A

## Slide 11: Straw Poll #2
Do you agree to add the following into 11bf SFD ?
  11bf supports the non-TB and TB measurement procedure.
    The non-TB and TB measurement procedures are distinguished by the presence of a Trigger frame.
    Trigger Frame is TBD.
    Y/N/A

## Slide 12: Straw Poll #3
Do you agree to add the following into 11bf SFD ?
  11bf supports the following common procedure in non-TB and TB measurement.
    A sensing transmitter may transmit the NDP Announcement frame with one or more STA information.
    NDP follows SIFS after the NDP Announcement frame.
    The feedback may not be present in Non-TB measurement.
    The details for NDPA is TBD.
    Y/N/A

## Slide 13: Reference
[1] 11-21/419r1, Sensing Measurement sequence of 11bf
[2] IEEE P802.11-REVmd/D5.0
[3] IEEE P802.11ax/D8.0