## Slide 1: Sensing measurement operation bottom up
Date: 2021-06-28
Authors:

## Slide 2: Abstract
Introduction to the limitations of the sub 7GHz part of the .11bf spec
The purpose of the proposal is to present existing supportive features defined in the amendments referred to in PAR and CSD, which can be used as a reference in defining new .11bf solutions. One criterion is presented to help to craft and to review the potential .11bf solutions.

## Slide 3: Hierarchy of the supportive features in the referenced amendments
Sensing specific PHY features: NDP sounding, LTF security, CSI reporting
Dependent MAC features:
Pairwise key hierarchy
Supporting MAC features:
Associated and Unassociated secure authentication
Exchange of protected action frames
Optional MAC features:
TDLS based peer to peer connection
1
2
5
6
AP centric TB sounding, maintained by control frames:
NDP announcement
Sounding trigger
Tightly coupled Lower MAC features:
Non- AP centric non-TB sounding, maintained by control frames
NDP announcement
3
4

## Slide 4: Background 11-19-2103-11-SENS-802-11-sens-sg-proposed-par
5.2.b. Scope of the project:
This amendment defines modifications to the IEEE 802.11 medium access control layer (MAC) and to the Directional Multi Gigabit (DMG) and enhanced DMG (EDMG) PHYs to enhance Wireless Local Area Network (WLAN) sensing (SENS) operation in license-exempt frequency bands between 1 GHz and 7.125 GHz and above 45 GHz.
This amendment defines modifications to the PHY service interface of the High Throughput (HT), Very High Throughput (VHT), High Efficiency (HE) and Extremely High Throughput (EHT) PHYs.
5.3 Is the completion of this standard dependent upon the completion of another standard: Yes
If yes please explain: As defined in 5.2.b, to enhance WLAN sensing, this amendment augments PHY and MAC capabilities defined in the IEEE P802.11ax, IEEE P802.11ay, IEEE P802.11az and IEEE P802.11be amendments and the IEEE P802.11 revision standard

## Slide 5: Executive summary
The diagram represents the building blocks of the .11bf amendment that are inherited from known .11 .11ax, and .11az solutions
Layers 1 and 2 represent the PHY features not to be changed as defined in the PAR and CSD
Proposal of the features to be included in the .11bf amendment should explain how those building blocks are built and used
Any changes in the overlying layers (3-6) should be limited so as not to require changes in the underlying layers, which in turn may require changes in layers 1 and 2

## Slide 6: SP1
Do you agree that the building blocks presented in slide 3 represent the features of existing amendments, that are most relevant to the sub 7 GHz part of the .11bf amendment?

## Slide 7: SP2
Do you agree that the approach presented in slide 5 may help to craft and review new features defined to be included in the sub 7 GHz part of the .11bf amendment?