## Slide 1: Coexistence between radars and communication systems in the 60GHz band – U.S. Update
Date: 2021-07-13
Authors:

## Slide 2: Abstract
This is a follow-up to our May 2021 presentation on sharing the 60 GHz band between by communication systems and radar sensing systems
  Each of these systems use different technologies and are subject to different access rules
  Coexistence among diverse uses is under discussion in several regulatory bodies and industry forums
The U.S. FCC plans to adopt on July 13, 2021, a Notice of Proposed Rulemaking (in ET Docket No. 21-264) proposing modifications to its 60 GHz rules to allow higher power radar operations while maintaining appropriate protections for incumbent unlicensed communications systems

## Slide 3: Communication usages in the 60 GHz band (review)
Gigabit and fast WLAN access (based on IEEE 802.11ad & 11ay)
Low latency applications like AR/VR (based on IEEE 802.11ad & 11ay)
Gigabit backhaul, fixed wireless access – indoor & outdoor (based on IEEE 802.11ay)
Legacy mmWave point-to-point links (proprietary PHY & MAC)
Other protocols (e.g., Wireless HDMI)
and more…
11ay&bf also can be used for radar/sensing function. From a coexistence point of view, 11ay&bf radar/sensing behaves exactly like an 11ad/ay communications device.

## Slide 4: Radar usages in the 60 GHz band (review)
Radar types include FMCW radar, pulse radars, and 11ay/11bf based radar to provide these capabilities:
Gesture recognition
Room sensing
Car in-cabin sensing (left behind child, driver sleepiness detection)
Health Application
  fall detection
  breathing/pulse tracking
Wall Penetrating Radar
and more…

## Slide 5: Communication Access (review)
WLAN (11 access) –
  LBT (listen before talk)
    Follow NAV rules
    preamble detection
    energy detection
  TDD access
    Scheduled Access in service periods
    Used in narrow beam systems
  Channelization
    11ad/ay can set up BSS in different channels for better coexistence

## Slide 6: FMCW Radar Access (review)
FMCW Radar is based on transmission of “sweep” CW pulse. One or more pulses form a burst, and bursts are periodically transmitted
Radar parameters: EIRP, sweep BW, sweep/pulse duration, number of pulses in a burst and burst period are derived from the radar requirements (max range, range resolution, max doppler, doppler resolution) and HW limitations.
In general, radar transmits periodically based on operational needs
There is no coordination of medium access
Due to the nature of FMCW signal, FMCW radar signals self-interference is limited

## Slide 7: Potential coexistence issues (review) Impact of FMCW radar on communication links
Communication links can be affected by FMCW radar.
  Most sensitive current use case is AR/VR/XR. Large delay and delay jitter lead to negative user experience and can cause motion sickness
Impact depends on FMCW operating parameters
  Link budget (EIRP, BW, distance, beamforming,…)
  Duty cycle limit definition and operational modes
  Activity time and pattern (e.g., burst duration and idle period between bursts)

## Slide 8: U.S. FCC Draft NPRM in ET Docket No. 21-264
Draft NPRM (released June 22, 2021):
Proposes allowing radar/sensing devices in 57-64 GHz with 20 dBm avg EIRP, 13 dBm/MHz avg PSD, 10 dBm conducted power, and 10% duty cycle in any 33 ms interval; Seeks input on closing duty cycle “loophole” by requiring any off-time period between two successive radar pulses less than 2 msec to be considered “on time” for purposes of computing the duty cycle.
Proposes allowing mobile (in addition to fixed) radars in the 60 GHz band
In the 61.0-61.5 GHz band only, proposes permitting mobile radar/sensing devices to the same 40 dBm EIRP thas is already permitted for fixed radar/sensing devices in this 500 MHz-wide band.
Seeks input on permitting radar/sensing devices that use LBT, sensing, or another coexistence means to operate in entire 57-71 GHz band at the same power level (i.e., 40 dBm EIRP) communication devices are permitted to use.

## Slide 9: Importance of Closing Duty Cycle Loophole
  To enable coexistence with 60 GHz communications devices and applications, the FCC should require any radar off-time period between two successive radar pulses that is less than 2 msec to be considered “on time” for purposes of computing the duty cycle
  This additional duty cycle condition is needed to close a loophole because FMCW radars may occupy the entire 7 GHz-wide 57-64 GHz band and continuously block/impact nearby 11ad/ay systems – even with a 10% duty cycle – by using a very short pulse.
  For example, FMCW radars may transmit for 10 µs followed by 90 µs of off time, but the 90 µs of off time is too short for nearby 11ad/ay system to effectively utilize the channel. An FMCW radar thus can occupy the entire 7 GHz-wide band and continuously block/impact nearby 11ad/ay systems. Additional duty cycle limitation is needed to ensure that this does not occur.
  Also, a long transmission time of 3.3 msec also can impact the ability of other systems to access the channel and may impact latency (e.g., AR/VR)
  Recent FCC waivers include the 2 msec loophole closing condition. See, e.g., DA-21-811A1.pdf DA-21-812A1.pdf DA-21-813A1.pdf

## Slide 10: U.S. FCC NPRM in ET Docket No. 21-264
Final NPRM to be released in mid-July – following its approval by the FCC on July 13, 2021
The Final NPRM may include non-material modifications to the draft NPRM based on inputs to the FCC since its release of the Draft NPRM
We are available to answer any questions or help any IEEE members provide comments to the FCC on the 60 GHz NPRM
Comments and Reply Comments likely will be due in September and October 2021 timeframe, 30 days and 60 days after the NPRM is published in the U.S. Federal Register

## Slide 11: Summary
There are coexistence issues in the 60 GHz band between FMCW (and other, e.g., pulsed) radars and WLAN communications (11ad/ay), especially for low latency applications
The U.S. FCC plans to adopt on July 13, 2021, a Notice of Proposed Rulemaking (in ET Docket No. 21-264) proposing modifications to its 60 GHz rules to allow higher power radar operations while maintaining appropriate protections for incumbent unlicensed communications systems
IEEE community should respond to NPRM and promote rules to ensure improved coexistence between communications and radar devices