## Slide 1: TGbh Excerpts of WBA Document “Wi-Fi Identification Scope”
Date: 2021-07
Authors:

## Slide 2: Objective
Provide an overview
Summarize identified impacts and link to identified Use Cases

## Slide 3: 1 - MAC Randomization Impacts
MAC-Based Access Control
  Deny or allow access based on MAC is ineffective
  Pay Per Use (PPU) associated with MAC ineffective
  Complimentary limited time services ineffective
“Passpoint” Profiles
  The acceptance of terms & conditions in Section 10.1 indicates that the AAA server saves the timestamp associated with the STA MAC address.
  Certificate Enrollment in Section 7.6.1/7.6.4, the STA MAC address is one of the options to identify a Wi-Fi client device and bind the certificate to.
  DevDetail MO vendor specific extension Section 9.2, the DevDetail MO contains a Wi-FiMACAddress node which the STA fills with its currently set MAC address

## Slide 4
Client Steering
  Different bands with different SSIDs (split-SSID on 2.4GHz and 5GHz), will see different MAC addresses on the different SSIDs, which will break MAC-based (band-)steering between the SSIDs. Any network supporting more than one SSID will suffer similar Wi-Fi client steering issues.
MAC Collisions
  understand that this is an exceedingly unlikely event and so not of any real concern.
Physical Layer Analytics
  identify a unique device consistently over time
  no longer be possible to identify manufacturer from OUIs or CIDs in the IEEE registry for the purposes of troubleshooting, diagnostics, and analytics
Accounting and billing issues
  rates rely on a unique device identifier. [This could be accomplished instead with proper support for Chargeable-User-Identity (CUI)].

## Slide 5
QoS and QoE
  APs that form the network hold a synchronized list of MAC address to QoS/QoE mapping to ensure that Wi-Fi clients receive a uniform QoS/QoE treatment throughout the full network.
DHCP and ACLs
  Devices asking for IP addresses or renewal are identified by MAC address
  Where MAC address instrumental in providing an identifier for use in ACLs - the MAC itself, the IP Address, or a MAC-based hostname – then the ACL will not function as intended.
Lawful Intercept LI
  LI may use the uniqueness of a Wi-Fi device’s MAC address to facilitate identification
  MAC address is used to help link IP sessions to particular users’ devices

## Slide 6: 2 - Wi-Fi Identification Standards
Home Networks
  Steering across ESSs
  Access time restrictions, QoS and QoE controls
  L2 analytics
  Support for IoT and legacy devices (e.g., registration).
  Providing restricted access
Community Networks
  Access Control
  MAC or IP based QoS (need to be tied to UID/DID every session.

## Slide 7
Enterprise/Corporate Networks
  MAC used for L2 QoS and Analytics
  BYOD, MAC filtering will not work
  Courtesy network suffers same as Community networks
Industrial Networks
  Non-IOT devices may have MAC dependence - printers, barcode readers, badge readers, robotics controls
  Trucking manifest and navigation systems information exchange, product delivery tracking
Hospitality Networks
  guest may need to reauthenticate daily or use an app.
  Change to Passpoint

## Slide 8
Public Networks
  accept per-session authentication and loss of control over access restrictions
  Passpoint networks requiring Ts & Cs acceptance – this and other Passpoint features may have a dependence on MAC.
  MACs can no longer be used to block devices that make repeated retries of invalid credentials, the AAA must communicate to the device that the credentials are not valid, and the device must honor that and seek remediation or stop trying to use them

## Slide 9: Future Investigation
The suitability of the following for alleviating MAC randomization issues should be investigated:
Passpoint and WRIX/AAA
  WRIX: Wireless Roaming Intermediary eXchange
OpenRoaming
  WBA centralized policy authority, allows users to join any network managed by a federation member.
  Identity Providers and Network Providers
Wi-Fi Easy Connect
Wi-Fi Open Enhanced
Captive portal and/or Capport
Resorting to indirect IDs such as a network operators App.

## Slide 10: Next Steps
recommend that the operator and vendor community join forces to identify further mitigations for the effects of MAC randomization, and alternative secure identifiers that are not publicly observable, nor shared outside of a network.