## Slide 1: Next steps in evaluating of the impact of varying ED threshold on performance of 802.11
19 July 2021
Authors:
Name | Affiliations | Phone | email
Gaurav Patwardhan | Hewlett Packard Enterprise |  | gaurav.patwardhan@hpe.com
Eldad Perahia | Hewlett Packard Enterprise |  | eldad.perahia@hpe.com
Stuart Walker Strickland | Hewlett Packard Enterprise | +1(510)358-5246 | stuart.wal.strickland@hpe.com
Slide 1

## Slide 2: Context
A consensus recently reached in ETSI BRAN:
    establishes a common energy detection (ED) threshold of -72 dBm for all technologies operating in the 6 GHz band
    allows 802.11ax and legacy 802.11 technologies to continue to use an ED threshold of -62 dBm in conjunction with preamble detection (PD) in the 5 GHz band, but requires future technologies, presumptively including 802.11be, to use a common ED threshold of -72 dBm
Slide 2

## Slide 3: Background
In a previous contribution (802.11-21/0705r0), we presented simulations results, concluding that:
The decision by ETSI BRAN to establish a common ED threshold of -72 dBm in 6 GHz will likely have a positive impact on efficient sharing in that band
When using an ED threshold of -72 dBm in 5 GHz, 802.11be would sometimes suffer and sometimes gain an advantage over legacy equipment operating with the current ED threshold
Observed imbalances may be partially mitigated by using RTS/CTS
Data on the distribution of wanted client and interfering co-channel neighbor signals suggest that ~10 to 12% of client traffic may fall within the region where 802.11be would be disadvantaged with respect to legacy equipment by using an ED threshold of -72 dBm
In managed 5 GHz networks where 802.11ax and .11be networks overlap, both systems may benefit from voluntarily operating with a common ED threshold of -72 dBm
Slide 3

## Slide 4: Possible Next Steps
Our simulations were based on a relatively simple network topology, consisting of 3 BSS systems, each with one AP and one client
Model more realistic and varied network topologies with multiple clients on each AP and a mixture of 802.11ax and 802.11be equipment
Our simulations assessed the impact on throughput as functions of wanted and unwanted signal strength
Consider also the impact on latency by monitoring delays in the time to access the medium
Our simulations were all based on full buffer, uplink, best effort, UDP traffic
Consideration a wider range of concomitant traffic models across a range of network loads
Our simulations modelled the 802.11ax PHY for all devices, all using 20 MHz channels, a single spatial stream, and a maximum MCS of 11
Consider characteristics and features specific to 802.11be, such as multi-link operation, higher order modulation schemes, OFDMA enhancements
In our simulations, all equipment used PD at -82 dBm in conjunction with ED at either -72 or -62 dBm
Consider scenarios with LAA/NR-U using ED only
Consider other other characteristics specific to 3GPP technologies