## Slide 1: NB Coexistence in 6 GHz – eDAA
Author:
Name | Affiliation | Address | Phone | Email
Menzo Wentink | Qualcomm | Utrecht, The Netherlands |  | mwentink qti.qualcomm.com

## Slide 2: Introduction
Several submissions have been made in relation to NB in 6 GHz
  11-21-0832-00-coex-Narrowband-Coexistence-with-Wi-Fi-in-6-GHz
  BRAN(20)108038 (6 GHz VLP Narrowband)
    introduces NB within the existing LBT framework
  BRAN(21)109e003r1 (EN 303 687 NB Inputs)
    this document proposes to use the NB channel access rules from EN 300 328 (2.4 GHz), like DAA, MU-factor
  BRAN(21)109e003r1 (EN 303 687 NB Inputs)
    presents interference measurements between BT and Wi-Fi
    the results omit several key parameters, such as impact on Wi-Fi latency and full buffer throughput, and it omits several intermediate data points, suggesting a gradual reduction in throughput
  BRAN(21)109e008 (Wifi BT Test Setup Simulations) and
  BRAN(21)109h007 (NB coexistence with WB in 6 GHz)
    presents simulation results on coexistence between BT and Wi-Fi
    shows that coexistence between BT and Wi-Fi is very poor based on the EN 300 328 NB adaptivity rules, and that coexistence in 2.4 GHz is not based on the EN 300 328 mechanisms, but by Wi-Fi using FDMA and TDMA
  BRAN(21)109h004r2 (EN 303 687 NB Proposals for DAA Optimisation)
    introduces eDAA, r2 adds the exponential unavailability time
  BRAN(21)109j004 (NB coexistence with WB in 6 GHz eDAA)
    analysis of eDAA without exponential unavailability time
  The current submission analyzes eDAA with exponential unavailability time

## Slide 3: Enhanced Detect and Avoid (eDAA)
Enhanced Detect and Avoid (eDAA) has been proposed in BRAN as a method to make Wi-Fi and NB coexist
  the basic DAA rules are specified in EN 300 328 (2.4 GHz)
  the enhancements to DAA are proposed in BRAN(21)109h004r2
    time between eDAA CCAs: 0.5 s
    channel unavailability time: 2.5 s, doubling for consecutive CCA busy events up to 40 s
    20 MHz block unavailability
    return after 500 ms when channel is idle (not simulated yet)

## Slide 4: Wi-Fi/NB test setup
AP
10 dBm
STA
10 dBm
NB1
10 dBm
NB2
10 dBm
Variable Attenuation
A dB (20 – 120 dB)
60 dB
60 dB
A dB
A dB
A dB
A dB
11ax Wi-Fi link
80 MHz, 2ss
1201 Mbps max PHY rate
(HE MCS11, 996-tone RU, NSS = 2, 800 ns GI)
NB link
79 MHz, 79 hops
1 MHz hop width
625 μs dwell time
425 μs Tx time, 200 μs switch time (68% duty cycle)
3 Mbps max PHY rate (EDR 8-DPSK)
(2 Mbps effective throughput at 68% duty cycle)

## Slide 5: Simulation settings Wi-Fi/NB
11ax Wi-Fi link
  80 MHz channel width, HE (11ax), Nss = 2
  Maximum throughput about 1.1 Gbps (HE MCS11, 996-tone RU, 800 ns GI, 80 MHz, 1201 Mbps)
  Receive bitrate based on SINR and MCS sensitivities for MCS0 – MCS11 (genie rate adaptation)
NB link
  79 hops, 1 MHz hop width, 79 MHz hopping bandwidth
  hopping sequence randomly spread equally over the 79 channels
  625 μs dwell time
    425 μs Tx time, 200 μs switch time (68% duty cycle)
    based on Bluetooth (BT) numerology
  3 Mbps PHY rate
    2 Mbps effective bitrate at 68% duty cycle
  NB is on the same channel as the Wi-Fi link (co-channel interference)
  eDAA with exponential unavailability time up to 40 s, 0.5 s before CCA

## Slide 6: Throughput (NB uses eDAA) (Wi-Fi/NB, interference level sweep, HE 2ss)
- interference level sweep
- NB uses eDAA
Blue: Wi-Fi throughput
Red: NB throughput
the average Wi-Fi throughput is fine when eDAA is active

## Slide 7: Throughput (NB uses LBT) (Wi-Fi/NB, interference level sweep, HE 2ss)
- interference level sweep
- NB uses LBT (FBE)
Blue: Wi-Fi throughput
Red: NB throughput
the average Wi-Fi throughput is also fine when LBT is active

## Slide 8: Access delay (NB uses eDAA) (Wi-Fi/NB, interference level sweep, HE 2ss)
but eDAA causes very high latency at both NB and Wi-Fi
- interference level sweep
- NB uses eDAA
Blue: Wi-Fi latency
Red: NB latency

## Slide 9: Access delay (NB uses LBT) (Wi-Fi/NB, interference level sweep, HE 2ss)
while LBT causes low latency
- interference level sweep
- NB uses LBT (FBE)
Blue: Wi-Fi latency
Red: NB latency

## Slide 10: NB/NB test setup
NB1
10 dBm
NB2
10 dBm
NB3
10 dBm
NB4
10 dBm
Variable Attenuation
A dB (20 – 120 dB)
60 dB
60 dB
A dB
A dB
A dB
A dB
NB link
(details below)
NB link
79 MHz, 79 hops
1 MHz hop width
625 μs dwell time
425 μs Tx time, 200 μs switch time (68% duty cycle)
3 Mbps max PHY rate (EDR 8-DPSK)
(2 Mbps effective throughput at 68% duty cycle)

## Slide 11: Simulation settings NB/NB, 79 hops
NB links
  79 hops, 1 MHz hop width, 79 MHz hopping bandwidth
  hopping sequence randomly spread over the 79 channels
  625 μs dwell time
    425 μs Tx time, 200 μs switch time (68% duty cycle)
    based on Bluetooth (BT) numerology
  3 Mbps PHY rate
    2 Mbps effective bitrate at 68% duty cycle
  NB is on the same channel as the Wi-Fi link (co-channel interference)
  eDAA with exponential unavailability time up to 40 s, 0.5 s before CCA

## Slide 12: eDAA – throughput as a function of time (NB/NB, 79 hops, high interference level, transient behavior)
with eDAA, the NB throughput fluctates heavily
- simulation at high interference level
- eDAA with exponential unavailability time
the NB throughput fluctuates heavily as well

## Slide 13: LBT – throughput as a function of time (NB/NB, 79 hops, high interference level, transient behavior)
- simulation at high interference level
- LBT (FBE)
with LBT, the NB throughput is essentially flat

## Slide 14: Conclusions
NB with eDAA may cause latency issues at Wi-Fi
  the interruptions for Wi-Fi can be 0.5 s, occurring periodically
  a starting Wi-Fi stream will experience 0.5 s delay before any meaningful throughput will occur
eDAA also appears inadequate for NB/NB sharing
  the throughput is unstable and there can be very high latency spikes, due to the very high penalty on hop collisions
  NB links may be unable to share the same spectrum when eDAA is used
LBT shows no issues for either Wi-Fi/NB or NB/NB coexistence
The eDAA coexistence issues pointed out in this analysis should make it unlikely that a notified body can certify 'no-LBT' NB equipment
  eDAA does not appear to satisfy the requirement of an 'adequate spectrum sharing mechanism' as required by the ECC