## Slide 1: Changing STA MAC addresses per association & SA/DA hiding
Date: 2021-08
Authors:

## Slide 2: Abstract
Problems: Client identifiers sent in clear OTA should change frequently, however:
  Regarding STA MAC address used OTA as TA/RA in 802.11 baseline
    TA/RA allowed to change for each association. However, not done due to impact on DS.
    TA/RA currently must persist for association, since AP processes received packets based on STA MAC address.
  Regarding STA MAC address used as SA/DA in the DS
    Legacy devices send & receive other devices SA/DA OTA. SA/DA available to all devices on DS. Potential Privacy issue.
    If SA/DA can change, should still persist for each association, to avoid impacting higher layer protocols.
  DS needs a client identifier persisting across multiple associations for managing connections.
Notes:     For example, a client might be associated with the AP in a vehicle for an extended period. If the client’s over-the-air (OTA) MAC address does not change, then the movement of the user can be determined.
    Similarly, if a client is associated with a stationary AP for an extended period, then presence of the OTA MAC address can be used to infer that the user has remained in radio range of the station AP.

## Slide 3: For Reference: Address fields
TA = MAC address of the AP/STA transmitting the frame
RA = MAC address of the AP/STA radio receiving the frame
SA = MAC address of the source device (wired or wireless) of the frame
  Can be the same as TA
DA = MAC address of the destination device (wired or wireless) receiving the frame
  Can be the same as RA

## Slide 4: Issues with Changing the OTA MAC address between Associations
802.11 baseline supports a client changing MAC address for each association.
Changing MAC address for each association causes issues in the DS
  Theses issues caused by DS management relying on a persistent MAC address to identify client.
  Consequently, clients do not change MAC address for each association
A persistent client identifier is needed which the DS can use to correlate multiple associations from the same client.
  This seems related to TGbh work is identifying and addressing issues related to changing the MAC address between associations.

## Slide 5: Issues with sending SA and DA in the clear OTA
Problem Statement: SA and/or DA (when present) should not be sent in the clear in OTA frames
  This information does not need to be in the clear
    Sending this in the clear is a historical artefact
  How can attackers exploit SA/DA sent in the clear in OTA frames?
    Identify wired devices present in the DS
    For STA with static SA/DA address: identifying STA present in DS
    For STA with random SA/DA address: determining whether the STA is still present in the DS for duration of STA’s SA/DA.
    Note: STA presence in DS can be detected in frames exchanged with any AP of the DS, even if the STA is outside the radio range of the attacker.

## Slide 6: Potential Solutions
3 tiers of client identifiers (using MLO Architecture).
  Affiliated STA MAC addresses (used as TA/RA): changes every association. For long-term association, perform new association to change addresses when needed. In clear OTA.
  Non-AP MLD MAC address (used SA/DA): can change every association (depending on use case). Encrypted OTA.
  Per-DS identifier: persistent across multiple associations with the DS. Encrypted OTA. (TGBh addressing this?)
Hide SA/DA OTA

## Slide 7: Potential Solution: 3 Tiers of Client Identifier using MLO Architecture
Identifier | Usage | Potential Solution | 
 |  | Identifier Persistence | Visibility over the air
Affiliated STA MAC addresses | Identifying Client using TA or RA in over the-air frames | Change randomly for each association | Unencrypted (in the clear)
Non-AP MLD MAC Address | Identifying Client using SA or DA in DS frames | Can change randomly for each association or persist across associations1 | Encrypted2 (hidden)
Persistent Identifiers | Identifying Client across multiple associations with same network. | Persistent across associations within a single network. Can change randomly from one network to another | Encrypted (hidden)
    If higher layer protocols sessions continue to new association, then keep existing MAC address If higher layer protocols sessions do not continue to new association, then change MAC address
    In 802.11be, non-AP MLD is current exchanged in the clear (un-encrypted). This would need to change.

## Slide 8: Potential Solution: Hiding SA and DA OTA
Solution Summary: SA and/or DA (when present) are sent encrypted OTA
  SA and/or DA are extracted from frame header inserted into the frame body prior to applying encryption and integrity protection.
    Fields containing SA and/or DA may be either removed from frame header, or set to some value (e.g. all zeroes or random values).
  After applying integrity verification and decryption, SA and/or DA are extracted from the frame body and used in further processing of the frame.
Note: SA/DA in frames used by legacy STAs will still reveal the per-association persistent MAC address (non-AP MAC Address) of source/destination STAs that use changing OTA MAC addresses (this slide). Note this is not an issue for a DS which prohibits STA-to-STA communications.

## Slide 9: Slides to add to 11-21-0641-r2 “Proposed Issues” (Use cases)

## Slide 10: X) STA MAC address persistence
Problem/Issue
Current STA MAC address usage presents challenges to providing privacy.
  MAC address used for TA/RA does not change
  MAC address used for DA/SA does not change
Additional challenges
  DS requires an identifier for correlating associations from a single STA
    Currently using the MAC Address, and we want to change MAC address to improve privacy
  MAC address for DA/SA is used in upper layers. Changing these within association impacts upper layers
  MAC address for TA/RA is used for received packet filtering at the AP.
Status
  [Text indicating when use case was presented and any agreements on the use case.]
Reference
(This contribution)

## Slide 11: Y) Tracking SA and DA OTA
Problem/Issue
SA and DA are currently sent in the clear OTA.
This reveals MAC addresses used in the DS, which allows /tracking
  Identifying Wired Devices
  Identifying 802.11 radios which use static MAC addresses for SA/DA in DS.
  Tracking network presence of 802.11 radios which support random MAC address for SA/DA in DS (for lifetime of each SA/DA address)
Status
  [Text indicating when use case was presented and any agreements on the use case.]
Reference
(This contribution)