## Slide 1: Threshold Based Sensing Procedure
Date: 2021-10-12
Authors:
Name | Affiliation | Address | Phone | Email
Mengshi Hu | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | humengshi@huawei.com
Rui Du |  |  |  | 
Chenchen Liu |  |  |  | 
Yi Lv |  |  |  | 
Danny Kai Pin Tan |  |  |  | 

## Slide 2: Introduction (1/2)
In [1][2], a threshold based sensing procedure was proposed to select the receivers with large CSI variations.
The CSI variation measured at the receiver is used to indicate the motions of objects.
Only the receiver detecting a large CSI variation compared with a threshold will be triggered to have a further feedback in Procedure B.
The overhead reduction results from the reduced number of receivers triggered in Procedure B. If the CSI variations of all devices are all relatively small, only Procedure A is needed in the threshold based sensing procedure.
Procedure A
Overhead A (small)
Procedure B
Overhead B (large)
Reference: [1]

## Slide 3: Introduction (2/2)
A motion related to the above threshold based procedure has passed [3]:
In the subsequent slides, we further give the following details of this optional threshold based sensing.
How to calculate the CSI variation
Details of the threshold based procedure
The 11bf amendment defines an optional threshold based measurement and reporting procedure in which
The difference between the current measured CSI and the previous measured CSI is quantified. The difference is referred to as CSI variation.
A threshold value to be used by the sensing receiver in the threshold based procedure is defined.
By comparing the CSI variation with the threshold, the sensing receiver can send a feedback resulting from the large CSI variation to the sensing transmitter.
Whether the threshold is predefined, or defined by the sensing receiver, transmitter, initiator or responder is TBD.
The threshold based procedure is not always required (Procedure A in 21/0351r5 is not always required).

## Slide 4: Calculation of CSI Variation
How to calculate the CSI variation?
The calculation of CSI variation is suggested to be implementation specific. Different devices can have different methods to determine the CSI variation.
Although this is implementation specific, the following rules shall be defined for the calculation, providing benefits for the metric unification and the threshold adaptation.
The estimation value of the CSI variation needs to be mapped to a closed interval [0, 1].
A larger estimation value indicates a larger CSI variation degree (strictly increasing)
The CSI variation of 0 indicates a minimum CSI variation.
The CSI variation of 1 indicates a maximum CSI variation.

## Slide 5: Signaling
Initiator Sends Threshold & Responder Feeds back CSI variation
The initiator sends the threshold to its corresponding responder.
Measurement setup level: No change within the measurement instances that have the same measurement setup ID. The threshold can be told in the measurement setup.
Measurement instance level: Can be changed in different measurement instances. The threshold can be told in the NDPA, or Feedback Request within the measurement instance.
Whether or not to use this can be told in the session setup.
The responder feeds back the CSI variation to the initiator in the Feedback Response in Procedure A in the measurement instance, and can compare its CSI variation with the obtained threshold to know whether it needs to feed back the full CSI later.
An example of the WLAN sensing procedure (Ref: IEEE 802.11-21/1321r1 [4])
Note: The signaling is based on the sensing procedure in 1321r1.

## Slide 6: Behavior
Initiator
The initiator should send a feedback trigger frame to a responder that reports a CSI variation that is greater than or equal to the threshold.
The initiator shall not send a feedback trigger frame to a responder that reports a CSI variation that is less than the threshold.
Responder
The responder with a CSI variation greater than or equal to the threshold should be triggered in Procedure B.
The responder with a CSI variation less than the threshold shall not be triggered in Procedure B.
Procedure A
Overhead A (small)
Procedure B
Overhead B (large)

## Slide 7: Examples of Behavior
Examples
A responder with the threshold set to 0 should always be triggered in Procedure B.
A responder with the threshold set to 0.5 and the CSI variation equal to 0.7 should be triggered in Procedure B.
A responder with the threshold set to 0.5 and the CSI variation equal to 0.2 shall not be triggered in Procedure B.
Note
The threshold set by the initiator indicates the degree of the CSI variation that the initiator is interested in. For example, if the threshold is 0.5, it means the initiator does not care about the information with a CSI variation less than 0.5.
A initiator can set a loose threshold to make sure that the information with a CSI variation less that the threshold is the useless information.
The threshold set by the initiator is equal to 0.5
0
1
The initiator is not interested in this at all
Information that the initiator is interested in
CSI variation
(The responder should be triggered)
(The responder shall not be triggered)

## Slide 8: Role of Initiator
The initiator might be a transmitter, a receiver, both or neither.
The applicative scenarios are shown as follows:
Note:
If the initiator’s role is a receiver, there is no need to implement this threshold based sensing measurement, because the receiver can already get the CSI information.
Initiator’s role | Measurement setup level | Measurement instance level
Transmitter | √ | √
Receiver | × | ×
Both | √ | √
Neither | √ | √

## Slide 9: Conclusion
Signaling
The initiator sends the threshold to its corresponding responder.
The responder feeds back the CSI variation to the initiator.
Behavior
The initiator shall not send a feedback trigger frame to a responder that reports a CSI variation that is less than the threshold.
The initiator should send a feedback trigger frame to a responder that reports a CSI variation that is greater than or equal to the threshold.
Applicative scenarios
If the initiator’s role is a receiver, there is no need to implement this threshold based sensing measurement

## Slide 10: References
[1] 11-21-0351-05-00bf-threshold-based-sensing-measurement
[2] 11-21-1069-05-00bf-threshold-based-sensing-measurement-follow-up
[3] 11-20-1874-13-00bf-tgbf-motions-list
[4] 11-21-1321-01-00bf-wlan-sensing-procedure

## Slide 11: Straw Poll 1
Do you agree that in the threshold based measurement instance, the estimation of CSI variation is implementation specific, but it shall follow the following rules?
The degree of the CSI variation shall be represented by a value in the closed interval [0, 1].
A larger degree shall reflect a larger CSI variation.
The degree of 0 indicates the smallest degree of the CSI variation (No CSI variation).
The degree of 1 indicates the largest degree of the CSI variation.
Note: Which CSI variation corresponds to the degree of 1 is implementation specific.
Y
N
A

## Slide 12: Straw Poll 2
Do you agree that in the threshold based measurement instance, the threshold to be compared with the CSI variation value is determined by the initiator?
Y
N
A

## Slide 13: Straw Poll 3
Do you agree that in the threshold based scheme
The initiator sends the threshold(s) to the responder(s) (Which frame transmits the threshold is TBD).
The responders feed back the CSI variation to the initiator in the Feedback Response frame.
The initiator shall not send a Feedback Trigger frame to a responder that reports a CSI variation that is less than the threshold.
The initiator should send a Feedback Trigger frame to a responder that reports a CSI variation that is greater than or equal to the threshold.
The above procedure is applicable to TB based sensing measurement instance.
Incorporate the figure in slide 13 of 11-21/1364r5 into the SFD.
Note: The “Feedback” frame shown in the figure should be “Measurement report” frame.
Y
N
A
Threshold based procedure in a sensing measurement instance (example)

## Slide 14: Motion 1
Move to add the following to 11bf SFD:
In the threshold based measurement instance, the estimation of CSI variation is implementation specific, but it shall follow the following rules:
The degree of the CSI variation shall be represented by a value in the closed interval [0, 1].
A larger degree shall reflect a larger CSI variation.
The degree of 0 indicates the smallest degree of the CSI variation (No CSI variation).
The degree of 1 indicates the largest degree of the CSI variation.
Note: Which CSI variation corresponds to the degree of 1 is implementation specific.
Corresponding document 21/1364r3, SP results: 14Yes, 5 No, 6 Abstain

## Slide 15: Motion 2
Move to add the following to 11bf SFD:
In the threshold based measurement instance, the threshold to be compared with the CSI variation value is determined by the initiator.
Corresponding document 21/1364r3, SP results: 16 Yes, 1 No, 6 Abstain