## Slide 1: Client ID Query concept
Date: 2021-08-17
Authors:

## Slide 2: Abstract
Proposal to add a new action frame request/response that an AP and STA can use to exchange a unique identifier for the STA (within a secured link).

## Slide 3: Background
MAC randomization has shifted from a theoretical discussion to widespread deployments
Different devices are offering MAC randomization features with different behaviors
Some devices already use randomized MAC addresses when they probe by default.
Some devices allow the user to enable the use of randomized MAC addresses when a device is associated.
  With some operating systems, the random MAC may be remembered and reused for a specific SSID, and it may also age out after a period of time to be replaced by a new randomized MAC.

## Slide 4: Background
MAC randomization can cause issues for APs as they deal with associated and unassociated STAs.
A liaison from WBA highlighted the many uses of MAC addresses within residential and enterprise products that may be affected by MAC randomization if it is widely used while associated. (11-18-1579-01)
  device steering (already potentially affected for initial association), parental controls, network access controls (PassPoint), device count limits, legal intercept, diagnostics, etc.
It is important to note that because many users take advantage of the current systems, they will experience a perceived loss of utility when they are forced to log in every time because the AP or a supervising system will not recognize the STA.
  These users may view the ability to use a stored randomized MAC address as still providing them with privacy when it really does not.
This proposal seeks primarily to help an AP with a STA that is associated and only if the user “opts in” (has chosen to provide an identifier).
  However, pre-association with appropriate security of the identifier is also possible.

## Slide 5: Allow an AP to request an ID from a STA
We propose a new action frame exchange that an AP can initiate with an associated STA to request a unique identifier from the STA for future use
The exchange would be secured and kept private.
The ID would have minimal requirements of form
  Flexible length and contents
  ID is per-network and implementation-specific. The ID contents can be the user’s choice, or automatically generated, for example.
  Not guaranteed to be unique, but if the STA replies with an ID, the STA should be motivated to make it unique
  The STA should remember the ID for the network and keep it consistent, but different IDs can be used on different networks
The ID Query message could be sent whether or not the STA provided a local MAC address
  Not all STAs have complied with the recommended use of a local MAC address.

## Slide 6: Also allow the STA to provide an ID, without solicitation or association
While the protocol is fundamentally request/response, the STA is also allowed to provide a “response” without needing a request
  For example, if the STA recognizes the network from a prior encounter, there is no requirement for the request.
  The STA response still must be secured and kept private.
  The security also assures the STA that the network is what it claims to be, before providing the ID.
In fact, as long as the security/privacy is ensured, the STA can provide the ID pre-association
  For example, a PASN (802.11az) security association can be used to protect the ID exchange, prior to (or instead of) a full association.

## Slide 7: Request Frame Format
The Request frame allows an AP to query an associated STA for a unique identifier.
Category | ID Query Action | Vendor Specific (optional)
Octets: 1 1 Variable

## Slide 8: Response Frame Format
The Response Frame format allows the responding STA to indicate either that it will not provide an ID or that it will.
The Response includes optional ID and TTL fields, if the STA decides to provide an ID.
The Response includes a Length field to allow for variable sized ID, and extensibility for vendor specific information, etc.
A Vendor Specific field is also included in the Response to allow vendor differentiation.
Octets: 1 1 1 2 Variable 2 Variable
Category | ID Query Action | Response | Length | ID (optional) | TTL (optional) | Vendor Specific (optional)

## Slide 9: Advertisement of Support for ID Query
An Extended Capability bit is proposed.
The IDQuery_Support bit set to 1 indicates that a STA can support an ID Query action frame.
At a higher layer, a user may direct a STA to not share a permanent or semi-permanent identifier, so a STA may still decline to provide an ID even though it indicates support for the message.
  For example, such a decision might be based on the network being associated, and the level of trust in the networks’ provider(s).

## Slide 10: Summary
APs and the larger network (including higher-layers) need more information to provide additional services when a STA uses a randomized MAC address while associated.
A message allowing an AP to query an associated STA for a unique ID with some informative parameters could be structured to allow a STA to opt in to sharing at least minimal information.
The STA could still ignore the message or decline to provide a unique identifier.
The STA can provide the ID without need for solicited request, if it recognizes (and validates) the network.