## Slide 1: View on Private Identifier
Date: 2021-08-24
Authors:

## Slide 2: Abstract
There has been a fair amount of presentations in 11m [1], 11bh[2, 3], and 11bi [4, 5] mentioning/hinting at additional “private identifier” from the client
  Different names are used in different presentations/discussions in different forums: ex. “unique identifier/identifier” [1], “client ID” [3], “a device or user identification ” [2], “persistent identifier/per-DS identifier” [5]
  “private” concept is emphasized as “ without exposing any new user privacy concern”, “encrypted”, “hidden”, “not identifiable/trackable by unauthorized/undesired observers”
The discussions had arguably left audience thoroughly perplexed
We discuss our view on how this topic is related to both 11bh and 11bi

## Slide 3: Go back to the basic
11aq defines randomized MAC address in 12.2.10 (Requirements for support of MAC privacy enhancements) for privacy enhancement with the following caveat:
  State created with an AP using a prior MAC address, for instance, RSN preauthentication state or FT state established over-the-DS, is bound to the MAC address used when that state was created. Prior to establishing an association to the AP, the non-AP STA shall change its MAC address to the MAC address used when the state was created.
  The non-AP STA connecting to an infrastructure BSS shall retain a single MAC address for the duration of its connection across an ESS.
The above spec texts show that there are two requirements that are battling against each other
  Privacy requirement => randomize MAC address
  State bound requirement => can not randomize MAC address

## Slide 4: Evaluation of the Two Requirements
Privacy Requirement | State Bound Requirement | Subcase | Action Today | Do we need to address the scenario?
No | No | N/A | Do not randomize MAC address | No, do not need to do anything
No | Yes | N/A | Do not randomize MAC address | No, do not need to do anything
Yes | No | N/A | Randomize MAC address | No, just use 11aq
Yes | Yes | Advantage of maintain “state bound” > advantage of Privacy | Do not randomize MAC address | 11bi angle: Can we have a way to keep privacy requirement?
Yes | Yes | Advantage of maintain “state bound” < advantage of Privacy | Randomize MAC address | 11bh angle: Can we have a way to keep state bound requirement?
Client Decision
Notes: Swap row 2 and 3

## Slide 5: Evaluation of the Two Requirements
Privacy Requirement | State Bound Requirement | Subcase | Action Today | Do we need to address the scenario?
No | No | N/A | Do not randomize MAC address | No, do not need to do anything
No | Yes | N/A | Do not randomize MAC address | No, do not need to do anything
Yes | No | N/A | Randomize MAC address | No, just use 11aq
Yes | Yes | Advantage of maintain “state bound” > advantage of Privacy | Do not randomize MAC address | 11bi angle: Can we have a way to keep privacy requirement?
Yes | Yes | Advantage of maintain “state bound” < advantage of Privacy | Randomize MAC address | 11bh angle: Can we have a way to keep state bound requirement?
Client Decision
Notes: Swap row 2 and 3

## Slide 6: Evaluation of the Two Requirements
Privacy Requirement | State Bound Requirement | Subcase | Action Today | Do we need to address the scenario?
No | No | N/A | Do not randomize MAC address | No, do not need to do anything
No | Yes | N/A | Do not randomize MAC address | No, do not need to do anything
Yes | No | N/A | Randomize MAC address | No, just use 11aq
Yes | Yes | Advantage of maintain “state bound” > advantage of Privacy | Do not randomize MAC address | 11bi angle: Can we have a way to keep privacy requirement? => Let’s have another “private identifier” tied to state bound requirement, and then randomize MAC address
Yes | Yes | Advantage of maintain “state bound” < advantage of Privacy | Randomize MAC address | 11bh angle: Can we have a way to keep state bound requirement? => Let’s have another “private identifier” tied to state bound requirement, so we do not break state bound requirement while randomize MAC address
Client Decision
Notes: Swap row 2 and 3

## Slide 7: Conclusion of the Evaluation
11bh and 11bi are looking at the same problem from different angles, and there are now two forums with solutions that try to address the same problem
It does not make sense to have two solutions in two different groups to solve the same problem
  The outcome is either solution may not be used eventually
A mechanism about “private identifier” that satisfies both state bound requirement and privacy requirement needs to be dealt in the amendment with larger scope
  Suggest to have the effort (if needed) in 11bi

## Slide 8: Straw Poll
Do you support that the optional mechanism to provide additional private identifier needs to be discussed in 11bi?

## Slide 9: Reference
[1] 11-19-0496-01 ID_Query_Proposal
[2] 11-21-0332-13 Issues Tracking
[3] 11-21-1378-00 Client ID query concept
[4] 11-21-993-00 hotel_privacy_usecase
[5] 11-21-1328-00 Changing STA MAC addresses per association and SA/DA hiding