## Slide 1: Topology and Address Mapping
Date: 2021-09-28
Authors:

## Slide 2: Abstract
This document proposes an addressing mechanism for EBCS

## Slide 3: Example EBCS Topology
Router
AP
AP
Broadcast Source/Sink
Internet
Broadcast
Source/Sink
STA
STA
LAN
BC Source/Sink reside on network.
EBCS content stream mapper maps data (content ID) to/from sink/source to EBCS content.
EBCS Filter maps content ID to/from EBCS frames.
EBCS content stream mapper
EBCS Filter

## Slide 4: 802.11 Architecture view of EBCS Topology
DS
EBCS Content Stream Mapper
AP
AP
EBCS Filter
EBCS Filter
Portal
LAN and Internet
Broadcast Source/Sink
Broadcast Source/Sink

## Slide 5: EBCS Service and LAN traffic
An EBCS stream can be available from multiple APs simultaneously. It is not limited by a BSS.
EBCS traffic is separate from group-addressed LAN traffic – it does not need to adhere to requirements for transmission/reception in a BSS.
STAs do not need to be associated to receive EBCS traffic
STAs can receive traffic from any STA that is broadcasting EBCS traffic.
EBCS traffic can be uplink or downlink
Typically, WLAN devices use a MAC address to filter traffic for reception.
Why not modify addressing to make EBCS traffic easier to transmit/receive?

## Slide 6: Mapping Content to Addressing
APs typically only send broadcast traffic to STAs associated in their BSS. Addressing is based on the BSS – identified by a BSSID (MAC Address).
EBCS traffic can be received by any device that subscribes to a given Content ID. Similarly, the device can broadcast traffic to any AP that subscribes to the Content ID.
Assigning a specific EBCS MAC Address for the stream makes it easier for STAs to send/receive traffic. STAs/APs use the MAC address to filter traffic.
Traffic Direction | LAN traffic | Content ID | EBCS MAC Address
Downlink | Broadcast/multicast address (BC/MC) | Assigned by stream mapper | Unique Address for EBCS traffic stream.
Uplink | Unicast or BC/MC | Assigned by stream mapper | Unique Address for EBCS traffic stream.
September 2021
Michael Montemurro, Huawei
Michael Montemurro, Huawei

## Slide 7: Identifying an EBCS traffic stream
A STA or AP can identify an EBCS traffic stream by the information:
  Content ID
  Multicast Address (note it could be a Broadcast Address)
  EBCS MAC Address
September 2021
Michael Montemurro, Huawei
Michael Montemurro, Huawei

## Slide 8: Downlink EBCS stream example
Router
AP
AP
Broadcast Source
Internet
Broadcast
Source
STA
LAN
EBCS content stream mapper
EBCS Filter
1
4
4
2
3
3
3
3
5
6
6
BC Source/Sink reside on network.
EBCS content stream mapper maps data (content ID) to/from sink/source to EBCS content.
EBCS Filter maps content ID to/from EBCS frames.

## Slide 9: Downlink EBCS stream steps.
Network Administrator configures multicast stream for EBCS by assigning a Content ID and EBCS MAC Address in EBCS Content Stream Mapper and EBCS Filter.
Multicast Stream packets are received by EBCA Content Stream Mapper and converted to EBCS frames (an EBCS Traffic Stream) identified by Multicast address, Content ID and EBCS MAC Address
EBCS Filter passes the EBCS frame to the AP and the AP transmits the frame OTA.
At the same time as 2 and 3, the AP advertises EBCS Content in either: Beacons, Probe Responses and ANQP frames.
A STA discovers the EBCS content advertised by an AP and subscribes to receive the EBCS traffic stream.
The STA begins receiving EBCS frames from an AP in range that is broadcasting that stream based on EBCS MAC Address, Content ID, and Multicast address. Note: The STA can move from AP to AP and continue to receive the broadcast.
September 2021
Michael Montemurro, Huawei
Michael Montemurro, Huawei

## Slide 10: Uplink EBCS stream example
Router
AP
AP
Broadcast Sink
Internet
Broadcast
Sink
STA
LAN
BC Source/Sink reside on network.
EBCS content stream mapper maps data (content ID) to/from sink/source to EBCS content.
EBCS Filter maps content ID to/from EBCS frames.
EBCS content stream mapper
EBCS Filter
1
5
3
3
2
1
4
4

## Slide 11: Uplink EBCS stream steps.
Network Administrator or manufacturer configures the multicast stream in both the STA and AP as EBCS by assigning a Content ID and EBCS MAC Address in Content Stream Mapper and EBCS Filter. Note that on the AP infrastructure, the destination address configured may be the address of the Broadcast Sink or a multicast address.
STA begins broadcasting EBCS frames using EBCS MAC Address, Content ID, and Multicast Address.
EBCS frames are received by the AP, identified as EBCS frames, and passed to the EBCS Filter and EBCS Content Mapper.
The EBCS Filter and Content Stream Mapper match the frame against configured information.
  Note that duplicate frames may be received if the frame was received by multiple APs. The duplicates may possibly be removed.
The Content Stream Mapper forwards the frame as multicast or to the Broadcast Sink address depending on the configuration for that EBCS traffic stream.
September 2021

## Slide 12: EBCS Addressing
(Relay excepted) Frames use A1, A2, A3, and ToDS/FromDS fields in the MAC header to send/receive frames.
Typically A1 = RA, A2 = TA, A3 = SA/DA/Context, ToDS/FromDS indicates direction.
Proposal:
  Introduce an EBCS Address to identify an EBCS traffic stream.
  There are a number of ways to do this:
    Reserve EBCS Addresses for UL/DL
      Could be taken from the SAI quadrant (see IEEE 802c-2017)
    Reserve MAC Address(es) with the 802.11 OUI
  Could be a single MAC address or a pool of MAC addresses.

## Slide 13: EBCS Frame Format Options

## Slide 14: Alternative 1: EBCS And Multicast Address
Direction | A1 (RA) | A2 (TA) | A3 | ToDS | FromDS
UL | EBCS | STA | MCAST | 1 | 0
DL | EBCS | AP MAC | MCAST | 0 | 1
Use EBCS MAC address to identify EBCS traffic
ToDS/FromDS to indicate UL/DL

## Slide 15: Alternative 2: EBCS Addresses And Multicast
Direction | A1 (RA) | A2 (TA) | A3 | ToDS | FromDS
UL | EBCS_UL | STA | MCAST | 0 | 0
DL | EBCS_DL | AP MAC | MCAST | 0 | 0
Use EBCS MAC address to identify EBCS traffic and UL or DL
Different MAC address for UL/DL

## Slide 16: Alternative 3: EBCS Addresses And Broadcast
Direction | A1 (RA) | A2 (TA) | A3 | ToDS | FromDS
UL | BCAST | STA | EBCS_ST1 | 1 | 0
DL | BCAST | AP MAC | EBCS_ST2 | 0 | 1
Use BCAST Address
ToDS/FromDS for UL/DL
EBCS Address identifies specific stream (could have different content IDs)

## Slide 17: Alternative 4: EBCS Addresses And Broadcast
Direction | A1 (RA) | A2 (TA) | A3 | ToDS | FromDS
UL | BCAST | STA | EBCS_ST1 | 0 | 0
DL | BCAST | AP MAC | EBCS_ST2 | 0 | 0
Use BCAST Address
EBCS Address identifies specific stream and direction (UL/DL)
Could still have different content IDs

## Slide 18: Alternative 5: EBCS Addresses And Multicast I
Direction | A1 (RA) | A2 (TA) | A3 | ToDS | FromDS
UL | MCAST | STA | EBCS | 1 | 0
DL | MCAST | AP MAC | EBCS | 0 | 1
Use EBCS MAC address to identify EBCS traffic
Swap A1/A3 from alternative 1

## Slide 19: Alternative 6: EBCS Addresses And Multicast II
Direction | A1 (RA) | A2 (TA) | A3 | ToDS | FromDS
UL | MCAST | STA | EBCS_UL | 0 | 0
DL | MCAST | AP MAC | EBCS_DL | 0 | 0
Use EBCS MAC address to identify EBCS traffic and direction
Swap A1/A3 from alternative 1