## Slide 1: TG bh Identifiable Random MAC Address
Date: 2021-10
Authors:
Name | Company | Address | Phone | email
Olivia Fernandez | SRT Group | Sunrise , FL |  | ofernandez@srtrl.com
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
This is a presentation on “Identifiable Random MAC Address”, IRMA
Rev 1,
Presented initial idea to TGbh 10/12/2021
Rev 2,
Added “No IRMK found” to cover case when the AP has deleted the “old” IRMKs. AP can ask for new IRMK (STA sends new or same)
Added “Private” to IRM element to allow IRM STA to use a private MAC address (eliminate need to set I/G bit)
Rev 3
Added “IRMK Check”
  Used to down-select stored IRMKs in AP
  Used to confirm back to STA that correct IRMK has been found
Rev 4
Discussed Change to stop any possible brute force attack
Rev 5
Delete Provide IRMK ? (can’t see a good use case for it)
Rev 6
Worked on Advantages. Corrected ANQP-element

## Slide 3: MAC Addresses
MAC Address 48-bit
Two Types:
Fixed
  Assigned MAC.
Random
  Two types,
    Non-identifiable - random, STA does not want to be known in any way
    Identifiable – random, but STA wishes to be identified/remembered by particular APs (networks)

## Slide 4: 802.11 Definitions
  Identifiable Random MAC (IRM) : a scheme where a non-AP STA uses identifiable random medium access control (MAC) addresses (IRMA) to prevent third parties from tracking the non-AP STA while still allowing trusted parties to identify the non-AP STA.
Identifiable Random MAC Address (IRMA) – a random MAC address used by a STA using IRM
Identifiable Random MAC Key (IRMK) – a Key used to resolve an IRMA

## Slide 5: Identifiable Random MAC Address - IRMA
Purpose
  Prevent third-parties from tracking the STA while still allowing trusted parties to recognize the STA.
Identifiable
  Uses a key shared with trusted AP/network – IRMK
    STA generates IRMK , or
    Option is that AP could provide an IRMK to a STA,
  STA generates an “IRM Hash” using IRMK and IRMA
  IRMA is the TA MAC address
  IRM Hash is sent in IRM element (in Association Request)
  STA can use same IRMK or may change it for every connection
Changing TA address
  TA MAC Address (IRMA) changes every use.
  No need to use same MAC address for each ESS

## Slide 6: IRM Address (IRMA)
Two basic random MAC address types:
  Random private (changes randomly, non-identifiable))
  Random identifiable IRMA
MAC Address is 48 bits
  Least significant bit of first octet (“I/G bit”)
    0 = unicast, 1 = multicast
  Second-least-significant bit of the first octet (“U/L bit”)
    0 = globally unique, 1 = locally administered
Random MAC is described in Clause 12.2.10 (D0.0)
  “The STA shall construct the randomized MAC address from the locally administered address space”
IRMA looks like any other randomized MAC address
IF IRM element includes the IRM Hash, then the address is an IRMA, i.e., “identifiable”
IF IRM element indicates “Private”, the IRM Hash is NOT sent and the address is a private randomized MAC, i.e., NOT an IRMA.

## Slide 7: CAPABILITY BIT
An IRM Capability field is used in the STA and AP
The AP looks for the IRM Capability AND the IRM Hash in IRM element
AP can use the IRM Capability bit to indicate to STAs that there may be a reason to be identified, i.e., “I provide a service”

## Slide 8: IRMK and Hash function
IRMK (Identifiable Random MAC Key)
STA generates the IRMK
  Could be constant; could vary for each SSID; could be preset.
  Option for AP to provide a key to the STA
STA shares IRMK with AP when first associated
STA provides IRM Hash in “IRM element”
The IRMK is used to resolve the identity of the STA
  verifies that the hash included in the IRM element matches the output of the local hash computation
  IRM hash = function (IRMK, IRMA)
Since the AP has the IRMK stored locally and has access to the IRMA included as the MAC address and the IRM Hash in the association packet, it can perform this computation and verify the IRMK
NOTE: A 128 bit hash function is proposed. A truncated SHA 256/128 hash may be used (see next slide)

## Slide 9: IRM Hash
Proposed to use SHA-256 truncated to 128 bits*, i.e.:
IRM Hash = SHA-256/128 (IRMK, IRMA)
Where SHA-256/128 is the truncated SHA-256 where the leftmost 128 bits of the 256-bit hash generated by SHA-256 are selected as the truncated 128 bit IRM Hash
A 3rd party chance of discovering the IRMK?
  Pre-image resistance
  1 in 2 128
Chance that AP finds wrong key or more than one key?
  Hash collision
  1 in 2 64
Two STAs pick same key
  Can ask for “New IRMK Request”
Note: AP can ask for new key if IRMK not found or duplicate, for example
* Could use other hash functions. Want to select a function already known and used.

## Slide 10: Basic Steps for IRM
STA indicates IRM support in Capability Field
STA generates 48 bit IRMA
  Generates a random 46 bit number
  Appends I/G = 0, U/L = 1 (Compatible with 12.2.10)
STA calculates IRM Hash value and includes it in the IRM element
  Element included in (re)association frame
  Element may be included pre-association ANQP frames
STA can also indicate other information for the AP, e.g.:
  First time association
  Been here before (you should have my key)
  Been here before but want to change key
When first associated, STA provides IRMK to AP
  Action frame Request and Response exchange(s)
  New key can be provided if STA wants
  AP can suggest new key
AP uses IRMA and stored IRMKs to calculate hash and identify the STA IRMK.
It’s important to note that the IRMK is not used to reveal the STA’s MAC or “identity” address but rather for verification purposes only, i.e., the hash matches

## Slide 11: IRM element
STA can use “private” address
IRM element sent in Association Request
AP then knows if STA IRMK already known (stored) or not
Change – Eliminates all chances of a brute-force attack.
See next slide

## Slide 12: IRMK Check field
IRMK Offset takes a value N, from 0 to 112 (Note: IRMK is 128 bits)
The Check field contains the 8 bits representing the EX-OR of the 8 bits of the IRMK, bN to bN+7 with the following 8 bits (bN+8 to bN+15)
i.e. For n = 0 to 7
Bits in Check field are bn = EX-OR (bN+n, bN+n+8) where bN is Nth bit in IRMK
As an example, IRKM Offset = 72
Check field b0 is EX_OR of bits 72 and 80, and b7 is EX-OR of bits 79 and 87
Acts as a “Hint” to the AP so AP can quickly find a stored IRMK.
But does not declare any part of the IRMK
Note that STA can change the IRMK at any point

## Slide 13: Action Frames to get IRMK
STA sends “Unknown”
AP sends IRMK Request, STA sends IRMK Response with IRMK
STA sends “Known” or “Change”
AP sends IRMK Confirm optionally with “IRMK check”
STA can ask AP for an IRMK (“Provide IRMK Request”)
AP can request New IRMK (with reasons)
STA can change IRMK whenever it wants (prevents any possible brute-force attack
Not sure required, can’t see a use case.
Suggest delete

## Slide 14: IRMK Confirm
The IRMK Confirm Action frame is transmitted from an AP to a non-AP STA to confirm that an IRMK has been recognized
The Check field allows the STA to check that it is the right IRMK without having to send 128 bits.
To provide extra security, AP confirms IRMK and STA can check it without having to declare the full IRMK

## Slide 15: AP requests new IRMK
AP can request a new IRMK (provides reason)
AP might delete stored IRMKs
  Old
  Capacity
If STA associates as “Known” and IRMK not found, then AP can request a new IRMA

## Slide 16: Pre-Association
STA can send IRM ANQP-element
AP can use the IRM Hash and the IRMA (TA) to find the IRMK
(Can only be used if AP already has the IRMK)

## Slide 17: Computational complexity lessened by IRMK Check
The “IRMK Check” field allows the AP to quickly sort ‘candidate’ IRMKs
  STA indicates 8 EX-OR’d bits of IRMK from a ‘random’ start
  AP can quickly sort through list to reduce number of possible IRMKs
IRM Check field also used by AP to Confirm IRMK back to STA.
  This provides double security that the AP is who it says it is, i.e. the same AP that was originally used to share the Key.

## Slide 18: Advantages
A different Random MAC can be used even when returning to same ESS – more privacy!
  Even though STA indicates “Known”, No way a 3rd party can know if same STA (unlike “same MAC address for same AP”)
  MAC address and IRM Hash field values change every time. The last associated IRMK stays constant at the AP.
An IRM STA can still choose to use “private” random MAC
  If no IRM Hash field, then private MAC address in use.
STA can change IRMK at any time
  Changed when associated. No way 3rd party can know. Hence even if brute force to find IRMK, if changed, impossible to know if same STA reassociates
  AP still knows that it is STA X even though IRMK has changed
AP can restrict its stored list if necessary and request a new IRMK if “No IRMK found”
  STA can provide old or new
  However, “IRMK Check” allows AP to keep a large store
STA can be identified pre-association
  AP can check stored IRMKs as soon as Association Request received OR wait for association
  STA can send IRMK-ANQP element
No reference to any ‘real’ address or real ID
Very flexible, easy to add Action frames
Provides an ID that solves many Use Case problems created by RCM

## Slide 19: 10 criteria
Is a private address/identifier dynamic or is it just a different static address/identifier? How often does/should it change?
  Dynamic as IRMA changes every time. The IRMK may remains constant or can be different per ESS. IRMK may be changed at an ESS.
Is it invertible such that the "real" address/identifier can be determined from a private address/identifier
  There is no concept of a “real” address. The IRMK stored at the AP identifies the STA.
Does a 3rd party know whether private identifiers are used?
  Yes, the U/L and I/G bits and “IRM capability” can indicate IRM is in use
Is it assumed that only certain entities can make a binding/track someone?
  Yes the AP must support and the STA makes the decision on whether to provide the IRMK
Is the private address/identifier bound to a secure connection or is unencrypted (poss. unassociated) use of this functionality required?
  Bound to a secure connection. Only pass IRMK when associated.
What are the assumptions on forgery of such an address/identifier? How hard does it need to be for someone to fake one?
  IRMK is well protected. 128 bit key and 128 bit hash function
Are there any requirements to force STAs to do a scheme like this?
  No, entirely up to the STA
What's the probability of collision?
  2 -64 or 2 -128
What about protecting client identities from the network?
  Actual ID is not known. Just an Identifier, i.e., the IRMK
What other requirements do we have on usage of this address/identifier (aside from “private”)?
  STA is only indicating it is the same STA as associated before. Also it can change its ID at any time.

## Slide 20: IRM Text
Document 21/1673 is the working document for the accompanying text

## Slide 21
QUESTIONS??

## Slide 22: Straw Poll
Do you agree that an Identifiable Random MAC scheme, along the lines as described in <this document>, should be further worked on for possible inclusion in the TGbh Amendment?