## Slide 1: TG bh Identifiable Random MAC Address (revised)
Date: 2022-01
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com
Olivia Fernandez | Harris |  |  | 

## Slide 2: Intro
This is a presentation on “Identifiable Random MAC Address”, IRMA
Original proposal was 21/1585r11
Changes made to the procedure such that STA spoofing is impossible

## Slide 3: 802.11 Definitions
  Identifiable Random MAC (IRM) : a scheme where a non-AP STA uses identifiable random medium access control (MAC) addresses (IRMA) to prevent third parties from tracking the non-AP STA while still allowing trusted parties to identify the non-AP STA.
Identifiable Random MAC Address (IRMA) – a random MAC address used by a STA using IRM
Identifiable Random MAC Key (IRMK) – a Key used to resolve an IRMA

## Slide 4: Identifiable Random MAC Address - IRMA
Purpose
  Prevent third-parties from tracking the STA while still allowing trusted parties to recognize the STA.
Identifiable
  Uses a key shared with trusted AP/network – IRMK
  IRMA is the random TA MAC address used by the STA
  STA generates an “IRM Hash” using IRMK and IRMA
  IRM Hash is sent in IRM element (in Association Request)
  STA changes IRMK for every network and association.
Changing fields
  The IRMA (TA), IRM Hash and IRMK change for every association
AP uses latest IRMK as the identification for the STA
  STA and AP keeps list of

## Slide 5: CAPABILITY BIT
An IRM Capability field is used in the STA and AP
The AP looks for the IRM Capability AND the IRM Hash in IRM element
AP can use the IRM Capability bit to indicate to STAs that there may be a reason to be identified, i.e., “I provide a service”

## Slide 6: IRMK and Hash function
IRMK (Identifiable Random MAC Key)
STA generates the IRMK
  Random128-bit number .
STA shares IRMK with AP when first associated
STA provides IRM Hash in “IRM element”
The IRMK is used to resolve the identity of the STA
  verifies that the hash included in the IRM element matches the output of the local hash computation
  IRM hash = SHA-256/128 (IRMK, IRMA)
  Could use a different Hash and could reduce IRMK to 64 bits.
Since the AP has the IRMK stored locally and has access to the IRMA (the TA address) and the IRM Hash in the association packet, it can perform this computation and verify the IRMK
NOTE: Scheme is based on known proven technology – “key derivation functions”.
A typical usage is take a secret, such as a password or a shared key (IRMK), and a random number (known as a ‘salt’) (IRMA) to produce a key (IRM Hash). Used in many applications.

## Slide 7: IRM Hash
Proposed to use SHA-256 truncated to 128 bits*, i.e.:
IRM Hash = SHA-256/128 (IRMK, IRMA)
Where SHA-256/128 is the truncated SHA-256 where the leftmost 128 bits of the 256-bit hash generated by SHA-256 are selected as the truncated 128 bit IRM Hash
A 3rd party chance of discovering the IRMK?
  Pre-image resistance
  1 in 2 128 (See slide 18)
Chance that AP finds wrong key or more than one key?
  Hash collision
  1 in 2 64
Two STAs pick same key , 1 in 264
  AP can ask for “New IRMK Request”
Could use other hash functions. Want to select a function already known and used.
Also could consider shorter IRMK, say 64 bit.
Actually this is a Key Derivation Function KDF, not a Hash.

## Slide 8: Basic Steps for IRM
STA and AP indicates IRM support in Extended Capability Field
First Time Association
STA generates 48 bit IRMA
  Generates a random 46 bit number
  Appends I/G = 0, U/L = 1 (Compatible with 12.2.10)
STA sends the IRM element in Association Request
  IRM Indicator set to “Unknown”
  IRM Hash is omitted.
After Association, AP requests the IRMK, and STA sends it.
Re-Associations
STA generate 48 bit IRMA
STA calculates IRM-Hash using IRMA and IRMK for that AP
STA sends the IRM element in Association Request
  IRM Indicator set to “Known” and IRM-Hash is included
AP uses IRMA and stored IRMKs to calculate IRM hash and identifies the STA IRMK.
AP then requests new IRMK from STA
AP and STA update their lists
It’s important to note that the IRMK is not used to reveal the STA’s MAC or “identity” address but rather for verification purposes only, i.e., the hash matches

## Slide 9: IRM element
STA can use “private” address
IRM element sent in Association Request
AP then knows if STA IRMK already known (stored) or not
See next slide
Element ID | Length | Element ID Extension | IRM Indicator | IRM Hash (Present only if IRM Indication is “Known”) | IRMK Check (Optional)

## Slide 10: IRMK Check field
IRMK Offset takes a value N, from 0 to 112 (Note: IRMK is 128 bits)
The Check field contains the 8 bits representing the EX-OR of the 8 bits of the IRMK, bN to bN+7 with the following 8 bits (bN+8 to bN+15)
i.e. For n = 0 to 7
Bits in Check field are bn = EX-OR (bN+n, bN+n+8) where bN is Nth bit in IRMK
As an example, IRKM Offset = 72
Check field b0 is EX_OR of bits 72 and 80, and b7 is EX-OR of bits 79 and 87
Acts as a “Hint” to the AP so AP can quickly find a stored IRMK.
Reduces the list of IRMKs by 1/256
e.g. correct key in a list of 1000 IRMKs found in just 2 calculations
Note that 256 combinations of the 16 bits satisfy the 8 bit Check field.
Reduces the integrity of key from 128 bits to 120 bits (see slide 18)

## Slide 11: Action Frames to get IRMK
STA sends “Unknown” if first time association
AP sends IRMK Request, STA sends IRMK Response with IRMK
STA sends “Known” if STA has previously associated with the AP
AP sends IRMK Request, STA sends IRMK Response with a new IRMK
AP can request New IRMK (with reasons)
AP can request “IRMK Check” (If many IRMKs stored for example, and Check not present in the IRM element).

## Slide 12: IRMK Check Request/Response
If AP has many IRMKs and STA did not include the IRMK Check field in IRM element, then AP can request it.
Notes:
STA could always includes Check in IRM element
STA could include Check only if it knows the AP is a busy one.
  IF STA recognizes AP as a “busy AP” then STA should include IRMK Check.
IRMK Check reduces the possibilities from 2127 to 2119
Note: 2119 = 6.65 x 1035
1 year = 3.15 x 1019 tera hash
This is way over the top for what we need. As the STA chooses a new key (IRMK) at every association, thee is no basic reason that the key or the hash be so long 128 bits.
Looking into using 64 or 72 bits for the key (IRMK)

## Slide 13: AP requests new IRMK
AP can request a new IRMK (provides reason)
REASON
AP might delete stored IRMKs
  Old
  Capacity
If STA associates as “Known” and IRMK not found, then AP can request a new IRMA

## Slide 14: Pre-Association
STA can send IRM ANQP-element
AP can use the IRM Hash and the IRMA (TA) to find the IRMK
(Can only be used if AP already has the IRMK)

## Slide 15: Security
The “IRMK Check” field allows the AP to down-select list
  Reduces APs stored list by 1/256
  Reduces security from 128 bits to 120 bits.
  3rd party must perform average of 2119 (6.65 x 1035) hash calculations to find the IRMK.
  A huge number, if performing 1 Hash calculation per tera second, takes 2 x 1016
  NOTE: as STA changes its IRMK on every association, there is no point in trying to find IRMK anyway.
Down-Select at AP with IRMK Check
  216 combinations for 16 bits, 28 combinations for 8 bit EXOR
  IRMK Check does not disclose any of the bits in the IRMK.
  Down Select is 216/28 = 256 i.e. 1000 IRMKs down selected to 4.
  1000 IRMKs in store, AP, on average, needs to check 2 to find correct IRMK

## Slide 16: IRM is very Secure
Every time STA associates, the address IRMA AND IRM Hash values change.
  Impossible to know if same STA associating.
Third party would need to brute strength all keys, IRMK (128 bits, or 120 bits if using IRMK Check), to find the IRMK. BUT, as IRMK changes each association, there is no point!!!
IMPOSSIBLE to know the STA.
Copying the IRMA and Hash from a previous association does not work, as the IRMK has been changed.

## Slide 17: Reduce the IRMK size?
As the IRMK is changed on every association, it could be made shorter. The important criteria are:
Chance of wrong key 2b/2
Chance of picking two the same 2b/2
For example, assume IRMK is 64 bits (8 octets)
Chance of wrong key 3x108
After IRMK Check effectively reduced to 256
  with 1 teraHash calculations per second (1012) takes 1 days on average to brute strength find the key.
However finding the key does not help as the key changes once associated

## Slide 18: STA details
IRM enables the AP to identify the STA,
  i.e. STA “123”
AP can exchange frames or higher layer APP can then associate STA 123 with some other specific details/IDs
  Membership ID , customer ID, guest ID, family member, employee ID, etc.

## Slide 19: Advantages
A different Random MAC can be used even when returning to same ESS – more privacy!
  Even though STA indicates “Known”, No way a 3rd party can know if same STA (unlike “same MAC address for same AP”)
  MAC address and IRM Hash field values change every time. The last associated IRMK stays constant at the AP.
An IRM STA can still choose to use “private” random MAC
  If no IRM Hash field, then private MAC address in use.
STA changes IRMK at every association
  Changed when associated. Hence even if brute force were practical to find IRMK, if changed, impossible to spoof or know if same STA reassociates
  AP still knows that it is STA X even though IRMK has changed
AP can store and long list but can request a new IRMK if “No IRMK found”
  IRMK Check down selects the list by a factor of 256
  AP can request IRMK but must provide a reason
STA can be identified pre-association
  AP can check stored IRMKs as soon as Association Request received OR wait for association
  STA can send IRMK-ANQP element
No reference to any ‘real’ address or real ID
Spoof attacks are nullified
Very flexible, easy to add Action frames
NOTE: Compatible with the ID Action frames.
Provides an ID that solves many Use Case problems created by RCM

## Slide 20: IRM Text
Document 21/1673 is the working document for the accompanying text

## Slide 21
QUESTIONS??

## Slide 22: Straw Poll
Do you agree that an Identifiable Random MAC scheme, along the lines as described in <this document>, should be included in the TGbh Amendment?