## Slide 1: Discussion on one-to-one sensing measurement instance
Date: 2021-09-29
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Pei Zhou |  |  |  | 
Lei Huang |  |  |  | 

## Slide 2: Introduction
The group has discussed to support an NDPA/NDP-based measurement procedure. [1]
We assume non-TB sensing only applies to one-to-one sensing scenario (only one Transmitter and one Receiver)
This contribution discusses more about the order of NDP frames in the procedure.

## Slide 3: Background-Unidirectional Sounding
Only consider (AP, non-AP STA) case, do not consider P2P case.
Unidirectional: in a single measurement instance, there are only two participants (AP and non-AP STA) , and one is Transmiter, the other is Receiver.
Case U1: if AP (Transmitter) obtains TXOP, then we assume to use TB procedure.
Case U2: if non-AP STA (Transmitter) obtains TXOP, then we assume to use non-TB procedure.
U1 (TB)
U2 (non-TB)

## Slide 4: Background-Bidirectional Sounding
Only consider (AP, non-AP STA) case, do not consider P2P case.
Bidirectional: in a single measurement instance, there are only two participants (AP and non-AP STA) and are both Transmiter and Receiver.
Case B1: if AP (Transmitter) obtains TXOP, then we assume to use TB procedure.
Case B2: if non-AP STA (Transmitter) obtains TXOP, then we assume to use non-TB procedure.
B1 (TB)
B2 (non-TB)

## Slide 5: Possible Solutions
Option | Description | Pros. | Cons.
1 | Fixed order: The AP always obtains TXOP and transmits NDPA | Simple | Could not apply to unidirectioanl case U2
2 | Fixed order: The non-AP STA always obtains TXOP and transmits NDPA | Simple | Could not apply to unidirectioanl case U1
3 | Flexible order: The order is decided in measurement setup. | Flexible | More info in measurement setup
4 | Flexible order: any Transmitter (AP or non-AP) that obtains TXOP may initiates the measurement instance. | Flexible; Double the chance to get TXOP; Could apply to U1, U2, B1 and B2 | N/A

## Slide 6: SP 1
Do you agree to add the following into 11bf SFD ?
  Any STA in Transmitter role may attempt to obtain an TXOP to initiate a one-to-one sensing measurement instance.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 7: SP 2
Do you agree to add the following into 11bf SFD ?
  In a one-to-one sensing measurement instance, if the AP obtains TXOP, then this instance shall be initiated as a TB measurement instance.
  In a one-to-one sensing measurement instance, if the non-AP STA obtains TXOP, then this instance shall be initiated as a non-TB measurement instance.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 8: SP 3
Do you agree to add the following into 11bf SFD ?
  For a non-TB measurement instance, the non-AP STA initiates the instance by transmitting NDPA.
    The non-AP STA transmits NDP at SIFS after NDPA.
    Optionally, the AP transmits NDP at SIFS after receive NDP from the non-AP STA.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 9: Reference
[1] 11-21-1015-02-00bf-non-tb-and-tb-measurement-procedure-for-wlan-sensing
Chaoming Luo (OPPO)