## Slide 1: TID to Link Mapping Enhancements
Date: 2021-11-016
Authors:
Name | Affiliations | Address | Phone | Email
Pooya Monajemi | Cisco |  |  | pmonajem@cisco.com
Brian Hart |  |  |  | brianh@cisco.com
Malcolm Smith |  |  |  | mmsmith@cisco.com
Eldad Perahia | HPE |  |  | eldad.perahia@hpe.com
Gaurav Patwardhan |  |  |  | gaurav.patwardhan@hpe.com
Notes: September 2012

## Slide 2: Topics
Introducing a number of TID-to-link-mapping concepts
  Forms of mapping
  Priority indication
  Broadcast Advertisement
  Association procedure
Includes policy aspects
  Motivation for policy
R1/R2 targets

## Slide 3: Motivation – 1/2
Enterprise APs support a number of features today
  To help all STAs, and solve real deployment problems. Relevant here is load balancing between bands because APs, with concurrent radios and not being as energy constrained as clients, have greater visibility on instantaneous and recent load on all bands
  For MLO to be widely enabled, MLO needs to support and enhance those practically-necessary features, not undermine them.
Wider discussions indicate IEEE needs more focus on marketing value of 11be
Responsibly enabling MLO
  Today an enterprise AP can manage 200+200+200 clients. Great challenges will arise with this number of clients in MLO mode
  MLO with all-to-all will increase congestion, which can undermine the value of MLO and in fact performance can go significantly backwards. See Ref [3]
  As the number of contending clients varies, it becomes necessary to dynamically enable MLO when congestion levels are suitable or smoothly revert to known-good (non-MLO) configuration
Low Latency
  Potentially the most valuable aspect of 11be in many deployments
  AP may move clients with low-latency applications to clean links

## Slide 4: Motivation – 2/2
MLO advantage for load balancing
  MLO with default mapping and the use of Link Recommendation will continue to be used as primary tool for load balancing
  MLO as it stands today can be updated to accommodate load balancing and replace disassoc-imminent BTM or de-auth
    For critical cases, AP side needs an additional and complementary tool to enforce more rigid link transition decisions
    Can revert to enabling complete set of links when traffic situation improves
Concerns for non-AP STAs
  Power consumption associated with having to frequently wake up on each link
  Scheduler complexity associated with having to frequently wake up on each link
  Duplicate avoidance on groupcast data : STA should have a method to avoid receiving duplicate groupcast data when it is switching from one link to another
  Coex factors

## Slide 5: State of the Draft
Default mapping is all-to-all
Negotiation required for a non-default mapping
  Negotiation may be broken by either side at any point in time to go back to default mapping
Non-AP STA may initiate mapping by including the TID-to-Link-Mapping element in assoc request.
AP may reject with one of the following:
  DENIED_TID_TO_LINK_MAPPING
  PREFERRED_TID_TO_LINK_MAPPING_SUGGESTED (and include suggestion)
STA Capability :
  Set to 0 if dot11TIDtoLinkMappingActivated is false.
  Set to 1 if dot11TIDtoLinkMappingActivated is true and the MLD supports mapping each TID to the same or different link set. (General TID mapping)
  Set to 2 if dot11TIDtoLinkMappingActivated is true and the MLD supports mapping all TIDs to the same link set. (All-TID-to-link-subset mapping)

## Slide 6: All-TID-to-Link-Subset Mapping
Mode of mapping equivalent to disabling a link or being associated to a subset of links
STA implementations naturally support All-TID-to-Link-Subset mode
  Similar to existing dual/tri-band non-concurrent implementations
  Any conflicts (coex/etc) are temporary
  Link switch complications with avoiding duplicate groupcast data can be addressed through allowing enough time for STA to switch
Proposal For R1:
  If the AP MLD is TID-to-Link mapping capable, then a non-AP MLD that requests more than one link in association shall support all-TID-to-link-subset mapping(value 2), may support the general mapping (value 1)
  If indicated as mandatory by the AP (see mapping priorities in later slides), a non-AP STA shall accept an all-TID-to-link-subset mapping
    Mapping change only takes effect at the next DTIM boundary
Link Subset |  |  |  |  | 
Link 1 | TID0 | TID1 | TID2 | TID3 | …
Link 2 | TID0 | TID1 | TID2 | TID3 | …
Link 3 | x | x | x | x | …

## Slide 7: Other Forms of TID Mapping
Not all STAs expected to support these other forms
Complications arise from a disjoint mapping of TIDs
  May cause scheduler issues, power consumption increase, etc.
If all TIDs can be communicated reliably on one link, the above power consumption and scheduler issues are addressed, while still possible to assign high priority/low latency traffic to specific links
Enhanced Link Subset |  |  |  |  | 
Link 1 | TID0 | TID1 | TID2 | TID3 | …
Link 2 | TID0 | TID1 | TID2 | TID3 | …
Link 3 | X | X | TID2 | TID3 | …
Draft text options for R2:
Option 1 : Define value 3 for the enhanced link subset mapping scheme
Option 2: No capability defined, but behavior is specified in spec
  Non-AP STA with capability “1” is able to use enhanced link subset mapping
  For a non-AP STA with capability “2” (only supports all-TIDs-to-link-subset), the above scheme is treated the same as all-TIDs-to-link-subset mapping on the link(s) that have all TIDs mapped
Enhanced Link Subset Mapping: all TIDs are mapped to one subset of links, while some TIDs may also be mapped to links outside this subset
A non-AP STA that supports general TID mapping (ie capability value 1) should accept a TID mapping negotiation that complies with the enhanced link subset mapping

## Slide 8: Priority Indication
Method needed for AP to indicate priority level for proposed mapping scheme
Desired to also have a method for non-AP to indicate the priority level in negotiations
  Useful to have other information from non-AP STA as well, such as preferred links
  Other information beyond the scope of this presentation, open to suggestions
Propose allocation of 2 bits in TID mapping negotiations (R1)
  At least one value is reserved as “mandatory” when negotiation is initiated from the AP
    Two values can be used to differentiate between “mandatory-override existing negotiation” and “mandatory-if no negotiation exists”
  Once operating under a mandatory mapping, a non-AP STA shall initiate a new negotiation in order to modify the mapping (including going back to default mapping)
TID-To-Link Control field of the TID-To-Link Mapping element

## Slide 9: Priority Interpretations
Priority Subfield Value | Request by AP MLD | Request by non-AP MLD | Response by AP MLD | Response by non-AP MLD
0 | Inquiry Only | Inquiry Only | Reserved | Reserved
1 | Request a change | Request a change | Amenable to change | Amenable to change
2 | Mandatory – Except Existing | Reserved | Prefer not to change | Prefer not to change
3 | Mandatory – Override Existing | Reserved | Cannot accept change | Strong objection to change

## Slide 10: Advertisement
AP may advertise a mapping scheme
  May be advertised with a priority level of preferred or mandatory
  Included in Beacons / Probe Responses / Assoc Responses
STAs are encouraged/required to adhere to this mapping
  Encouraged or required is based on priority level announced
  A STA’s mapping scheme X complies with an advertised mapping scheme Y if, for each TID, the set of all the mapped links in Y is a subset of the set of all the mapped links in X
  Two priority levels reserved for indicating if we are overriding existing negotiations
  STA may enforce the new mapping at DTIM boundaries (to avoid groupcast duplicates)
  A link that is advertised as disabled in the Beacon’s mapping scheme, if mandatory, may not be used to initiate association or for probing
R1 : An R1 AP MLD can only advertise an all-TID-to-Link-Subset mapping as mandatory
R2 : An R2 AP MLD may also advertise an Enhanced Link Subset mapping as mandatory
  When a non-AP STA supports general TID mapping, it may either switch to the same mapping scheme as advertised by the AP, or announce a compliant scheme (ie. no negotiation)
  When a non-AP STA supports only all-TID-to-link-subset mapping, if the AP advertised mapping is an enhanced link subset mapping, then the STA maps all TIDs to the subset of advertised links that have all TIDs mapped (compliant).

## Slide 11: Association Procedure
Current Draft :
STA may initiate mapping by including the TID-to-Link-Mapping element in assoc request.
AP may reject with one of the following:
  DENIED_TID_TO_LINK_MAPPING
  PREFERRED_TID_TO_LINK_MAPPING_SUGGESTED (and include suggestion)
Proposal for R1:
Sequence 0: AP doesn’t advertise a TID mapping scheme. Client’s preference adopted directly
  Default or client’s requested TID-to-link-mapping is accepted
Sequence 1: AP advertises a mandatory mapping scheme. Client initiates association with a compliant mapping, association is accepted.
Sequence 2: AP advertises a mapping scheme, a negotiation ensues
  AP advertises a TID mapping scheme (mandatory or preferred)
  Client sends association request
  AP includes TID-to-link-mapping IE in assoc response frame (unsolicited or in response to client’s request)
    TID-to-link-mapping IE includes field to indicate AP priority
  AP may disassociate client if TID-to-link-mapping negotiation fails

## Slide 12: Conclusions
Topics covered
Need for all-TID-to-link-subset mapping support
Defining the enhanced link subset mode of TID mapping
Enhancements in association procedure
Defining the priority bit in mapping announcements and negotiations
  Rules for non-AP compliance when mandatory mapping is proposed
Broadcast mapping announcement

## Slide 13: SP1
Do you agree that in R1 if an AP MLD is TID-to-Link mapping capable, then STA MLD that requests more than one link in association request to that AP MLD shall support all-TID-to-link-subset mapping, and may support the general mapping?

## Slide 14: SP2
Do you agree to define a priority level in R1 in the TID to link mapping negotiation frame as follows:
  Priority value can be used by both non-AP and AP
  When sent by an AP the highest value indicates mandatory
  A non-AP STA MLD shall initiate a new TID-to-link-mapping negotiation in order to modify the existing mapping, if the existing mapping was formed with the highest priority indicated by the AP

## Slide 15: SP3
Do you agree that in R1 a non-AP MLD shall comply with a TID mapping negotiation initiated by the AP MLD as mandatory when the mapping scheme announced by the AP is either all-TID-to-link-subset mapping or enhanced link subset mapping?
  An enhanced link subset mapping is one in which all TIDs are mapped to one subset of links, while some TIDs may also be mapped to links outside this subset
  Mapping scheme A is compliant with mapping scheme B if there exists no TID which is mapped to a link in A that is not mapped to that link in B
  Note : As defined above, a non-AP STA that is only capable of all-TID-to-link-subset mapping can comply with an enhanced link subset mapping by choosing the subset of links that have all TIDs mapped.

## Slide 16: References
[1] 11be Draft 1.0
[2] 11-21/0792r3 PDT for CC34 Resolution for CID3222
[3] 11-20/1841r2 Performance Evaluation of Various MLO TID Mapping Configurations

## Slide 17: Backup

## Slide 18: TID-To-Link Mapping Element