## Slide 1: Simplified Scaling Factor Feedback for CSI Matrices Quantization
Date: 2021-10-12
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin |  |  |  | 
Osama AboulMagd |  |  |  | 
Edward Au |  |  |  | 

## Slide 2: Background
802.11n Specification provides the detail CSI matrices quantization procedure [1]
We examined the 11n based CSI matrices quantization with simulations
The procedure of scaling factor computation in 11n specification seems quite complicated by repeating the linear to dB and dB to linear conversion
We propose a simplified scaling factor computation procedure and check the performance based on the simplified scaling factor computation

## Slide 3: 802.11n CSI matrices quantization procedure [1]
The maximums of the real and imaginary parts of each element of the matrix in each subcarrier are found as following
The scaling ratio is calculated and quantized to 3 bits as following

## Slide 4: 802.11n CSI matrices quantization procedure continues [1]
3. Linear Scaler of step 2 is given as following
4. The real and imaginary parts of each element in the matrix (k) are quantized to Nb bits in twos complement encoding as defined by following
NSR indicates the half the size of
Subcarriers per symbol excluding Nulls
k is the subcarrier index
R represents real component
I represents imaginary component

## Slide 5: Simplified Scaling Factor based CSI matrices quantization
The maximums of the real and imaginary parts of each element of the matrix in each subcarrier are found as following
Choose the scaling factor, as following, (now is not a function of subcarrier)
3. The real and imaginary parts of each element in the matrix (k) are quantized to Nb bits in twos complement encoding as defined by following

## Slide 6: How to recover the CSI matrices in the Initiator
* /
Where is the recovered CSI per subcarrier, per a spatial stream, and per Real (Imag) component
Where is the quantized CSI fed-back per subcarrier, per a spatial stream, and per Real (Imag) component
is the scaling factor in case of our proposed simplified scaling factor
For 11n based CSI quantization, becomes (k)

## Slide 7: Quantization of scaling factor ()
Let’s denote the quantized scaling factor to be
  (Quantize)
Let’s assume K bits to be the quantization size for
 Feedback to the initiator
The reconstruction of scaling factor at the initiator

## Slide 8: Simulation
80 MHz (11ax SU-PPDU Tone Plan), 2X2 MIMO
  Hence, there are 8 CSI matrices values to feedback per sub-carrier
  The number of subcarriers to feedback depends on Ng size, we used Ng=1 for simulation, but for total bit size analysis, Ng=2 assumed
20 MHz (11ax SU-PPDU Tone Plan), 1X1
  There are 2 CSI matrices values to feedback per sub-carrier
Tested over 100 different TGn-D channel realizations
Performance metric
  Source to Quantization Noise Ratio (SQNR) : 10log(E(x2)/E(q2)) (dB), where x is the source data (raw CSI) and q is the quantization noise (difference between the raw CSI in the responder and the recovered quantized CSI feedback in the initiator)

## Slide 9: Simulation Results
FB Bit size (Nb) | 11n based (SQNR, dB) | Total Size of FB Bits | Steve’s Low complexity Scaling [2] (=SQNR, dB) | Total Size of FB Bits | Our proposed Simplified Scaling Factor (SQNR, dB) | Total Size of FB Bits
4 | 23 | 15120 | 21 | 15120 | 18 | 13840
6 | 36 | 22032 | 33 | 22032 | 31 | 20752
8 | 48 | 28944 | 45 | 28944 | 43 | 27664
10 | 60 | 35856 | 57 | 35856 | 55 | 34576
12 | 72 | 42768 | 69 | 42768 | 67 | 41488
Total FB size is (3+2*Nb*Nr*Nc)*(Number of Fed-back subcarriers) for 11n based CSI Quantization, and Steve’s Low complexity scaling method (Not clear 3 bits of scaling factor is fed-back in [2] but assumed to be 3 bits here)
Total FB size for our proposed Simplified Scaling Factor method is 16+(2*Nb*Nr*Nc) * (Number of Fed-back subcarriers)  16 is from M =4 and K is 12 according to slide 7
For the analysis of the total FB Bit size, 80 MHz with Ng=2 is assumed for the Number of Fed-back subcarriers, 432
Our proposed Simplified Scaling Factor method shows about 1500 total bits smaller than 11n based method which is about 0.5 bit save per Nb size, that is about 3 SQNR dB save.

## Slide 10: 20 MHz Sim Results
The degradation of our proposed Simplified Scaling Factor method is reduced to 4 dB, compared to the 11n based in 20 MHz 1X1
FB Bit Size | 11n based (SQNR) | Our proposed Simplified Scaling Factor (SQNR)
4 | 36 | 32
6 | 49 | 45
8 | 61 | 57
10 | 73 | 69
12 | 85 | 81

## Slide 11: Summary
We proposed a simplified scaling factor method to improve the 11n based CSI matrices quantization procedure
  Now, we do not have to convert the linear scale factor to dB, and dB to linear anymore
  Performance degradation is only 2dB worse than 11n based method for 80 MHz, 2x2 Ng=2 CSI feedback case, in consideration of the total FB Bit size in each CSI report time

## Slide 12: Reference
[1] 802.11-2012.pdf, page 1731
[2] S. Shellhammer, et. al., “Quantization Error Analysis for CSI Report”, TGbf, 21/1595

## Slide 13: SP 1
Do you agree that the 11n based CSI matrices quantization method in [1] and recapped on slide 3&4 is the mandatory CSI quantization method for the CSI report?
  Y/N/Abs

## Slide 14: SP 2
Do you agree that the simplified scaling factor feedback, a single scaling factor per CSI report described on slide 5&7 is an optional CSI quantization method for the CSI report?
  Y/N/Abs