## Slide 1
Start time sync PPDUs medium access considering internal collision
Date: 2021-10-11
Authors:

## Slide 2: Introduction
In Draft 1.1, Start time sync PPDUs medium access is defined [1]
The defined medium access procedure does not cover internal collision cases
  While waiting with the backoff counter of a certain AC at zero, the backoff counter of other AC may become zero leading to internal collision
  There should be a clear rule to resolve the internal collision
This contribution discusses “Start time sync PPDUs medium access” in case of the internal collision

## Slide 3: Recap: Start time sync PPDUs medium access
In Draft 1.1, Start time sync PPDUs medium access is defined [1]
  A STA of an MLD operating on a link that is part of an NSTR link pair for that MLD shall follow the channel access procedure described below:
    The STA may initiate transmission on a link when the medium is idle as indicated by the physical and virtual CS mechanism and one of the following conditions is met:
      The STA obtained an EDCA TXOP following the procedure in 10.23.2.4 (Obtaining an EDCA TXOP).
      The backoff counter of the STA is already zero, and the STA operating on the other link of NSTR link pair of the affiliated MLD obtains an EDCA TXOP following the procedure in 10.23.2.4 (Obtaining an EDCA TXOP).
    When the backoff counter of the STA reaches zero, it may choose to not transmit and keep its backoff counter at zero.
    If the backoff counter of the STA has already reached zero, it may perform a new backoff procedure following deferral procedures as described in 10.23.2.4 (Obtaining an EDCA TXOP) and 10.3.4.3 (Backoff procedure for DCF). CW[AC] and QSRC[AC] are left unchanged.

## Slide 4: Internal collision
In Draft 1.1, internal collision is defined for a STA that has chosen not to transmit
  A STA that chooses not to transmit after the backoff counter reached zero on a link of NSTR link pair may have one or more EDCAF backoff counters with value zero on that link. The STA that initiates transmission on that link following condition a) or b), and has one or more EDCAF backoff counters that already reached zero shall choose only one implementation specific EDCAF for the transmission.
There is an ambiguity on handling multiple EDCAF backoff counters
  When more than two EDCAF backoff counters become zero, this shall be handled as an internal collision
There are several possible cases for choosing only one implementation specific EDCAF
  However, due to internal collision resolution, while keeping one EDCAF backoff counter at zero, if one of the other EDCAF backoff counters becomes zero, a STA shall choose one EDCAF backoff counter to keep zero.

## Slide 5: Internal collision
Letting multiple EDCAF backoff counters become zero is a violation of internal collision resolution (10.23.2.4)
  In order for multiple EDCAF backoff counters to become zero, a STA, which applied a rule “may choose to not transmit and keep its backoff counter at zero” to one of ACs, shall apply the same rule to the other ACs.
While keeping one EDCAF backoff counter at zero, if one of the other EDCAF backoff counters becomes zero, a STA shall
  choose the AC between two ACs which become EDCAF backoff counter zero
  and “may choose to not transmit and keep its backoff counter at zero”
How to handle CW[AC] and QSRC[AC] for the AC which is not chosen ?
  In internal collision resolution, when an AC is not chosen, CW[AC] and QSRC[AC] shall be updated
  However, this is a special case, CW[AC] and QSRC[AC] might be handled differently
Which AC to choose might not be an implementation specific
  As in the base spec, higher priority AC might be chosen
  In multi-link case, the AC which has reached zero first might be chosen

## Slide 6: Internal Collision Resolution
In link 1, AC_VI backoff counter has reached zero and chosen not to transmit
While keeping AC_VI backoff counter at zero, AC_VO backoff counter has become zero. A STA shall decide a backoff counter between the two to keep at zero
  The AC of higher priority AC
  The AC reached zero first
As a result of internal collision resolution, the ACs of frames transmitted over link 1 and link 2 using synchronized transmission might be different.

## Slide 7: Internal Collision Resolution
As a result of internal collision resolution, the ACs of frames synchronously transmitted over multiple links might be different.
A rule for CW[AC] and QSRC[AC] needs to be decided
  If the AC of higher priority AC is chosen
    CW[AC] and QSRC[AC] may be updated
      Penalty for not to transmit and keep its backoff counter at zero
    CW[AC] and QSRC[AC] shall be unchanged
      It could have transmitted the frame. It is waiting for the other link’s backoff reach zero
  The AC reached zero first
    CW[AC] and QSRC[AC] shall be unchanged
If the frames of the same AC shall be transmitted over multi-link, a different rule needs to be defined

## Slide 8: Reference
[1] Draft P802.11be D1.1
[2] 11-20/1730r3, “UL Sync Channel Access Procedure”
[3] 11-21/0514r10, “CC34 Comment Resolution for Sync PPDU start time”

## Slide 9: Straw Poll #1
Is a rule for internal collision resolution required in Start time sync PPDUs medium access?
  Yes
  No