## Slide 1
TXOP limit considerations in
an NSTR link pair
Date: 2021-10-11
Authors:

## Slide 2: Introduction
In Draft 1.1, Start time sync PPDUs medium access is defined [1]
In Draft 1.1, PPDU end time alignment is also defined for simultaneous transmission [1]
The defined medium access procedure may choose to transmit PPDUs of different ACs over multiple links
Each AC has its own TXOP limit
There is a case where synchronized transmission with end time alignment is not possible due to the TXOP limit difference
This contribution discusses TXOP limit differences in an NSTR link pair

## Slide 3: Different AC’s frames over an NSTR link pair
In Draft 1.1, implementation specific EDCAF selection is recommended
  A STA that chooses not to transmit after the backoff counter reached zero on a link of NSTR link pair may have one or more EDCAF backoff counters with value zero on that link. The STA that initiates transmission on that link following condition a) or b), and has one or more EDCAF backoff counters that already reached zero shall choose only one implementation specific EDCAF for the transmission.
Since the other link’s backoff finishes later than the link with implementation specific AC selection, different AC might be selected
In case of sync transmission, TXOP holder can be the STA of each link
In case of AP MLD, the AC of one link of an NSTR link pair and the AC of the other link of an NSTR link pair might be different
In an NSTR link pair, end time alignment is crucial in order to avoid NSTR interference

## Slide 4: TXOP duration selection on ML start time sync PPDUs medium access (1/2)
When different AC’s frames are transmitted over an NSTR link pair, TXOP duration selection rule shall be modified
TXOP duration is selected within a value of TXOP limit
In a certain case, end time can not be aligned due to TXOP limit

## Slide 5: TXOP duration selection on ML start time sync PPDUs medium access (2/2)
Therefore, TXOP duration of one link shall be selected considering TXOP limit of the other link
When TXOP limit of one link is shorter than TXOP limit of the other link, short TXOP duration shall be selected for both links.

## Slide 6: TXOP selection for downlink end time alignment
The AP of each link performs medium access procedure and transmits PPDU
The AC of link1 can be different from the AC of link2
Due to different TXOP durations selected within the value of TXOP limits, NSTR interference may cause a frame error
Possible solution
  Option 1) Delayed ACK
  Option 2) Delayed PPDU transmission

## Slide 7: DL TXOP limit difference – Option 1
Block ACK can be delayed until the transmission of the other link finishes in order to avoid interference

## Slide 8: DL TXOP limit difference – Option 2
Transmission of the PPDU with smaller TXOP duration can be delayed in order to align the end time

## Slide 9: Conclusion
In this contribution, TXOP selection for NSTR transmission was discussed
Each link’s TXOP owner shall be the STA of an operating link
In an NSTR link pair, the chosen AC of one link might be different from the chosen AC of the other link
Since each AC has its own TXOP limit, some considerations are required for sync PPDUs medium access and end time alignment
  TXOP selection for sync PPDUs medium access
  Delayed ACK or PPDU transmission for end time alignment

## Slide 10: Reference
[1] Draft P802.11be D1.1
[2] 802.11-19/1144r6 Channel Access for Multi-link Operation
[3] 802.11-20/0026r7 MLO: Sync PPDUs
[4] 802.11-20/0275r2 MLO: Need for sync PPDUs
[5] 802.11-20/0487r5 Multiple Link Operation Follow Up
[6] 802.11-20/0081r3 MLO-Synch-Transmission

## Slide 11: Straw Poll #1
Do you agree with the followings ?
1. The TXOP owner of multi-link is the STA of each link
2. A TXOP duration selection rule needs to be defined in case of transmitting PPDUs of different ACs over an NSTR link pair.
  Yes
  No