## Slide 1: Proxy for non-AP Initiator
Date: 2021-10-14
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Pei Zhou |  |  |  | 
Lei Huang |  |  |  | 

## Slide 2: Introduction
A sensing initiator might be a sensing transmitter, a sensing receiver, both or neither. (Motion 10c, 21/0147r3)
There are a few discussions on sensing measurement flow for non-AP initiator, involves AP as coordinator and other non-AP responders case, as in 21/1331r0.
This contribution discusses about measurement setup and reporting procedure if the Initiator is a non-AP STA.

## Slide 3: Recap: AP Initiator
An example of the sensing measurement by AP Initiator. [21/0644r4]

## Slide 4: Proposal: Proxy for non-AP Initiator
Only consider (AP, non-AP STA) case, do not consider P2P case.
If the Initiator is a non-AP STA, and Responders include other non-AP STAs and AP, a simple way is to ask the AP to be a proxy for the Initiator.
Case 1: the Initiator does not participate in measurement. (neither TX nor RX).
Init Request & Response
Measument setup
Measument (e.g. trigger based)
Reporting to Proxy
Proxy forwards Reports (or processed result) to Initiator

## Slide 5: Proposal: Proxy for non-AP Initiator
Only consider (AP, non-AP STA) case, do not consider P2P case.
If the Initiator is a non-AP STA, and Responders include other non-AP STAs and AP, a simple way is to ask the AP to be a proxy for the Initiator.
Case 2: the Initiator participates in measurement.
Init Request & Response
Measument setup
Measument (e.g. trigger based)
Note: STA 1 parcipates.
Reporting to Proxy
Note: STA 1 may also report to Proxy if Proxy will do data processing
Proxy forwards Reports (or processed result) to Initiator

## Slide 6: Proposal: Proxy in Measurement Setup and Reporting
In Measurement Setup phase, the Initiator may send Measurement Init Request to AP, to inform the AP to be the Proxy, information may include:
  AID/UID/MAC of Responders
  How does the Proxy report the result to the Initiator, e.g., forward the received reports to the Initiator, or, process the reports and generate and send the final sensing result to the Initiator.
  Sensing use case (e.g., gesture detection, or people presense detection) and/or accuracy requirements (e.g., range/velocity/angular accuracy) for processing the reports if needed.
In Reporting phase, Receivers send reports to the Proxy. the Proxy may forward the received reports to the Initiator, or, process the reports and generate and send the final sensing result to the Initiator.
  If the Initiator peforms as one Receiver and the Proxy does not process the reports, the Initiator does not send report to the Proxy.

## Slide 7: SP 1
Do you agree to add the following into 11bf SFD ?
  If the Initiator is a non-AP STA, and Responders include other non-AP STAs and AP, the AP may work as Proxy for the Initiator in measurement setup and reporting phases.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 8: SP 2
Do you agree to add the following into 11bf SFD ?
  The Proxy may forwad measurement reports to the Initiator, and/or, the Proxy may process the measurement reports and report the sensing result to the Initiator.
    The Initiator may send sensing requirement information for data processing to the Proxy in measurement setup. Detailed information is TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 9: Reference
[1] 11-21-0644-04-00bf-sensing-session-and-measurement-exchange-identification
[2] 11-21-0147-03-00bf-definitions-and-scenarios-of-the-wlan-sensing-follow-ups
[3] 11-21-1331-00-00bf-further-consideration-on-sensing-measurement-flow-for-non-ap-initiator
Chaoming Luo (OPPO)