## Slide 1: CR for Low-Latency stream identification
Date: 2022-01-21
Authors:

## Slide 2: Abstract
In this contribution, we discuss about how to identify and discriminate latency sensitive traffics, in order to be efficiently transported over 802.11be resource reservation mechanisms (e.g. rTWT).

## Slide 3: Motivation
Section “35.7.2.1 Latency sensitive traffic differentiation” of 802.11be D1.1 is empty
There are inconsistencies in 802.11be D1.1 :
  Restricted TWT DL/UL TID Bitmaps (9.4.2.199 TWT element) specify TID(s) identified as latency-sensitive streams
  SCS has been recently re-introduced along with modified TSPEC specification and TCLAS classification, providing a fine identification of latency-sensitive streams.
  =>It seems that a traffic specification is provided (SCS), but no medium access means is setup for accurate transportation
Issue not yet addressed:
  There could have several LL streams on a STA, but also non-LL streams that share same TID/AC as LL streams. Non-LL streams shall not take advantage of medium access offered to LL streams., otherwise unfair !
LL stream: Low-Latency, aka. Latency Sensitive, stream/traffic

## Slide 4: Related CIDs
CID | Commenter | Clause Number | Comment | Proposed Change | 
6511 | Pascal VIGER | 35.6.2.1 | "Latency sensitive traffic differentiation" is not clear enough. As nowadays a end-device is multiple content producer, there shall exist a diferenciation of latency sensitive and not-latency-sensitive traffics (e.g. from local application) belonging to a same TID. Otherwise, considering all traffics belonging TID as identical transportation is unfair ! | as in comment. Please consider fairness by differenciating transportation of LS and non-LS traffic of a same TID | Assigned: Duncan Ho
6521 | Pascal VIGER | 35.4.2 | There is plan to add TSPEC based signaling to provide parameters that describe traffic characteristics within the SCS procedure, especially the low latency (LL) parameters, so that AP shall be able to create an optimal schedule. In order to meet those Low latency requirements, the AP shall be able to finely (or let us say only) trigger the LL data, and not all the pending data of same traffic class or TID (because the remaining traffic remaining in the TID are not-LL sensitive and shall not be conveyed with same means like rTWT). | The LL data shall be managed by SCSID identifier for the communications, that is to say the SCSID is used to discriminate LL data inside a TID and that have to be handled by LL medium access mechanisms: e.g. MU triggering, rTWT use. In complement, the LL data shall be conveyed over multiple links, independently of remaining not-LL traffic. | Assigned: Duncan Ho

## Slide 5: Discussion
3 main elements have to be considered for latency-sensitive stream:
  Buffer status report (BSR) is used to indicate to the AP the amount of data the STA has available in its queues for transmission.
    BSRs takes the form of QoS-Control with Queue Size, or BSR-Control
    BSR can be solicited by a TF
  Trigger Frame is used by AP to control medium access and trigger a specific stream
  Restricted-TWT (rTWT) : UL/DL TID bitmap are under consideration
Current issues:
  BSR:
    BSRs work at AC level (Queue Size subfield, Queue Size All subfield)
  Trigger frame :
    Today, only Preferred AC may be identified
  rTWT:
    Problem is that a TID can also contain non latency sensitive (non-LL) data, thus it is unfair to transport those non-LL data as well as highest-priority LL data.

## Slide 6: Proposal
An LL stream is individually specified by a Qos_Characteristics IE within an SCS Descriptor.
It is therefore required to consider both TID and SCSID to qualify the stream in both BSRs and TFs for efficient UL MU operation :
SCSID-based low latency traffic differentiation mechanism, to be used by high-end STAs able to finely separate low latency data against normal data,
TID-based low latency traffic differentiation, for other STAs.

## Slide 7: Related discussions and comments, since last presentation
Implementations drive the identification mode of low latency traffic:
  Some implementations can handle extra queues (> 8 TIDs) : SCSID-based identification (fairest)
  Other implementations rely only on 8 TIDs (note possibly multiple flows are combined in a TID) :
    Case 1: SN assignment performed on MAC arrival (no intra-TID prioritization is possible, Head-of-line blocking exists) : TID-based identification, as a sort of “best-effort LL traffic prioritization”
    Case 2: SN assignment performed upon transmission (intra-TID/per-SCS prioritization is performed prior SN, without HOL issue) : both TID-based or SCSID-based identifications can be used (of course later is more explicit and efficient, especially when 2 SCS belong to same TID class)
Concept of prioritization is now adopted for LL traffic delivery (21-1802r9)
  §37.7.5 Traffic delivery :
    “In a trigger-enabled restricted TWT SP, when scheduling the transmission of Trigger frames, the r-TWT scheduling AP shall first trigger member r-TWT scheduled STAs to facilitate them to first deliver their QoS Data frames of r-TWT UL TID(s), if any.”
  TID-based implementations:
    As each r-TWT scheduled STA selects a TID by its own, there is chance that all TIDs become r-TWT TIDs (that means all TIDs are listed in r-TWT IE for Broadcast TWT, and STA doesn’t know which considered)*.
    Therefore r-TWT scheduled STA must know which TID is requested with regards to itself
  SCSID-based implementations :
    Support of SCSID in rTWT and TF
    As each r-TWT scheduled STAs selects an SCSID value by its own (generally starting from 0), SCSID shall be triggered with regards to a specific STA (in TF and r-TWT IE).
Notes: *Agreed during presentation of 1802r9, MAC session 2022_01_21

## Slide 8: Example formats to support TID and SCSID
Trigger Frame is updated to trigger an SCS stream (through TID/SCSID):
  Applicable only to EHT STAs,
  “Trigger Dependent User Info” Format compatible with HE format
    B5 set to ‘1’ indicates new EHT Trigger Dependent User Info field variant
    B2 (Trigger Dependent Type subfield) identifies the encoding of the EHT Trigger Dependent User Info field variant:
      Value 0: SCSID/TID subfields (part 1 and part 2) represent a TID value
      Value 1: SCSID/TID subfields (part 1 and part 2) represent an SCSID value
802.11ax format when B5 is Reserved (value 0)
802.11be format when B5 takes value 1
MPDU MU Spacing factor
2
Bits:
SCSID/TID
part 1
2
Presence of EHT format
1
SCSID/TID
part 2
2
B0 B1
B2
B5
B6 B7
B3 B4
Trigger Dependent Type
1

## Slide 9
TWT IE can be adapted to identify precisely SCS stream per STA:
  Applicable only to EHT STAs,
  In order to provide precise identification of low latency streams per station in Broadcast TWT SP, individual identifications (either TID/SCSID-based) are supported per each scheduled STA
    “Individual ID Info” is mutually exclusive against TID bitmaps
  Possible location may be inside ‘Restricted TWT Traffic Info’ field
Request Type
2
Octets:
Target Wake Time
2
Nominal Minimum TWT Wake Duration
1
TWT Wake Interval Mantissa
2
Broadcast TWT Info
1
Restricted TWT Traffic Info
0 or 3
B0
B1
B3 B7
B2
DL TID Bitmap Valid
1
Bits:
UL TID Bitmap Valid
1
Individual ID Valid
1
Reserved
5
Traffic Info Control
1
Octets:
Restricted TWT DL TID Bitmap
1
Restricted TWT UL TID Bitmap
1
Individual ID Info
variable
Figure 9-689b—Restricted TWT Traffic Info field format
Figure 9-689c—Traffic Info Control field format
Number of SCSID tuples
1
Octets:
ID tuple #1
2
…
Variable
Bits:
B0 B11
AID12
12
TBD if 4 enough?
B13 B15
B16 B31
SCSID / TID
Reserved
1 3
Type
B12

## Slide 10: Summary
This contribution discussed about similar identification of latency sensitive streams, in TF and rTWT: both TID-based and SCSID-based.
Use of SCSID may be preferred by high-end STAs, because it is:
  More efficient, as SCSID finely identifies streams at AP and STA sides
  Transparent to HE devices,
  Fair, as only the identified LL stream is triggered (no other data in TID/AC queue takes advantage of this medium access)
Use of TID (instead of AC) is still possible:
  Simple, even less efficient than SCSID, for STAs not able to finely discriminate LL streams,
  Finer granularity, (e.g. in TF or BSR) as one AC contains 2 TIDs,
  Transparent to HE devices.

## Slide 11: Straw Poll #1
Do you support that 802.11be makes use of both TID and SCSID as individual identification inside TFs and rTWT elements for latency-sensitive traffics ?
  Note: result of the strawpoll aims to trigger the resolution of CIDs 6511/6521
Results: Y/N/A

## Slide 12: Straw Poll #2
Do you support that 802.11be support individual identification (stream identifier per r-TWT scheduled STA) inside rTWT elements for latency-sensitive traffics ?
Results: Y/N/A

## Slide 13: Reference
[1]. Draft P802.11be_D1.1
[2]. CR for Low Latency BSR: https://mentor.ieee.org/802.11/dcn/21/11-21-1577-00-00be-cr-for-low-latency-bsr.pptx