## Slide 1: Measurement setup termination
Date: 18-Oct-21
Authors:

## Slide 2: Abstract
A proposal on the measurement setup termination

## Slide 3: General
A measurement setup can represent the parameters of a specific application(s). Attributes/parameters that belong to the application(s) may remain unchanged for a certain period
The Measurement setup ID identifies the attributes/parameters agreed upon between the initiator and one or more responders
The Measurement setup is associated with the Measurement instances
Once established, the Measurement setup consumes the resources of the initiator and the responder

## Slide 4: Motivation
The Initiator and the Responder may want to terminate the Measurement setup due to several reasons, for example:
  Application is terminated, and there is no more need for a specific set of attributes/parameters
  The initiator or the responder are not able to keep the agreed attributes/parameters of the specific Measurement setup ID

## Slide 5: Basic rules
The device keeps active the established Measurement setup identified with the Measurement setup ID until it is terminated
Termination of the Measurement setup identified with the Measurement setup ID by one device does not impact the activity of this Measurement setup of another device(s)/session(s)
Termination of the Measurement setup identified with one Measurement setup ID does not impact the device/session activity of another Measurement setup with a different Measurement setup ID
The Initiator and the Responder may initiate termination of the Measurement setup
A handshake between the Initiator and the Responder and/or expiration of the predefined inactivity time may terminate the Measurement setup (detailed protocol TBD)

## Slide 6: Basic rules (cont.)
The Initiator and the Responder may release the resources they allocated to store the setup after the termination of the Measurement setup
The Initiator should not indicate the Measurement setup ID of the terminated Measurement setup in the measurement instances it initiates
The Initiator may ignore the pending report(s) indicated to belong to the terminated Measurement setup
The Responder should not respond to request/poll/trigger that all Measurement setups it indicates are terminated
The Responder should not transmit the report that indicates the terminated Measurement setup

## Slide 7: Example of the Measurement setup termination

## Slide 8: Example of the Measurement setup termination (cont.)
The example illustrates that:
The Measurement setup ID=1 termination applies to the device (session) (MAC ADDR=A, AID=1) indicated in the termination; see the Measurement setup termination
The Measurement setup ID=1 cannot be used with the device (session) MAC ADDR=A, AID=1 after the termination; see the Measurement instance ID=4
The Measurement setup ID=1 after termination with the device (session) MAC ADDR=A, AID=1 is still applicable to another device (session) MAC ADDR=B, UID=2, see the Measurement instance ID=4
The Measurement setup ID=2 is applicable for the device (session) MAC ADDR=A, AID=1 after the termination of the Measurement setup ID=1, see the Measurement instance ID=2, Measurement setup ID=2

## Slide 9: SP1
Do you agree to append to the SFD the rules in slides 5 and 6?