## Slide 1: BW signaling for control frames
Date: 10/20/2021
Authors:

## Slide 2: Introduction
11ac introduced BW signaling for Control frames sent in non-HT duplicate format
  Purpose: provide explicit BW information that can not be carried natively in non-HT duplicate, such as:
    Occupied BW
    Support of dynamic BW RTS/CTS negotiation
  To pre-11ac devices, the frames still looks like “ordinary” non-HT
For compatibility with legacy devices, the signaling is somewhat “unconventional”:
  Repurposing some bits of the PHY scrambler seed
  Indicate presence of signaling through the Individual/Group bit of the TA (“bandwidth signaling TA”)

## Slide 3: Introduction (2)
Non-HT duplicate format is preferred for Control Frames, even for 11be
  Common denominator to all generations of Wi-Fi
  Duplication makes information available to all devices, even for partially overlapping OBSS or OBSS with different primaries

## Slide 4: BW signaling in 11be
11be needs extra BW information to be conveyed
  New bandwidth (320 MHz)
  Large set of possible puncturing patterns
For “R1”:
  Only static puncturing considered
    No need to include info on puncturing patterns in Control Frames
    Only need to accommodate signaling of new value (320 MHz)
  Existing BW signaling mechanism extended by repurposing one bit of the SERVICE Field
For “R2”:
  No final decisions yet, but dynamic puncturing is in scope

## Slide 5: Discussion for R2
We’re reaching the limit with what can be signaled using the current mechanism
  Scrambler seed is intended to be a random value, we can’t (or shouldn’t) borrow any more bits from this seed
  The number of puncturing patterns is pushing the limits of what is available in the SERVICE field
    Especially when considering possible error protection [1]
  There will be generations of 802.11 after 802.11be that may require further extensions
We need a robust, future-proof mechanism for BW signaling in non-HT duplicate
  Possibly even including information other than BW

## Slide 6: Requirements
A BW signaling mechanism should be:
  Fully compatible with non-HT duplicate
  Transparent to legacy devices
    i.e., everything up to and including 11be R1
  Able to carry all information required in R2
  Future-proof for further additions (R2 or beyond)

## Slide 7: Control Wrapper Frame
Existing Control frame subtype (Subtype value 0111)
Provides a straightforward way to carry any other Control Frame with additional information
Currently used to convey HT Control information in addition to the “native” Control frame information
Extra information can be conveyed between devices that support Control Wrapper Frame
“Legacy” devices can still extract Duration and Address field
  Devices that support HT Control field can fully process

## Slide 8: Control Wrapper Frame - Details
Control Wrapper Frame carries all original Control Frame information, expect Duration and FCS
Extra Frame Control is added
Payload carries both the “wrapped frame” and HT Control

## Slide 9: Advantages
Control Wrapper frame satisfies the requirements:
  Uses non-HT/non-HT duplicate
  Compatible with legacy devices
    Duration, Address, …
  Flexible payload can carry all required information, and more
  Based on existing proven method defined in the standard
    Introduced in 802.11-2012 (per Amendment 802.11n-2009)

## Slide 10: Proposed mechanism
For BW signaling in R2 and beyond, either:
  Define new Control Frame subtype
    “BW signaling Control Wrapper”
    Similar to Control Wrapper but with BW info instead of HT Control
  Keep existing Control Wrapper Subtype and define new HT Control value that carries BW information
Content and format of extra information TBD
  Even one byte would provide plenty of information
  Doesn’t have to be limited to BW information
    E.g., Color?

## Slide 11: Discussion
Support for Control Wrapper frame is already mandatory for STAs that support the HT Control field, so processing does not add new requirements for EHT
Only needed for “R2” signaling
  No impact on existing designs or planned R1 designs
Control Wrapper adds negligible overhead
  To be expected when carrying extra information
  Only 2 bytes of “real” overhead (i.e., unrelated to the new information)

## Slide 12: Conclusion
A Control Wrapper frame (or modified Control Wrapper) can be used to signal BW information in non-HT duplicate format
Mechanism is flexible, backwards compatible and reuses existing design

## Slide 13: Questions?

## Slide 14: References
[1] BandwidthIndicationInRtsCtsIn320MHzPpdu AndPuncturedPreambles, Brian Hart, 11-21/0427r4