## Slide 1
TID-to-Link mapping in eMLSR
Date: 2021-10-30
Authors:

## Slide 2: Introduction
eMLSR STA MLD can communicate with AP MLD using the links negotiated with EML OMN
Depending on the TID-to-Link mapping, there might be a case where AP MLD can not transmit DATA with a certain TID using the negotiated link
  Since TID-to-Link mapping is a separate procedure, TID can be mapped to a link which is not negotiated with EML OMN
TID-to-Link mapping considering EML OMN and eMLSR link management are discussed

## Slide 3: Recap: eMLSR EML OMN
Links to use for eMLSR can be negotiated with EML OMN
Since TID-to-Link mapping is a separate procedure, a certain TID can be mapped to a link not used for eMLSR

## Slide 4: eMLSR TID-to-Link mapping
Option 1) EML OMN may include TID-to-Link mapping element
  During EML OMN negotiation, TID-to-Link remapping can be negotiated.
Option 2) TID-to-Link mapping for eMLSR can be default mapping
  In order to avoid eMLSR link to TID mismatch, TID-to-Link mapping can be automatically switched to default mapping (all TID to all link mapping) after EML OMN negotiation

## Slide 5: Conclusion
eMLSR links can be negotiated with EML OMN.
Since TID-to-Link mapping is a separate procedure, mismatch on eMLSR link with TID-to-Link mapping can happen.
During EML OMN negotiation, TID-to-Link remapping can be performed.
  Default TID-to-Link mapping
  TID-to-Link mapping element in EML OMN
In this presentation, considerations on TID-to-Link mapping in eMLSR were discussed.

## Slide 6: Reference
[1] Draft P802.11be D1.2