## Slide 1
Reverse Direction in Triggered TXOP Sharing
Date: 2021-10-30
Authors:

## Slide 2: Introduction
Triggered TXOP sharing procedure is defined in the Draft 1.2 [1].
Within an established TXOP, two communicating nodes can efficiently perform bidirectional communication utilizing the reverse direction scheme defined in the base spec.
Reverse direction can be applied to the triggered TXOP sharing procedure.
In this contribution, reverse direction scheme in the triggered TXO sharing is discussed.

## Slide 3: Recap: Reverse Direction
Reverse direction initiator (TXOP holder) can share its TXOP with a PPDU recipient (reverse direction responder).
  RDG/ MorePPDU
    RD initiator uses this bit as RDG: indicates whether reverse direction is granted or not
    RD responder uses this bit as MorePPDU: indicates whether there is a PPDU to transmit in reverse direction
  AC constraint can indicate whether same AC or any AC is allowed in the reverse direction transmission

## Slide 4: RD in sharing mode 1
The TXOP holder of the shared TXOP can be STA2.
  STA2 can be a RD initiator and AP can be a RD responder.

## Slide 5: RD in sharing mode 2
The TXOP holder of the shared TXOP can be STA2.
  STA2 can be a RD initiator and STA3(P2P recipient) can be a RD responder.
AP may include STA3 in MU-RTS to allow STA2 and STA3 to use RD

## Slide 6: Conclusion
Reverse Direction can be applied to the triggered TXOP sharing.
  STA can be the TXOP holder of the shared TXOP
RD in the triggered TXOP sharing.
  Sharing mode 1:
    STA: RD initiator, AP: RD responder
  Sharing mode 2:
    STA: RD initiator, other P2P STA: RD responder
In this presentation, RD in the triggered TXOP was discussed.

## Slide 7: Reference
[1] Draft P802.11be D1.2