## Slide 1: Support for Sensing Measurement Instances
Date: 2021-11-01
Authors:

## Slide 2: Background
“CSI (that is, the channel measured during the training symbols of a received PPDU) is a type of sensing measurement result for sub-7 GHz WLAN sensing” (Clause 8 of TGbf SFD, DCN 21-0504r3)
For a given pair of sensing initiator and sensing responder, two types of sensing measurement instances have been discussed in 11bf:
  Measurement (e.g., CSI or its variant) feedback is required
  Measurement feedback is not required
For most CSI-based sensing use cases, either one of these two types of sensing measurement (i.e., measurement in two opposite directions) is adequate.
The contribution addresses the support for these two types of sensing measurement instances.

## Slide 3: Sensing Measurement Requiring Feedback
The sensing initiator is the sensing transmitter, and the sensing responder is the sensing receiver.
  The NDPA sounding phase defined in Clause 7.1.4.2.2 of SFD is shown in the figure below as an example.
The sensing responder receives NDP and estimates and feedbacks full CSI matrix or its variant.
  CSI feedback not supported by 11ac/11ax/11be
  Wider bandwidth  higher sensing resolution but higher over-the-air overhead
  Quantization and subcarrier grouping needed to reduce overhead  degradation of CSI
  Since estimation of CSI is implantation specific, it is difficult for the initiator to control the quality and fidelity of CSI estimates from different responder/receiver implementations.
I2R NDP
AP (initiator)
STA (responder)
Measurement Feedback
SIFS
Sensing NDPA
SIFS
SIFS
CTS-to-self
Poll Frame
SIFS

## Slide 4: Sensing Measurement without Feedback
The sensing initiator is the sensing receiver, and the sensing responder is the sensing transmitter.
  The trigger frame sounding phase defined in Clause 7.1.4.2.3 of SFD is shown in the figure below as an example.
The sensing initiator receives NDP and estimates CSI.
  Measurement feedback not needed  higher efficiency and less complexity
  No over-the-air overhead  maintain wider bandwidth for higher sensing resolution
  Finer quantization  no degradation of CSI
  Easy to control the quality and fidelity of CSI estimated from the same receiver implementation.
Trigger Frame
AP (initiator)
STA (responder)
CTS-to-self
SIFS
Poll Frame
SIFS
R2I NDP
SIFS

## Slide 5: Sensing by Proxy
Recently presented in DCN 1684 and DCN 1692
The sensing initiator is a client (i.e., a non-AP STA), which is neither the sensing transmitter nor the sensing receiver.
Requested by the sensing initiator, the AP obtains sensing measurements and reports them to the requesting client.
  The AP may serve as the sensing receiver to estimate CSI.
  Reporting raw CSI to the requesting client leads to the tradeoff between CSI precision and overhead.

## Slide 6: Summary
Proposal:
  Mandatory support: sensing measurement does not require measurement report
  Optional support: sensing measurement requires measurement report
A single mandatory mode for sensing measurement will lead to simplified hardware design and hence lower the bar of implementation.
  Shorten the time to market
  Allow 11bf to progress more easily in WFA
  Facilitate the industry to adopt 11bf faster

## Slide 7: SP
Do you agree with the following?
  Support for sub-7 GHz sensing measurement which does not require measurement report is mandatory.
  Support for sub-7 GHz sensing measurement which requires measurement report is optional.