## Slide 1: (E)DMG multi/bistatic radar
Date: 2021-06-10
Authors:

## Slide 2: Abstract
The following document discusses a general proposal for the PHY and lower MAC of a bistatic/multi-static radar/sensing in DMG and EDMG. It assumes a single Tx/Rx chain per STA.

## Slide 3: Agenda
In 11-21-1431 we presented a framework for DMG/EDMG Bi-static/multi-static sensing
In this presentation we lay out the general structure for this type of sensing and go into some details.
As a reminder
  we propose that bi-static sensing basic building block will be based on existing BRP frames
  we propose that for multi-static sensing a modified frame structure will be used.

## Slide 4: Reminder – E/DMG BRP request/response
BRP – Beam Refinement Protocol
  Used for beamforming training in DMG/EDMG
The initiator uses a BRP frame to send a request.
  If the request is for transmit training, it appends a TRN field to the PPDU. The response frame will include a best sector index or some type of CSI (channel measurement feedback)
  If the request if for receive training, the response includes a TRN field that the initiator can use for receive beamforming training.
  in EDMG, a TRN field can be used for both Tx and Rx training – the initiator trains its TX antennas and the receiver its RX antennas.

## Slide 5: Reminder – EDMG TRN field
The TRN field is composed of TRN subfields
  each subfield is composed of a set of Golay sequences that can be used for accurate channel estimation (6 sequences, 2 of them are used a cyclic prefix/suffix)
The TRN field can be a TRN-T/TRN-R/TRN-T-R
  in a TRN-R field, all the subfields are transmitted in the same direction as the data part of the PPDU (used for RX training)
  in a TRN-T field, the transmitter may change direction in each subfield. Periodically, a set of subfields are transmitted using the same antenna setting used to transmit the data part of the PPDU, to enable frequency/timing tracking
  in TRN-T-R field, the transmitter transmit a group of subfields in one directions then another group in another direction and so on. Each of these groups is large enough to allow receiver training

## Slide 6: Bi-Static sensing – Tx initiator – Measurement Instance
Existing EDMG BRP frame with TRN-R-T field (can be also TRN-T or TRN-R field)
  The transmitter may transmit the TRN subfields in many directions and the receiver may receive in many directions
  The preamble and data fields, and periodically repeating fields within the TRN field are transmitted in the direction of the RX STA
feedback is included in the BRP response.
  Feedback may be delayed or aggregated when doppler computations are needed.

## Slide 7: Bi-Static Sensing – Receiver Initiator
BRP frame requests responder to send a PPDU with a TRN field
  change from existing structure
The TX STA may switch TX direction while transmitting the TRN field and the RX STA may switch RX directions while receiving the TRN field
  synchronization fields provided by periodic TNR subfields using the same antenna pattern as the one used for the preamble and data fields.
  The PPDU may be TRN-R-T, TRN-R or TRN-T.

## Slide 8: Capabilities Need to be exchanged
The initiating and responding STAs need to exchange capabilities
  sequence length supported (of the Golay Sequences in the TRN field)
  number of directions in Tx and Rx
  Feedback capabilities
  Phased Array Antenna control sets.
  Beam sets in which every beam has direction, gain, and beam width.

## Slide 9: Measurement parameters needs to be exchanged
The Initiator and responder need to exchange the following parameter
  number of exchanges in a burst – may be needed for doppler estimation
  set of beam directions in TX
  set of beam directions in RX
  beamforming TRN field information such as TRN-P, TRN-M, TRN-M
  location and orientation of each of the STAs
    coordinates can be local or earth coordinates
    relative locations orientation may be estimated using TGaz based exchanges or available from management layer
  Scheduling
    how many measurements are needed.

## Slide 10: Generic View of a sensing/radar session
Based on the procedure already in the SFD and the 11az procedure
Terminations not shown

## Slide 11: Multi-Static Sensing Transmit Initiator
Meas. Setup/Trigger assign sync index to STA, indicate when sense PPDU starts.
Sense PPDU contains a sync field for all STAs except STA1
  the sync field is used to provide timing and frequency offset locking quality similar to that achieved with the preamble.
  the sync field is STA specific.
Feedback is polled
  Feedback may be delayed or aggregated (per STA).
  Feedback may indicate failure (e.g., of acquiring the sync)

## Slide 12: Straw Poll 1
Do you agree to add to the SFD the following text:
EDMG transmitter initiator bi-static sensing is based on a BRP request in a BRP-RX/TX, BRP-TX, BRP-RX PPDU and the BRP response
Feedback for the measurement is carried in the BRP response
  Feedback may be delayed
  Feedback may be aggregated (single feedback for some measurements, to facilitate doppler measurement)

## Slide 13: Strawpoll 2
Do you agree to add to the SFD the following text:
EDMG receiver initiator bi-static sensing is based on a BRP request frame that includes a request for the responder to transmit a BRP-RX/TX, BRP-TX, BRP-RX PPDU.

## Slide 14: Strawpoll 3
Do you agree to add to the SFD the following text:
EDMG Bi/multi-static sensing capability set will include:
  sequence length supported (of the Golay Sequences in the TRN field)
  number of directions in Tx and Rx
  Feedback capabilities
  Beam sets in which every beam has direction, gain, and beam width.

## Slide 15: Strawpoll 4
Do you agree to add to the SFD the following text:
In an EMDG Bi/Multi-static measurement setup exchange the following parameters exchanged:
  number of exchanges in a burst – may be needed for doppler estimation
  set of beam directions in TX
  set of beam directions in RX
  beamforming TRN field information such as TRN-P, TRN-M, TRN-N
  location and orientation of each of the STAs
    coordinates can be local or earth coordinates
    relative locations orientation may be estimated using TGaz based exchanges or available from management layer
  Scheduling

## Slide 16: Strawpoll 5
Do you agree to add to the SFD the following text:
A multi-static EDMG sensing measurement instance has the following parts:
  A measurement setup/trigger part in which STA index is assigned to each responding STA. The responding STA responds with an ACK
  A multi-static EDMG sensing PPDU addressed to responding STA1 in which there are sync fields per each of the other STAs. Each sync field is transmitted in the direction of the other STAs. A TRN field is part of the PPDU
  A feedback part in which the initiator polls each responding STA for feedback.

## Slide 17: References
11-21-1431-00-00bf-DMG-bistatic-radar-PHY-and-Low-MAC