## Slide 1: Measurement setup frame formats
Date: 2021-11-09
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that an optional negotiation process in the sensing measurement setup is defined. [1]
This contribution discusses more about the detail of measurement setup frame formats.

## Slide 3: Recap-measurement setup
Measurement setup in SFD:
An optional negotiation process in the sensing measurement setup is defined that allows for a sensing initiator and a sensing responder to exchange and agree on operational attributes associated with a sensing measurement instance.
The operational attributes may include initiator’s and responder’s roles, measurement report types, and other operational parameters.
The type of measurement result reported in a WLAN sensing procedure shall be decided by its initiator.
Trigger-based (TB) sensing measurement setup – TBD.
Non-TB sensing measurement setup – TBD.
Note: according to “Figure 1: WLAN sensing procedure (example)” in SFD, we assume the negotiation is pairwised conversation.

## Slide 4: Proposal-Measurement Setup frames
Propose a new subtype of Public Action frame: Sensing Public Action frame. It may be a protected frame if RSNA is established.
  Consider that we may support sensing with unassociated-STAs, Public Action frame is the best choice. (Note: 11az also use Public Action frames)
Propose to define all possible sensing action frames using the same Public Action field value (e.g., 51), and have to a Sensing Subtype field to differentiate them.
  Reserve more Public Action field values for future amendment specs.
Detailed parameters are contained in frame dependent fields and elements.

## Slide 5: Proposal-Sensing Subtype field
Sensing Subtype field, e.g:
Sensing Subtype field value | Description
<ANA> | Sensing Measurement Setup Request
<ANA> | Sensing Measurement Setup Response
<ANA> | Sensing Measurement Setup Termination
<ANA> | Sensing Measurement Report (Action No Ack)
Other Sensing Subtypes are TBD

## Slide 6: Proposal-Measurement Setup Request
Frame dependent fields and elements for Sensing Measurement Setup Request:
  Setup Command field: Demand(0)/Suggest(1). (size TBD)
  Measurement Info element: operational attributes for the Responder
    Measurement Setup ID: idendify the operational attributes. (size TBD)
    Initiator AID/UID: Measurement Setup ID may not unique among different Inititiators.
    Report Type: type of measurement result. (size TBD)
    Receiver: the Resopnder will be Receiver or not
    Transmitter: the Resopnder will be Transmiter or not
    Enable Threshold: using threshold or not
    Threshold Value/Reserved: reserved if not using threshold. (size TBD)
    Other fields and/or subelements are TBD.

## Slide 7: Proposal-Measurement Setup Response
Frame dependent fields and elements for Sensing Measurement Setup Response:
  Setup Command field: Accept(2)/Alternate(3)/Reject(4). (size TBD)
  Reason Code field: exists when Setup Command field is Reject. (size TBD)
  Alternate Attributes: exists when Setup Command field value indicates Alternate. (size TBD)

## Slide 8: Proposal-Measurement Setup Termination
Frame dependent fields and elements for Sensing Measurement Setup Termination:
  Reason Code field: reason code indicating why the STA initiates this termination. (size TBD)
  Measurement Setup ID: ID of the measurement setup to be terminated. (size TBD)

## Slide 9: SP 1
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Public Action frame, and the format of this frame is shown in the figure of slide 4, including:
    The Sensing Subtypes includes: Sensing Measurement Setup Request, Sensing Measurement Setup Response, Sensing Measurement Setup Termination, and Sensing Measurement Report.
    Other Sensing Subtypes are TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 10: SP 2
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Measurement Setup Request frame, and the format of this frame is shown in the figure of slide 6, including:
    Measurement Info element: includes operational attributes for this measurement setup.
      Measurement Setup ID field : idendify this measurement setup. (size TBD)
      Initiator AID/UID field: idendify the Initiator.
      Report Type field: type of measurement result. (size TBD)
      Receiver field: the Resopnder will be Receiver or not
      Transmitter field: the Resopnder will be Transmiter or not
      Enable Threshold field: using threshold or not
      Threshold Value/Reserved field: reserved if not using threshold. (size TBD)
      Other fields and/or subelements are TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 11: SP 3
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Measurement Setup Response frame, and the format of this frame is shown in the figure of slide 7, including:
    Reason Code field: indicates reason code(s) for rejecting the request. (size TBD)
  Y/N/A
Chaoming Luo (OPPO)

## Slide 12: SP 4
Do you agree to add the following into 11bf SFD ?
  The Sensing Measurement Setup Request frame and Sensing Measurement Setup Response frame shall include a Setup Command field (size TBD), as following:
    Demand: indicates demanded operational attributes in Measurement Info element of the request frame.
    Suggest: indicates suggested operational attributes in Measurement Info element of the request frame.
    Accept: indicates the Responder accepts the request.
    Reject: indicates the Responder rejects the request.
    Alternate: indicates the Responder suggests alternate operational attributes in Alternate Attributes field of the response frame.
  Sensing Measurement Setup Response frame may include a Alternate Attributes field (size TBD), which includes alternate operational attributes, exists when the Setup Command field value indicates Alternate.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 13: SP 5
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Measurement Setup Termination frame, and the format of this frame is shown in the figure of slide 8, including:
    Reason Code field: reason code indicating why the STA initiates this termination. (size TBD)
    Measurement Setup ID: ID of the measurement setup to be terminated. (size TBD)
  Y/N/A
Chaoming Luo (OPPO)

## Slide 14: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
Chaoming Luo (OPPO)