## Slide 1: Measurement setup frame formats
Date: 2021-11-09
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that an optional negotiation process in the sensing measurement setup is defined. [1]
This contribution discusses more about the detail of measurement setup frame formats.

## Slide 3: Recap: measurement setup
Measurement setup in SFD:
An optional negotiation process in the sensing measurement setup is defined that allows for a sensing initiator and a sensing responder to exchange and agree on operational attributes associated with a sensing measurement instance.
The operational attributes may include initiator’s and responder’s roles, measurement report types, and other operational parameters.
The type of measurement result reported in a WLAN sensing procedure shall be decided by its initiator.
Trigger-based (TB) sensing measurement setup – TBD.
Non-TB sensing measurement setup – TBD.
Note: according to “Figure 1: WLAN sensing procedure (example)” in SFD, we assume the negotiation is pairwised conversation.

## Slide 4: Discussion: procedure
What are the possible sensing measurement setup procedures?
  Option 1 (unified sequence): A sequence of a Request and a Response frame.
  Option 2 (mixed sequence): Either a sequence including a Request and a Response frame, or a sequence including a Request and a Response and a Confirmation frame.

## Slide 5: Discussion: option 1
It’s pretty straightforward that a sensing measurement setup procedure as following could handle the most common cases.
If the Responder rejects the proposed operational attributes, the Initiator may request again as shown in case 2 with modified operational attributes based on the rejection reason of the previous response.
case 1: Responder accepts the attributes at the first shot.
case 2: Responder rejects the attributes at the first shot but accepts at the second.

## Slide 6: Discussion: option 1 (cont.)
However, a Responder may provide more information for preferred operational attributes, to assist the Initiator to make a successful setup.
  Note: the setup is actually fails when using the Measurement Setup Response with Alternate attributes, which is similar as TWT setup exchange in 11ax.
    Alternate means preferred attributes but also willing to accept other attributes.
    Dictate means only willing to accept the proposed attributes and any other will be rejected.
  Need a second measurement setup exchange in order to succeed. – unified procedure with possible overhead.
case 3.1: Responder proposes different attributes at the first shot but accepts or rejects at the second.

## Slide 7: Discussion: option 2
So, should we go with the same way as TWT setup exchange in 11ax? A possible options 2 is:
  For case 1 and 2, it’s same as option 1.
  For case 3, a Measurement Setup Confirmation frame could be considered to reduce overhead. --a little bit more complex procedure reducing overhead of one frame.
case 3.2: Responder proposes different attributes and Initiator confirms to accept or reject Responder’s proposal.

## Slide 8: Proposal: Measurement Setup frames
Propose a new subtype of Public Action frame: Sensing Public Action frame. It may be a protected frame if RSNA is established.
  Consider that we may support sensing with unassociated-STAs, Public Action frame is the best choice. (Note: 11az also use Public Action frames)
Propose to define all possible sensing action frames using the same Public Action field value (e.g., 51), and have to a Sensing Subtype field to differentiate them.
  Reserve more Public Action field values for future amendment specs.
Detailed parameters are contained in frame dependent fields and elements.

## Slide 9: Proposal: Sensing Subtype field
Sensing Subtype field, e.g:
Sensing Subtype field value | Description
<ANA> | Sensing Measurement Setup Request
<ANA> | Sensing Measurement Setup Response
<ANA> | Sensing Measurement Setup Termination
<ANA> | Sensing Measurement Report (Action No Ack)
Sensing Measurement Setup Confirmation depends on whether we choose option 2
Other Sensing Subtypes are TBD

## Slide 10: Proposal: Measurement Setup Request
Frame dependent fields and elements for Sensing Measurement Setup Request:
  Setup Command field: Demand(0)/Suggest(1). (size TBD)
  Measurement Info element: operational attributes for the Responder
    Measurement Setup ID: idendify the operational attributes. (size TBD)
    Initiator AID/UID: Measurement Setup ID may not unique among different Inititiators.
    Report Type: type of measurement result. (size TBD)
    Receiver: the Resopnder will be Receiver or not
    Transmitter: the Resopnder will be Transmiter or not
    Enable Threshold: using threshold or not
    Threshold Value/Reserved: reserved if not using threshold. (size TBD)
    Other fields and/or subelements are TBD.

## Slide 11: Proposal: Measurement Setup Response
Frame dependent fields and elements for Sensing Measurement Setup Response:
  Setup Command field: Accept(2)/ Reject(3)/Alternate(4). (size TBD)
  Reason Code field: exists when Setup Command field is Reject. (size TBD)
  Alternate Attributes: exists when Setup Command field value indicates Alternate. (size TBD)

## Slide 12: Proposal: Measurement Setup Confirmation
Frame dependent fields and elements for Sensing Measurement Setup Confirmation:
  Setup Command field: Accept(2)/ Reject(3). (size TBD)
  Reason Code field: exists when Setup Command field is Reject. (size TBD)

## Slide 13: Proposal: Measurement Setup Termination
Frame dependent fields and elements for Sensing Measurement Setup Termination:
  Reason Code field: reason code indicating why the STA initiates this termination. (size TBD)
  Measurement Setup ID: ID of the measurement setup to be terminated. (size TBD)

## Slide 14: SP 1
Which option do you prefer to design the sensing measurement setup procedure?
  Option 1 (unified sequence): A sequence of a Request and a Response frame.
  Option 2 (mixed sequence): Either a sequence including a Request and a Response frame , or a sequence including a Request and a Response and a Confirmation frame.
  Abs
  Y/N/A
Chaoming Luo (OPPO)

## Slide 15: SP 2a
Do you agree to add the following into 11bf SFD ?
  A sensing measurement setup procedure is defined in which:
    An Initiator sends a Sensing Measurement Setup Request frame to a Responder that indicates a request to perform WLAN sensing procedure(s) with the operational attributes requested within the frame.
    A Responder that receives a Sensing Measurement Setup Request frame shall respond with a Sensing Measurement Setup Response frame to accept or reject the request.
    A Responder may respond with alternate operational attributes in the Sensing Measurement Setup Response frame which indicates to reject the request.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 16: SP 2b
Do you agree to add the following into 11bf SFD ?
  A sensing measurement setup procedure is defined in which:
    An Initiator sends a Sensing Measurement Setup Request frame to a Responder that indicates a request to perform WLAN sensing procedure(s) with the operational attributes requested within the frame.
    A Responder that receives a Sensing Measurement Setup Request frame shall respond with a Sensing Measurement Setup Response frame to accept or reject the request or propose alternate operational attributes.
    The Initiator shall send a Sensing Measurement Setup Confirmation frame to accept or reject the response which proposes alternate operational attributes.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 17: SP 3a
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Public Action frame, and the format of this frame is shown in the figure of slide 8, including:
    The Sensing Subtypes includes: Sensing Measurement Setup Request, Sensing Measurement Setup Response, Sensing Measurement Setup Termination, and Sensing Measurement Report.
    Other Sensing Subtypes are TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 18: SP 3b
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Public Action frame, and the format of this frame is shown in the figure of slide 8, including:
    The Sensing Subtypes includes: Sensing Measurement Setup Request, Sensing Measurement Setup Response, Sensing Measurement Setup Confirmation, Sensing Measurement Setup Termination, and Sensing Measurement Report.
    Other Sensing Subtypes are TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 19: SP 4
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Measurement Setup Request frame, and the format of this frame is shown in the figure of slide 10, including:
    Setup Command field (size TBD), as following:
      Demand: indicates demanded operational attributes in Measurement Info element of the request frame.
      Suggest: indicates suggested operational attributes in Measurement Info element of the request frame.
    Measurement Info element: includes operational attributes for this measurement setup.
      Measurement Setup ID field : idendify this measurement setup. (size TBD)
      Initiator AID/UID field: idendify the Initiator.
      Report Type field: type of measurement result. (size TBD)
      Receiver field: the Resopnder will be Receiver or not
      Transmitter field: the Resopnder will be Transmiter or not
      Enable Threshold field: using threshold or not
      Threshold Value/Reserved field: reserved if not using threshold. (size TBD)
      Other fields and/or subelements are TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 20: SP 5
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Measurement Setup Response frame, and the format of this frame is shown in the figure of slide 11, including:
    Setup Command field (size TBD), as following:
      Accept: indicates the Responder accepts the request.
      Reject: indicates the Responder rejects the request.
      Alternate: indicates the Responder suggests alternate operational attributes in Alternate Attributes field of the response frame.
    Reason Code field: indicates reason code(s) for rejecting the request. (size TBD)
    Alternate Attributes field (size TBD), which includes alternate operational attributes, exists when the Setup Command field value indicates Alternate.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 21: SP 6b
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Measurement Setup Confirmation frame, and the format of this frame is shown in the figure of slide 12, including:
    Setup Command field (size TBD), as following:
      Accept: indicates the Initiator accepts the alternate attributes in the previous response frame.
      Reject: indicates the Initiator rejects the alternate attributes in the previous response frame.
    Reason Code field: indicates reason code(s) for rejecting the response. (size TBD)
  Y/N/A
Chaoming Luo (OPPO)

## Slide 22: SP 7
Do you agree to add the following into 11bf SFD ?
  11bf shall define a Sensing Measurement Setup Termination frame, and the format of this frame is shown in the figure of slide 13, including:
    Reason Code field: reason code indicating why the STA initiates this termination. (size TBD)
    Measurement Setup ID: ID of the measurement setup to be terminated. (size TBD)
  Y/N/A
Chaoming Luo (OPPO)

## Slide 23: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
Chaoming Luo (OPPO)