## Slide 1: Measurement setup frame formats
Date: 2021-11-09
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that an optional negotiation process in the sensing measurement setup is defined. [1]
This contribution discusses more about the detail of measurement setup procedure and frame formats.

## Slide 3: Recap: measurement setup
Measurement setup in SFD:
An optional negotiation process in the sensing measurement setup is defined that allows for a sensing initiator and a sensing responder to exchange and agree on operational attributes associated with a sensing measurement instance.
The operational attributes may include initiator’s and responder’s roles, measurement report types, and other operational parameters.
The type of measurement result reported in a WLAN sensing procedure shall be decided by its initiator.
Trigger-based (TB) sensing measurement setup – TBD.
Non-TB sensing measurement setup – TBD.
Note: according to “Figure 1: WLAN sensing procedure (example)” in SFD, we assume the negotiation is pairwised conversation.

## Slide 4: Discussion: procedure
What are the possible sensing measurement setup procedures?
  Option 1 (unified sequence): A sequence of a Request and a Response frame.
  Option 2 (mixed sequence): Either a sequence including a Request and a Response frame, or a sequence including a Request and a Response and a Confirmation frame.
Proposal: use option 1 for sensing.

## Slide 5: Discussion: option 1
It’s pretty straightforward that a sensing measurement setup procedure as following could handle the most common cases.
If the Responder rejects the proposed operational attributes, the Initiator may request again as shown in case 2 with modified operational attributes based on the rejection reason of the previous response.
case 1: Responder accepts the attributes at the first shot.
case 2: Responder rejects the attributes at the first shot but accepts at the second.

## Slide 6: Discussion: option 1 (cont.)
However, a Responder may provide more information for preferred operational attributes, to assist the Initiator to make a successful setup.
  Note: the setup is actually fails when response with Alternate attributes, which is similar as TWT setup exchange.
    Alternate in TWT setup means preferred attributes but also willing to accept other attributes.
    Dictate in TWT setup means only willing to accept the proposed attributes and any other will be rejected. (Dictate is not so usefull in sensing, TBD)
  Need a second measurement setup exchange in order to succeed. – an unified procedure with little overhead.
    The measurement setup exchange is likely to proceed with little to no rejection as the initiator is likely to learn about the responder’s capability during the session setup and assign the parameters accordingly.
case 3.1: Responder responds with reject and proposes different attributes at the first shot, it probably accept at the second round, althouth it could reject again.

## Slide 7: Discussion: option 2
The possible options 2 may be:
  For case 1 and 2, it’s same as option 1.
  For case 3, a Measurement Setup Confirmation frame could be considered to reduce overhead. --a more complex procedure reducing little overhead of one frame.
    Note: the setup is actually fails when response with Alternate attributes, if there is no confirmation of accept.
case 3.2: Responder responds with reject and proposes different attributes, Initiator confirms to accept or reject Responder’s proposal.

## Slide 8: Proposal: Measurement Setup frames
Add new entries (e.g., 51, 52, …) in the “Table 9-438—Public Action field values” for for sensing related Public Action frames.
  These new frames may be used when management frame protection is diabled, or for low robust sensing use cases.
Add a new category (e.g., 38) in the “Table 9-79—Category values”, and a Sensing Action field differentiates between various protected sensing related frames.
  These new frames may be used for robust sensing use cases.
Detailed format is TBD.
Public Action frame:
Protected Sensing frame:

## Slide 9: Proposal: Measurement Setup Request
Frame dependent fields and elements for Sensing Measurement Setup Request:
  Sensing Operational Parameters element: operational attributes for the Responder.
Public Action:
Protected Sensing frame:

## Slide 10: Proposal: Measurement Setup Response
Frame dependent fields and elements for Sensing Measurement Setup Response:
  Setup Command field (size TBD): Accept(1)/ Reject(2)/Alternate(3)
  Reason Code field (size TBD): reason of reject, exists only when Setup Command field indicates Reject.
  Sensing Operational Parameters element: alternate operational attributes proposed by the Responder, exists only when Response Code field indicates Alternate.
Public Action:
Protected Sensing Action:

## Slide 11: Discussion: Sensing Operational Parameters element
Information in Sensing Operational Parameters element:
  Report Type: type of measurement result, e.g., CSI. (only in request frame)
  Measurement Setup ID: idendify the operational attributes.
    Initiator ID: may be needed, since Measurement Setup ID may not be unique among different Inititiators. (TBD) [3]
  Receiver: the Resopnder will be Receiver or not
  Transmitter: the Resopnder will be Transmiter or not
  Enable Threshold: using threshold or not (only in request frame)
  Threshold Value/Reserved: reserved if not using threshold. (only in request frame)
  Scheduling Info: scheuding information for TB instances. (TBD) (only in request frame)
    start time: scheduled start time of the first instance
    period: time interval between instances.
  Other information is TBD.

## Slide 12: SP 1
Do you agree to add the following into 11bf SFD ?
  A sensing measurement setup procedure consists of a request frame exchange initiated by the initiator followed by a response frame exchange initiated by the responder.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 13: SP 2
Do you agree to add the following into 11bf SFD ?
  In a sensing measurement setup procedure, if the sensing responder intends to reject the assigned operational parameters included in the sensing measurement setup request frame, it may provide its preferred operational parameters in the sensing measurement setup response frame.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 14: SP 3
Do you agree to add the following into 11bf SFD ?
  11bf shall define both public and protected sensing management frames, which include sensing measurement setup request/response, sensing measurement report, sensing measurement setup termination, and SBP request/response frames.
  Note: Other public and protected sensing management frames are TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 15: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
[2] 11-21-1735-01-00bf-procedure-of-sensing-measurement-setup
[3] 11-21-1941-00-00bf-discussion-on-measurement-setup-id-setting
Chaoming Luo (OPPO)

## Slide 16: SP 2b
Do you agree to add the following into 11bf SFD ?
  A sensing measurement setup procedure is defined in which:
    In a sensing measurement setup procedure, if the sensing responder intends to reject the assigned operational parameters included in the sensing measurement setup request frame, it may provide its preferred operational parameters in the sensing measurement setup response frame.
    The sensing initiator shall send a sensing measurement setup confirmation frame to accept or reject the alternate operational attributes proposed by the sensing responder in the previous response.
  Y/N/A
Chaoming Luo (OPPO)