## Slide 1: Address Block Assignment with P802.1CQ BARC
Date: 2021-11-09
Author:

## Slide 2: P802.1CQ Status [1]
IEEE SA Project Authorization (PAR) P802.1CQ
- Initiated: 2016-02-05; Extended 2020-06-03; Expires: 2022-12-31
Draft Standard for Local and Metropolitan Area Networks: Multicast and Local Address Assignment
In 802.1 Working Group, Time-Sensitive Networking (TSN) Task Group
  https://1.ieee802.org/tsn/802-1cq/
Current draft: P802.1CQ/D0.7
  reviewed in Task Group Ballot
  comment resolution completed in September
Awaiting editor’s implementation of new draft

## Slide 3: P802.1CQ PAR Details
Scope: This standard specifies protocols, procedures, and management objects for locally-unique assignment of 48-bit and 64-bit addresses in IEEE 802 networks. Peer-to-peer address claiming and address server capabilities are specified.
Need: Currently, global addresses are assigned to most IEEE 802 end station and bridge ports. Increasing use of virtual machines and Internet of Things (IoT) devices could exhaust the global address space. To provide a usable alternative to global addresses for such devices, this project will define a set of protocols that will allow ports to automatically obtain a locally-unique address in a range from a portion of the local address space. Multicast flows also need addresses to identify the flows. They will benefit from a set of protocols to distribute multicast addresses. Peer-to-peer address claiming and address server capabilities will be included to serve the needs of smaller (e.g., home) and larger (e.g., industrial plants and building control) networks.

## Slide 4: Multicast Address Assignment
In P802.1CQ, multicast addresses are assigned to end stations.
- In other scenarios, multicast addresses are assigned to protocols.
In some TSN networks, streams are addressed to multicast addresses assigned by the sender (the “talker”).
A peer-to-peer protocol (MAAP) for a talker to claim a multicast address range is specified in IEEE Std 1722 ("Transport Protocol for Time-Sensitive Applications in Bridged LANs").
P802.1CQ provides backward compatibility with MAAP.
  new functionality:
    address blocks
    Registrars (address servers)
    operation without a global address

## Slide 5: Power of Dynamic Software-Defined Addressing
Half of IEEE 802 addresses are global
  unique among all devices over an intended span of 100 years
  generally burned-in by the factory, so flat
Half of IEEE 802 addresses are local
  assignable dynamically
  vast quantity available, since uniqueness restriction limited to the LAN
  can be liberally assigned
  can be thoughtfully assigned to have addressing power
"Block Address Registration and Claiming” (BARC) protocol

## Slide 6: BARC assigns MAC Addresses in Blocks
An Address Block (AB) is a set of local BARC addresses.
An AB includes equal-sized and unicast and multicast contiguous sub-blocks.
No BARC address falls within more than one AB.
Registrable Address Block Identifier (RABI)
  identifies Registrable Address Block (RAB) with Registrable Addresses (RAs)
  RABIs are held in inventory of a Registrar
- may be assigned to Claimants
Claimable AB Address (CABA)
  identifies Claimable Address Blocks (CABs) with Claimable Addresses (CAs)
  claimable by a Claimant without using a Registrar
  CABA is a multicast MAC address, not in any AB, and used as a DA
An Address Block Designation (ABD) is a CABA or a RABI.
A large set of Temporary Unicast Addresses (TUAs) is specified
  useful for initial discovery by Claimant lacking a unicast address

## Slide 7: BARC MAC Address Structure

## Slide 8: CABA and CA, CAB Size 0-3

## Slide 9: BARC Claiming Process (not intended for WLAN)

## Slide 10: Registrar
Claimant need not be aware of Registrar when initiating a claim.
Registrar maintains an inventory of RABIs.
  a protocol specifies how Registrars acquire RABIs.
  set of RABs is disjoint from the set of CABs
– AB is either claimable (CAB) or registrable (RAB); not both
Registrar listens for all messages to a CABA.
Registrar can respond to a DISCOVER with an offer of a RABI in its inventory.
  The offer can also defend the DISCOVER’s CABA.
  Registrar confirms registration of request for offered RABI.
Pre-claim Inquiry lets Claimant reach Registrar or Advisor.
– Client can learn of Registrars and received Claim proposals.

## Slide 11: BARC Registrar Process (not intended for WLAN)

## Slide 12: potential use: Semantic Address Block Assignments

## Slide 13: Pre-association Address Block Assignment

## Slide 14: BARC over WLAN
BARC Claimant exchanges messages on the LAN for address block assignment
association is bound to one address
inefficient to associate, run BARC, and rebuild association
address block could be assigned with 802.11 pre-association communication
Current lines of thought are:
  Modify Local MAC Address Policy ANQP-element to include an address block assignment
  Develop within IEEE 802.1CQ a new protocol payload to be included in the Service Information Request/Response ANQP-elements
Assigned multicast addresses could be used for stream Das
How to use multiple unicast addresses assigned to STA?
  Multiple associations?
  Single association enabled to carry all assigned addresses?

## Slide 15: BARC Applications
General address assignment
  eliminates need for global addresses
    reducing consumption
    may simplify manufacturing
  maintains uniqueness within the LAN
  backward-compatible with IEEE 802 addressing and bridging
  could be useful to address privacy concerns in global addressing
  provides contiguous unicast and multicast blocks (identical but 1 bit)
Apply address blocks to structure semantic addresses
  addressing to reflect topology and hierarchy
    simplified forwarding
  add flow identification to address
    useful in forwarding and for other purposes
    e.g., to multiplex within a single end station
  alternative to completely random assignment; e.g., in WLAN
    dynamic assignment provides MAC address privacy
    protocol protects against duplication
    address blocks can code frames for location, flow, stream, etc.
  bridging of 64-bit addressing in a 48-bit bridged LAN

## Slide 16: References
[1] IEEE Standards Project P802.1CQ, “Multicast and local address assignment.” https://1.ieee802.org/tsn/802-1cq
[2] IEEE Standards Association, “IEEE Standard for Local and Metropolitan Area Networks: Overview and Architecture – Amendment 2: Local Medium Access Control (MAC) Address Usage,” IEEE Std 802c-2017 https://ieeexplore.ieee.org/document/8016709