## Slide 1: NSEP Priority Access Treatment Discussion
Date: 2021-11-12
Authors:
Name | Affiliation | Address | Email
Yonggang Fang Yongho Seok Frank Hsu James Yee | MediaTek |  | yonggang.fang@mediate.com
Subir Das John Wullert | PERATON LABS |  | <sdas@peratonlabs.com>

## Slide 2: Background NSEP EDCA Parameter Distribution in Current Specification
NSEP Priority Access is enabled at the MLD level
  When enabled, NSEP priority access is applied to all enabled links
AP transmits EDCA parameters to non-AP STA in NSEP Priority Access Enable Request and NSEP Priority Access Enable Response frames
  Note: the current 802.11 baseline supports a single set of EDCA parameters for a link
Shortcomings
  Current specification does not explicitly state how NSEP EDCA parameters should be applied to all enabled links
    Applying single set to all enabled links limits flexibility of AP MLD to adapt to differences between links (e.g., differences in capacity and/or load)
    If the set is applied only to link on which it is received, then there is currently no mechanism to communicate EDCA parameters for other enabled links
  In addition, current specification does not provide any means for APs affiliated with AP MLD to update EDCA parameters after NSEP priority access is enabled
    e.g., in response to change in networking environment

## Slide 3: Use Cases to Consider
Initial EDCA Parameter Distribution: Mechanism for AP MLD to transmit link-specific NSEP EDCA parameters
  To non-AP MLDs while enabling NSEP priority access
Update of EDCA parameters: Mechanism for AP MLD to transmit updated NSEP EDCA parameters
  In response to changing conditions of wireless media
  Distribution to all non-AP MLDs that have NSEP priority access enabled
Following slides compare options for these two cases

## Slide 4: Initial NSEP EDCA Parameter Distribution Option A: Default EDCA parameters for NSEP
  Procedures (Will require changes to D1.2)
    The NSEP enabled AP MLD will not include the NSEP EDCA parameter set in NSEP Priority Access Enable Request/Response for a setup link.
    When NSEP priority access is enabled, NSEP-enabled non-AP MLDs use the default EDCA parameter set for priority access on all setup links.
    When NSEP priority access is enabled for at least one non-AP MLD, the NSEP enabled APs affiliated with AP MLD announce degraded EDCA parameters in management frames (i.e. Beacon or Probe Response) to lower priority for all non-NSEP device.
  Discussion
    Advantages:
      Steps 2 and & step 3 are already specified in 11be D1.2
      No need to carry NSEP EDCA parameters in NSEP Priority Access Enable Request/Response frames
    Disadvantages:
      Limited flexibility: this approach makes updating NSEP EDCA parameters impossible:
        Cannot handle situations with congestion among multiple NSEP enabled non-AP MLDs, which could lead to extremely poor performance for NSEP devices.

## Slide 5: Initial NSEP EDCA Parameter Distribution: Option B: NSEP EDCA Parameters in Request/Response Frames
  Procedure (Will require changes to D1.2)
    Define an NSEP EDCA parameter set for each enabled link for the NSEP enabled non-AP MLDs associated with the NSEP enabled AP MLD for NSEP priority access.
    One AP affiliated with AP MLD transmits multiple NSEP EDCA parameter sets (one per enabled link) via NSEP Enable Request/Response action frame using one of two methods
      Define new element that contains multiple (Link ID, EDCA parameter) pairs
      Use Multi-Link Element
    The non-AP STAs affiliated with the non-AP MLD associated with the NSEP enabled AP MLD shall update the EDCA parameters on their respective links to the received NSEP dedicated EDCA parameter set within the time of Beacon Interval after receiving the action frames and use them for NSEP priority access.
    APs affiliated with AP MLD ensure that EDCA parameter sets sent in Beacon and Probe Response frames are degraded compared to NSEP EDCA parameters
  Discussion
    Advantages: provides NSEP EDCA parameters immediately when needed; compatible with methods to update NSEP EDCA parameters
    Disadvantages: Both AP & Non-AP MLD must communicate EDCA parameters to affiliated APs & STAs for each link
    Options for carrying multiple EDCA parameter sets
      Define new element that contains multiple (Link ID, EDCA parameter) pairs
        Advantages: Can be easily added to the existing frame as a simpler element that minimizes bloat
        Disadvantages: Requires new element; future enhancements would require changes to the element definition
      Use Multi-Link Element:
        Advantages: Provides flexibility and room for future enhancements; element is already defined for other purposes
        Disadvantage: Element contains many features not likely to be required for this purpose, and requires bundle with MLO

## Slide 6: NSEP EDCA Parameter Update: Option A NSEP EDCA in a Broadcast Action Frame
  Procedure (Will require changes to D1.2 – new frame)
    APs affiliated with AP MLD determine NSEP EDCA parameter sets for their respective links
    APs affiliated with NSEP-enabled AP MLD announce the NSEP dedicated EDCA parameter set on their respective links via a unsolicited broadcast Action frame
    Each NSEP non-AP STA that receives the broadcast frame shall update its EDCA parameter sets within the time of Beacon Interval after receiving the management frames which carry the NSEP EDCA parameters for that link and use them for NSEP priority access
      Note: Non-AP STAs that do not have NSEP priority access activated will ignore this frame
  Discussion
  Advantages: Broadcast Action frame sent only once on each link
  Disadvantages: Requires specification/development of a new unsolicited broadcast Action frame

## Slide 7: NSEP EDCA Parameter Update: Option B Reuse NSEP Priority Access Enable Request Frame
  Procedure (Will require changes to D1.2)
    APs affiliated with AP MLD determine an NSEP EDCA parameter set for their respective links
    One AP affiliated with NSEP-enabled AP MLD transmits multiple NSEP EDCA parameter sets (up to one per link) to a STA affiliated with NSEP-enabled non-AP MLD using NSEP Priority Access Enable request frame
    The STA affiliated with the non-AP MLD shall update their EDCA parameters to the received NSEP EDCA parameter set within the time of Beacon Interval after receiving the management frames which carry the NSEP EDCA parameters for that link and use them for NSEP priority access
  Discussion
  Advantages: Uses NSEP Priority Access Enable request frame already defined and required for related purpose
  Disadvantages: Unicast Action frame of NSEP Priority Access Enable request must be transmitted individually to each non-AP MLD that has NSEP priority access enabled

## Slide 8: Straw Poll 1
  Which option do you support for Initial NSEP EDCA parameter Distribution
    Option A: Using default EDCA parameters for NSEP as described in slide #4
    Option B: Using dedicated NSEP EDCA Parameters in Request/Response Frames as described shown in slide #5
    Option C: Do not care
  Results:

## Slide 9: Straw Poll 2
  Which option do you support for NSEP EDCA Parameter Update
    Option A: Distribute NSEP EDCA in a Broadcast Action Frame as described in slide #6
    Option B: Reuse NSEP Priority Access Enable Request Frame as described in slide #7
    Option C: Do not care
  Results: