## Slide 1: DMG Multi-Static PPDU structure
Date: 7-Oct-21
Author:

## Slide 2: Agenda
This presentation proposes a PPDU format and synchronization sequences for Multi-Static sensing in DMG.

## Slide 3: Reminder
In presentation 11-21-1431 we proposed the structure above for EDMG initiating transmitter multi-static sensing.
This structure requires sync sequences.
  In this presentation we propose a structure for PPDU and the sequences

## Slide 4: EDMG Multi-Static PPDU frame structure
The PPDU is an EDMG data MCS PPDU with a TRN field with the additions of sync fields.
A padding field makes sure that the sync fields together are equal in length to a multiple of TRN-Unit length
  this makes it easier to “spoof” legacy devices with the length of the PPDU, while allowing them to decode the PPDU
The TRN field now has P Channel Estimation TRN subfields per each responder STA – to allow all STAs to track the frequency and phase.
  each set of P TRN subfields are transmitted in the direction of a specific STA.
The sync fields are described in the next slides

## Slide 5: What is the purpose of the sequences
Each STA, except STA1 may not receive the preamble, header and data part of the PPDU.
  need to know when the TRN fields start
Each sync field is transmitted in the direction of a specific STA
  it may be received by other STAs, but possibly it will not.
The sync field must be unique per STA, so the STA will know how long does the TRN field starts after it.
The sync field should enable accurate synchronization of the receivers of all STAs that do not receive the PPDU header
  up to ~1 sample accuracy
The sync field should enable fine frequency offset estimate – we do not assume the use of an offset from the measurement setup frames.
  the STA may be able to receiver sequences directed to other STAs, it should be able to determine which sequence is directed to it.

## Slide 6: Proposed Structure for a Sync field
The sequence is composed of Golay Ga, Gb sequences, based on the first basic 128 samples Golay sequence used in 11ad.
The first part is used for detection and coarse frequency estimate.
  is assumed that AGC is already set and that the SNR is high enough to enable data transmission
The Ua and Ub are Golay Sequences.

## Slide 7: Proposed Structure (cont.)
The Multiplier M(r,q) are used to generate the Ua, Ub Golay sequences
  r is a STA index
  q is the Golay sequence index
The sequences are designed to have high correlation with the sequence directed to the STA and low correlation with sequence directed to other STAs.

## Slide 8: Performance
In the following slides we show the performance of the sync fields with the structure above.
The matrix used is an 8x8 matrix
Remember the purpose of the sequences to have an accurate sync and separate one sync sequence from those of other STAs
M(:,1) | M(:,2) | M(:,3) | M(:,4) | M(:,5) | M(:,6) | M(:,7) | M(:,8)
-1 | 1 | 1 | 1 | 1 | 1 | -1 | 1
1 | -1 | 1 | 1 | -1 | 1 | 1 | 1
-1 | 1 | 1 | 1 | -1 | -1 | 1 | -1
1 | -1 | 1 | 1 | 1 | -1 | -1 | -1
1 | 1 | -1 | 1 | -1 | -1 | -1 | 1
1 | 1 | -1 | 1 | 1 | 1 | 1 | -1
-1 | -1 | -1 | 1 | 1 | -1 | 1 | 1
-1 | -1 | -1 | 1 | -1 | 1 | -1 | -1

## Slide 9: Performance – output for STAs sync sequences vs output for other STAs sync sequences – no channel

## Slide 10: Performance – output for STAs sync sequences vs output for other STAs sync sequences– Conference Room LOS channel

## Slide 11: Performance – Performance – output for STAs sync sequences vs output for other STAs sync sequences – Conference Room NLOS channel

## Slide 12: Performance – output for STAs sync sequences vs output for other STAs sync sequences – Conference Room NLOS channel – 0dBSNR

## Slide 13: Performance – output for STAs sync sequences vs output for other STAs sync sequences – Conference Room NLOS channel – 0dBSNR

## Slide 14: Conclusions
We see that the proposed sync sequence enables both accurate timing detection and also determination with high probability that this is the sequence directed to the specific STA.

## Slide 15
Backup

## Slide 16: Comparison of proposed sync fields to existing constructs
The purpose of the sync fields is to enable:
  accurate synchronization (one sample accuracy)
  frequency offset estimation
  detection of whether this is the specific sync sequence for this STA.
  Accurate channel estimation of all syncs (except the one related to the STA) is not necessary
The length of the sequence is 13 Golay sequences
  for 8 STAs
There are two constructs in 11ay that enable channel estimation when multiple sequences are transmitted:
  Multi-STS (MIMO) CEF
  Multi-STS (MIMO) TRN subfields

## Slide 17: Comparison of proposed sync fields to existing constructs
The 11ay CEF and TRN subfield enable full CE for signals transmitted concurrently
  The length of the TRN subfield for 8 STA is 24 Golay sequences not including detection and frequency offset estimation fields.
  The length of the CEF for 8 STA is 55 Golay sequences not including detection and frequency offset estimation fields.
  Both sequences require 8 correlator running in parallel
Conclusion – The proposed sync sequences are shorter when more than two STAs are present.
They are better for the purposes they serve.

## Slide 18: TRN field performance - output for STAs sync sequences vs output for other STAs sync sequences – Conference Room NLOS channel – 0dBSNR