## Slide 1: Local Reporting of Sensing Measurements
Date: 2021-11-xx
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Background
According to specification framework SFD (0504r3),
a sensing receiver receives PPDUs sent by a sensing transmitter and performs sensing measurements in a sensing procedure.
the sensing receiver can use a sensing measurement reporting frame to report sensing measurements.
But there is no explicit statement in SFD that
  the sensing measurement can be used by the sensing receiver.
  the sensing measurement can be locally reported and consumed

## Slide 3: Local consumption of sensing measurement
  Applications can benefit from “local” reporting/consumption of sensing measurements (e.g. CSI) in the sensing receiver, instead of “nonlocal” reporting (transmit to sensing initiator using sensing measure report frame)/consumption (by sensing initiator).
  For example, the sensing initiator and the sensing receiver may be designed/operated by the same company to perform a sensing task jointly. The sensing initiator may be designed to set up the WLAN sensing network while the sensing receiver may be designed to perform locally a majority of the sensing computation (e.g. motion/breathing detection) based on locally reported sensing measurements. The locally computed sensing results (much simpler than raw sensing measurements) may be transmitted to the sensing initiator for fusion/further procession.
  Advantage: This would significantly reduce heavy network resources (signaling, bandwidth, air time, delay) needed in the nonlocal reporting, as sensing measurements (e.g. CSI) are sizable.
  Local consumption distributes sensing computation to many sensing receivers (=> relatively low computation/memory requirement for each), while nonlocal consumption centralizes ALL sensing computation in sensing initiator (=> high computation/memory requirement).

## Slide 4: Local reporting of sensing measurement
  We propose to report the sensing measurement locally in the sensing receiver via an MLME primitive so that the sensing measurement can be locally consumed by the sensing receiver.

## Slide 5: Straw Poll 1 (SP1)
Do you agree with the following statement?
  Sensing measurements may be reported locally in the sensing receiver via a MLME primitive.
Yes
No
Abstain