## Slide 1: Precision Control for Local Reporting of Sensing Measurements
Date: 2021-11-19
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Background
In our previous submission (xxxxr0),
We propose “local” reporting of sensing measurement in the sensing receiver via an MLME primitive so that sensing measurement can be consumed locally in the sensing receiver.
According to specification framework SFD (0504r3),
a sensing receiver receives PPDUs sent by a sensing transmitter and performs sensing measurements in a sensing procedure.
the sensing receiver can use a sensing measurement reporting frame to report sensing measurements. We call this “nonlocal” reporting.

## Slide 3: Precision Reduction for Nonlocal Reporting
Some (1705r0, 1676r1, 1573r1, 1676r0) propose to reduce precision of sensing measurement (e.g. CSI) by performing some quantization on it before sending it in the sensing measurement report frame. Advantages may include: reduced computation complexity, reduced hardware cost, increased/sustained throughput.
But for local consumption by the sensing receiver (or local reporting of sensing measurement), the sensing measurement can/should be reported at highest possible precision!

## Slide 4: No Precision Reduction for Local Reporting
We propose to skip any precision reduction measures applied to the sensing measurement for the purpose of nonlocal reporting in the sensing receiver. And sensing measurement shall be locally reported in the sensing receiver via an MLME with a highest precision supported by the hardware of the sensing receiver.

## Slide 5: Straw Poll 1
Do you agree with the following statement?
  Assuming local reporting of sensing measurement is available in the sensing receiver,
  any precision reduction measures applied to the sensing measurement for nonlocal reporting shall be skipped for the purpose of nonlocal reporting.
Yes
No
Abstain

## Slide 6: Straw Poll 2
Do you agree with the following statement?
  Assuming local reporting of sensing measurement is available in the sensing receiver,
  sensing measurement shall be locally reported in the sensing receiver via an MLME with a highest precision supported by the hardware of the sensing receiver.
Yes
No
Abstain