## Slide 1: Measurement Instance Sharing
Date: 2022-01-17
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Recall SFD, “Figure 1”: - Each measurement instance is associated with one measurement setup, though it can be associated with more than one sessions.

## Slide 3: Measurement Instance Sharing within a Session
According to SFD, one measurement instance is associated with one measurement setup.
However, it can be useful to associate a measurement instance with more than one measurement setups. This can reduce the total amount of measurement instances which implies less air time/bandwidth/network resources for sensing, less buffering memory, lower power, longer battery life, etc.

## Slide 4: Example1: Associating a measurement instance with more than one measurement setup ID (in red)
Session setup
Measurement Instance/Reporting
Measurement setup
Measurement setup
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
t=0
t=2
t=4
t=6
t=8
t=10
t=12
t=14
t=16
t=18
t=3
t=9
t=15
MAC ADDR=A. AID=1
Measurement setup ID=1, MAC ADDR=A. Period=2.
Measurement setup ID=2, MAC ADDR=A. Period=3.
Measurement instance ID=1, Measurement setup ID=1. Measurement instance ID=1, Measurement setup ID=2. AID=1.
Measurement instance ID=2, Measurement setup ID=1. AID=1.
Measurement instance ID=3, Measurement setup ID=1. AID=1.
Measurement instance ID=4, Measurement setup ID=1.
Measurement instance ID=3, Measurement setup ID=2. AID=1.
Measurement instance ID=5, Measurement setup ID=1. AID=1.
Measurement instance ID=6, Measurement setup ID=1. AID=1.
Measurement instance ID=7, Measurement setup ID=1.
Measurement instance ID=5, Measurement setup ID=2.
AID=1.
Measurement instance ID=8, Measurement setup ID=1. AID=1.
Measurement instance ID=9, Measurement setup ID=1. AID=1.
Measurement instance ID=10, Measurement setup ID=1. Measurement instance ID=7, Measurement setup ID=2. AID=1.
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement instance ID=2, Measurement setup ID=2. AID=1.
Measurement instance ID=4, Measurement setup ID=2. AID=1.
Measurement instance ID=6, Measurement setup ID=2. AID=1.
Sampling time of measurement setup 1
Sampling time of measurement setup 2
Common sampling time of measurement setup 1 and setup 2
Measurement instance with more than one measurement setup ID
Measurement instance with more than one measurement setup ID
Measurement instance with more than one measurement setup ID

## Slide 5: Measurement instances of measurement setup ID=1 (period=2) when there are two measurement setups.
Session setup
Measurement Instance/Reporting
Measurement setup
Measurement setup
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
t=0
t=2
t=4
t=6
t=8
t=10
t=12
t=14
t=16
t=18
t=3
t=9
t=15
MAC ADDR=A. AID=1
Measurement setup ID=1, MAC ADDR=A. Period=2.
Measurement setup ID=2, MAC ADDR=A. Period=3.
Measurement instance ID=1, Measurement setup ID=1. AID=1.
Measurement instance ID=2, Measurement setup ID=1. AID=1.
Measurement instance ID=3, Measurement setup ID=1. AID=1.
Measurement instance ID=4, Measurement setup ID=1. AID=1.
Measurement instance ID=5, Measurement setup ID=1. AID=1.
Measurement instance ID=6, Measurement setup ID=1. AID=1.
Measurement instance ID=7, Measurement setup ID=1. AID=1.
Measurement instance ID=8, Measurement setup ID=1. AID=1.
Measurement instance ID=9, Measurement setup ID=1. AID=1.
Measurement instance ID=10, Measurement setup ID=1. AID=1.

## Slide 6: Measurement instances of measurement setup ID=2 (period=3) when there are two measurement setups.
Session setup
Measurement Instance/Reporting
Measurement setup
Measurement setup
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
t=0
t=2
t=4
t=6
t=8
t=10
t=12
t=14
t=16
t=18
t=3
t=9
t=15
MAC ADDR=A. AID=1
Measurement setup ID=1, MAC ADDR=A. Period=2.
Measurement setup ID=2, MAC ADDR=A. Period=3.
Measurement instance ID=1, Measurement setup ID=2. AID=1.
Measurement instance ID=2, Measurement setup ID=2. AID=1.
Measurement instance ID=3, Measurement setup ID=2. AID=1.
Measurement instance ID=4, Measurement setup ID=2. AID=1.
Measurement instance ID=5, Measurement setup ID=2. AID=1.
Measurement instance ID=6, Measurement setup ID=2. AID=1.
Measurement instance ID=7, Measurement setup ID=2. AID=1.

## Slide 7: Measurement Instance Sharing across Sessions
According to SFD, one measurement instance is associated with one measurement setup.
However, it can be useful to associate a measurement instance with more than one measurement setups. This can reduce the total amount of measurement instances which implies less air time/bandwidth/network resources for sensing, less buffering memory, lower power, longer battery life, etc.
As one measurement instance can be associated with more than one session in SFD, a measurement instance associated with more than one measurement setups should be associated with more than one sets of {measurement setup ID, session ID}.

## Slide 8: Example2: Measurement instances with more than one {measurement setup ID, session ID} (in red)
Session setup
Measurement Instance/Reporting
Measurement setup
Measurement setup
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
t=0
t=2
t=4
t=6
t=8
t=10
t=12
t=14
t=16
t=18
t=3
t=9
t=15
MAC ADDR=B. AID=2
Measurement setup ID=1, MAC ADDR=A. Period=2.
Measurement setup ID=2, MAC ADDR=B. Period=3.
Measurement instance ID=1, {Measurement setup ID=1. AID=1.} Measurement instance ID=1, {Measurement setup ID=2. AID=2.}
Measurement instance ID=2, {Measurement setup ID=1. AID=1.}
Measurement instance ID=3, {Measurement setup ID=1. AID=1.}
Measurement instance ID=4, {Measurement setup ID=1. AID=1.}
Measurement instance ID=3, {Measurement setup ID=2. AID=2.}
Measurement instance ID=5, {Measurement setup ID=1. AID=1.}
Measurement instance ID=6, {Measurement setup ID=1. AID=1.}
Measurement instance ID=7, {Measurement setup ID=1. AID=1}
Measurement instance ID=5, {Measurement setup ID=2. AID=2.}
Measurement instance ID=8, {Measurement setup ID=1. AID=1.}
Measurement instance ID=9, {Measurement setup ID=1. AID=1.}
Measurement instance ID=10, {Measurement setup ID=1. AID=1.} Measurement instance ID=7, {Measurement setup ID=2. AID=2.}
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement Instance/Reporting
Measurement instance ID=2, {Measurement setup ID=2. AID=2}.
Measurement instance ID=4, {Measurement setup ID=2. AID=2.}
Measurement instance ID=6, {Measurement setup ID=2. AID=2.}
MAC ADDR=A. AID=1
Session setup
Measurement instance with more than one {measurement setup ID. Session ID}
Measurement instance with more than one {measurement setup ID. Session ID}
Measurement instance with more than one {measurement setup ID. Session ID}

## Slide 9: Straw Poll 1
IN 802.11bf, should a measurement instance be allowed to be associated with more than one measurement setup ID?
Yes
No
Abstain

## Slide 10: Straw Poll 2
IN 802.11bf, should a measurement instance be allowed to be associated with more than one {measurement setup ID, session ID}?
Yes
No
Abstain