## Slide 1: Discussion on Adaptation of MLO to Dynamic Changes in Link Conditions
Authors:
Name | Affiliations | Address | Phone | Email
Yoshihisa Kondo | ATR |  |  | kondo@atr.jp
Hiroyuki Yokoyama |  |  |  | 
Michio Miyamoto |  |  |  | 
Ayano Onishi |  |  |  | 
Toru Osuga | NICT |  |  | 
Tomoki Ohsawa |  |  |  | 
Fumiko Ohori |  |  |  | 
Satoko Itaya |  |  |  | 
Takeshi Matsumura |  |  |  | 
Date: 2021-12-10

## Slide 2: Introduction
11be MLO is expected to provide efficient and robust communications using multi-link
More discussions on multi-link transmission controls are needed for achieving ideal behaviors of MLO
In this contribution, we show example of multi-link transmission control and evaluation results for discussions

## Slide 3: Expected behaviors of multi-link transmissions
Maximize amount of data transmission per unit time
  If link conditions are same, Round-robin is best
Adapt to dynamic changes in link conditions
  Balance frame transmissions nicely
  Avoid causing large latency by exploiting alternative link(s)
    Sudden “Wait” caused by interferences
    Sudden increase of error rate
1
2
3
4
MLO
1
3
2
4
1
2
3
4
MLO
1
3
2
4
1
2
3
4
MLO
1
3
2
4
1
2
3
4
MLO
1
１
Retry
3
2
4
1
2
3
4
MLO
1
１
Retry
3
2
4
Balance
Exploit alternative link

## Slide 4: Design of multi-link transmission control
Design policy
  Follow structure of 802.11 MAC
  Based on protocols defined in 11be
  Maximize amount of data transmission per unit time
Design concept
  Enhance response
    Control on A-MPDU Tx buffer, lower part of MAC, is employed
  Enhance robustness
    All frames are replicated and stored in all Tx buffers for exploiting alternative links promptly
  Enhance efficiency
    Delivered frames on a link are deleted from all Tx buffers for mitigating redundant transmissions
1
１
Retry
3
2
4
Store replicated frames
Delete delivered frames
1
2
3
4
MAC
1
2
3
4
1
2
3
4
MAC

## Slide 5: Implementation of multi-link transmission control Mirroring + Merged BA （MMBA）
Information sharing
  Block Ack（BA）carries information of delivered frames on all links
Deletion of delivered frames
  Delivered frames on other links are deleted from Tx buffer according to received BA
Operation overview
  All frames are stored in all Tx buffers（Mirroring）
  Scoreboard contexts are shared among all Rx MACs
  Merged scoreboard information is sent to Tx MACs using BAs
  Each Tx MAC deletes delivered frames according to received BA
Wait/Retry
Wait/Retry
STA(Tx)
BA:1,2,3,4,
5,6,7,8,9
BA:1,2,3,4,
5,6,7,8
1
1
2
9
8
9
10
BA:9,10
1
2
3
4
5
6
7
8
9
10
BA:10
STA(Rx)
MAC
MAC
MAC
MAC
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
9
10
1
2
3
4
5
6
7
8
9
10
10
Tx buffer
Tx buffer
Sharing
ML
1
2
3
10
1
2
3
10
1
2
3
10
Mirroring

## Slide 6: Evaluation results Achieved data rate and channel occupation time for delivery of 100 frames
Round-robin
Mirroring
MMBA
（Total airtime including retransmissions and duplicated transmissions）
Chanel occupation [ms]
Achieved data rate [Mbps]
Round-robin：Efficiency becomes degraded as gap of link speed becomes larger
Mirroring：Achieved data rate becomes larger as gap of link speed becomes larger
MMBA：Efficiency is improved by frame deletion using sharing BA
Improved by Mirroring
Improved by MMBA
Good
Poor
Good
Poor
Combination of MCS of each link is different

## Slide 7: Conclusion
Adaptation to changes in link conditions is one of important capabilities of multi-link transmission
We showed a transmission control scheme which exploited shared Rx frame information carried by BAs for deleting delivered frames on other links
Our simulation results showed that the transmission control scheme improved achieved data rate efficiently when link conditions of multi-link are different

## Slide 8
Appendix

## Slide 9: Overview of simulation setup
Evaluated schemes
  Round-robin
    Allocate frames to each link in sequence order
  Mirroring
    Each frame is replicated and allocated to both links
  Mirroring + Merged BA（MMBA）
    Delivered frames deleted from all Tx buffers using sharing BAs
Simulation environment
  MAC and PHY: 11ax(EDCA)
  Simultaneous Tx/Rx device
CSMA/CA
Packet error
TX MAC 1
TX MAC 2
Alloc
APP
(Source)
CSMA/CA
Packet error
RX MAC 1
RX MAC 2
Reordering
APP
(Sink)
802.11
802.11
BA
BA
Notify
Notify
Latency measurement

## Slide 10: Measured latency when FER of a link becomes high
FER of Link-2 is changed from 0 to 0.8
Round-robin (Delivered via Link-1)
Round-robin (Delivered via Link-2)
MMBA (Delivered via Link-1)
MMBA (Delivered via Link-2)
MCS4 is applied to each link
Tx frame ID (Transmission interval is 100us)
Latency does not become larger even when FER of Link-2 becomes higher
Transmission from alternative link works efficiently when one of links is in a bad condition
1
2
3
4
1
2
3
4
1
１
Retry
3
2
4
1
Retry
１
3
2
4
・Behavior when Round-robin is applied
・Behavior when MMBA is applied
Latency
Latency

## Slide 11: Response time of frame deletion from Tx buffers
MMBA: Duplicated Tx occurs
MMBA: Duplicated Tx does not occur
(Frame deletion using BA works fine)
MCS4 is applied to each link
After 2 ms from start of blocking, frame deletion using sharing BA starts working
Duplicated
Non-duplicated
Start blocking of Link-2
2ms
Busy
AMPDU
AMPDU
i - j
i
j
k
BA
i - k
i
j
k
BA
Arrival of frames on Tx STA
Link-1
Delete i-k
AMPDU
(k +1) - l
Transmitted multiple times
These types of duplicated transmissions do not occur when MAC blocks are synchronized on a Tx STA
Tx frame ID (Transmission interval is 100us)