## Slide 1: Aggregation in Sensing Measurement Instance
Date: 2021-11-20
Authors:
Name | Affiliation | Address | Phone | Email
Mengshi Hu | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | humengshi@huawei.com
Rui Du |  |  |  | 
Yi Lv |  |  |  | 
Danny Kai Pin Tan |  |  |  | 

## Slide 2: Introduction (1/2)
In the SFD, the following WLAN sensing procedure is given:
  In the example, an initiator can establish multiple measurement setups (see blue blocks), each of which is identified by a measurement setup ID.
  Each measurement instance corresponds to one measurement setup ID in the example.
  In this contribution, the following topic is discussed:
  Can we have multiple measurement setup IDs in one measurement instance?
[Motion 29, 21/1543r1]
WLAN sensing procedure (example)

## Slide 3: Introduction (2/2)
Actually, the answer is yes, and a motion related to this has already passed:
  From the above motion, it can be seen that in the report frame of one measurement instance, results corresponding to different measurement setup IDs already can be aggregated.
  In this contribution, we further extend this concept to the following:
  Not only the reporting phase, but also the other phases corresponding to different measurement setup IDs can be aggregated.

## Slide 4: Instance with multiple measurement setup IDs
The benefit of having multiple measurement setup IDs in one measurement instance (call it aggregated measurement instance here) can be found in the following example:
  The last two yellow blocks are aggregated into one block in the example.
Instance with one measurement setup ID
Instance with multiple measurement setup IDs
Separate measurement
Aggregated measurement

## Slide 5: Benefits
The benefits of the aggregated measurement instance are:
  Devices related to different measurement setup IDs can share the same NDP sent from the initiator in an aggregated measurement instance.
  The initiator can trigger NDPs from devices related to different measurement setup IDs in an aggregated measurement instance.
  The initiator can trigger reports from devices related to different measurement setup IDs in an aggregated measurement instance.
  The overhead can be saved according to above procedures.
Instance with one measurement setup ID
Instance with multiple measurement setup IDs

## Slide 6: Details in aggregated instance (1/2)
Some examples of the phases in TB sensing measurement instance are given in the above figure. To achieve an aggregated measurement instance, the following designs should be considered:
  Aggregated NDPA
  Aggregated trigger
  Aggregated reporting
  Note: There is no need to change the format of an NDP. It can be shared by the receivers corresponding to different measurement setup IDs in the one-to-many case.
  E.g. Different sounding frequency -> use the larger one
  E.g. Different feedback types->feed back in one measurement instance
TB sensing measurement instance [Motion 29, 21/1543r1]

## Slide 7: Details in aggregated instance (2/2)
  Since the NDPA and trigger frames already support one-to-many signaling, it is easy to support signaling different measurement setup IDs to devices.
  For example, this information can be added to the Per User field to tell the corresponding measurement setup ID of a responder.
  Regarding sending NDPs from the responders in a TF sounding, since resources can be divided into different pieces (such as RUs, spatial streams, etc.), it is easy to support sending NDPs corresponding to different measurement setup IDs.
  Regarding the reporting phase, since resources are divided into different pieces (such as RUs, spatial streams, etc.), it is easy to support reporting feedbacks corresponding to different measurement setup IDs.

## Slide 8: Summary
In this contribution an aggregated measurement instance was proposed, which supports doing sensing measurements with the devices corresponding to different measurement setup IDs.
  Compared with the traditional measurement instance which only corresponds to one measurement setup ID, the proposed aggregated measurement instance saves overhead by aggregating multiple instances into one.

## Slide 9: SP 1
Do you agree to define an aggregated measurement instance which supports doing sensing measurements with the responders corresponding to different measurement setup IDs in the WLAN sensing procedure?
  Y
  N
  A