## Slide 1: Discussion on Session Setup
Date: 2022-2-28
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that a sensing session is an agreement between a sensing initiator and a sensing responder to participate in a WLAN sensing procedure. [1]
This contribution discusses more about the detail of session setup procedure and frame formats.

## Slide 3: Overview and focus
WLAN Sensing procedure may comprise of several phases [1].
This contribution focuses on Sensing Discovery and Sensing Session Setup.
Sensing Initiator
Sensing Responder
Sensing Measurement Setup
Sensing Measurement Instances
Sensing Measurement Setup Termination
Sensing Session Setup
Sensing Session Termination
Sensing Discovery

## Slide 4: Abstract
Sensing Discovery is the exchange of sensing capabilities (essential and detailed), two options of the procedure are discussed.
  Option 1: A two-way Sensing Capability Information frame exchange initiated by non-AP STA, after 4-way HS or PASN.
  Option 2:
    Non-AP STA’s sensing capabilities in Probe Request/Assocciate Request/Responder Information Notify
    AP’s sensing capabilities in Beacon/Probe Response/Association Response.
Sensing Session, Sensing Session Setup and Sensing Session Termination phases are removed.
Note: since the case for associated STAs is straightforward, we mainly discuss the case of unassociated STAs in this contribution.

## Slide 5: Discussion: Essential Sensing Capabilities
Essential Sensing capabilities are carried in Extended Capabilities element and includes:
  support of SBP procedure
    Note: Support of SBP procedure for a non-AP STA means the non-AP STA supports SBP requester role
    Note: Support of SBP procedure for an AP means the AP supports SBP responder role
  support of TB measurement procedure
  support of non-TB measurement procedure
Other sensing capabilities in Extended Capabilities element are TBD.

## Slide 6: Discussion: Detailed Sensing Capabilities
Detailed sensing capabilities are carried in Sensing Capabilities element and includes:
  sensing measurement result types supported, e.g., CSI, TCIR
  support of sensing receiver role
  support of sensing transmitter role
  support of sensing initiator role
  support of sensing responder role (Note to editor: replace it with its sub-bullets)
    support of TB sensing responder role (for non-AP STA only)
    support of non-TB sensing responder role (whether it’s for AP only is TBD)
  support of threshold based sensing
  support of aggregated reporting (Note to editor: replace it with its sub-bullets)
    support of aggregated reporting as a sensing initiator
    support of aggregated reporting as a sensing receiver
    Note: refer to motion 34 for the exact meaning of these two capabilities.
Other capabilities in Sensing Capabilities element are TBD.

## Slide 7: Option 1 for sensing discovery
An unified procedure for associated STA or unassociated STA.
An non-AP STA, which intends to initiate or join a sensing procedure, shall peform a detailed sensing capability exchange, after PASN or 4-way HS.
Beacon and Probe Response shall carry the essential sensing capabilities of the AP.
Probe Request/Response and Association Request/Response may also carry the detailed sensing capabilities of a STA. (TBD)
‘Invitation of Responder’: indicates whether to invite an intended STA to join a sensing measurement as a sensing responder, so the unassociated STA may stand by and wait for a predefined timeout T1.

## Slide 8: Option 2 for unassociated STA as responder
Since an unassociated STA has no idea of whether the AP needs it, Unicast Probe Response frame shall carry an ‘Invitation of Responder’ bit, which indicates whether to invite the intended STA to join a sensing measurement as a sensing responder.
A Responder Information Notify (denoted as RIN) frame carrying the detailed sensing capabilities of the unassociated STA is sent to trigger the AP to send MS Request.
Note:
  This RIN frame is required only if the unassociated STA is capable and intends to participate as a sensing responder.
  T1 is the timeout for AP to initiate the MS Request, which indicates how long the STA will stand by.

## Slide 9: Option 2 for unassociated STA as initiator
An unassociated STA, which intends to initiate a measurement setup, gets the detailed sensing capabilities of the responder in Beacon and/or Probe Response.
Note: The RIN frame is not required in this case.
Note: It’s straightforwat that an associated STA exchanges sensing capability information with AP using Associate Request/Response in this option, no much to discuss.

## Slide 10: Discussion: Sensing Session
Sensing Session in SFD:
  A WLAN sensing procedure is composed of one or more of the following: sensing session setup, sensing measurement setup, sensing measurement instance, sensing measurement setup termination, and sensing session termination.
  In the sensing session setup of a WLAN sensing procedure, a sensing session is established, and operational parameters associated with the sensing session are determined and may be exchanged between STAs.
  A sensing session is pairwise and is identified by MAC addresses and/or associated AID/UID.
  A sensing initiator may maintain multiple sensing sessions.
Are there any possible operational parameters should be exchanged in session setup?
  No session specific operational parameter has been identified.
  Operational attributes are exchanged in measurement setup.
Proposal: remove sensing session, and remove related sensing session setup and sensing session termination phases.

## Slide 11: Proposal: modified SFD text
Modify the related SFD text as following:
  A WLAN sensing procedure is composed of one or more of the following: sensing session setup, sensing measurement setup, sensing measurement instance, sensing measurement setup termination, and sensing session termination.
  In the sensing session setup of a WLAN sensing procedure, a sensing session is established, and operational parameters associated with the sensing session are determined and may be exchanged between STAs.
  A sensing session is pairwise and is identified by MAC addresses and/or associated AID/UID.
  A sensing initiator may maintain multiple sensing sessions establish a measurement setup with multiple sensing responders.
  A sensing responder may join multiple measurement setups, established by either the same sensing initiator or different sensing initiators.

## Slide 12: Proposal: AID/UID assignment
AID of the STA is allocated by AP and sent to the STA in (Re)Association Response.
  Note: to have a unified measurement setup (denoted as MS) request frame, AP may also send AID of the STA in MS request again. e.g., AP sends MS request to associated STA 1, carries AID1 of STA1 (AID1 was assigned during association)
UID of the STA is allocated by AP and sent to the STA in the first MS request frame.
Proposal: a unified MS request frame, which always carries an AID/UID of the responder.
  AP initiated MS with associated non-AP STA: e.g., AP sends MS request to associated STA 1, carries AID1 of STA1.
  AP initiated MS with unassociated non-AP STA: UID is in every measurement setup request, STA could reject if mismatch. e.g., AP sends MS request to unassociated STA 2, carries the UID2 assigned to STA 2.
  (Associated or unassociated) Non-AP STA initiated MS with AP: AID/UID of the initiator is not needed. e.g., (associated or unassociated) STA 3 sends MS request to AP, carries AID of AP (it's always 0).

## Slide 13: SP 1
Which option do you prefer for sensing capability exchange?
  O1: A two-way Sensing Capability Information frame exchange as shown in slide 7.
  O2: A RIN frame as shown in slide 8 and 9.
  O1/O2/A
Chaoming Luo (OPPO)

## Slide 14: SP 2
Do you agree to add the following into 11bf SFD ?
  The Extended Capabilities element carries essential sensing capabilities as shown in slide 5.
  A Sensing Capabilities element is defined, which carries detailed sensing capabilities as shown in slide 6.
  Other sensing capability information is TBD.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 15: SP 3
Do you agree to modify the SFD the text changes as shown in slide 11?
  Y/N/A
Chaoming Luo (OPPO)

## Slide 16: SP 4
Do you agree to add the following into 11bf SFD ?
  Measurement setup request frame includes an AID/UID field. The AID/UID field indicates the AID/UID assigned to the intended non-AP STA by the AP, or the AID of the intended AP.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 17: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
[2] 11-21-1828-03-00bf-mesurement-setup-frame-formats
Chaoming Luo (OPPO)

## Slide 18: Backup: capability exchange
Case 1: A non-AP STA broadcasts probe request due to any of the following reasons
  Finds another BSS to join (or catalog for roaming later), mostly intend for communication.
  Finds an AP that supports SBP responding STA role, because the non-AP STA needs an proxy to initiate sensing procedure for it.
  Finds an AP that supports responder role, because the non-AP STA wants to initiate a non-TB sensing procedure.
  Finds an AP that supports sensing.
Case 2: A non-AP STA retrives information of an AP from Beacon. The non-AP STA may broadcast/unicast probe request to get more information.
Case 3: A non-AP STA exchanges capability information with AP using Associate Request/Response.