## Slide 1: Discussion on Session Termination
Date: 2021-11-29
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
The SFD states that: in the sensing session termination, STAs stop performing measurements and terminate the sensing session. [1]
This contribution discusses about the detail rules for sensing session termination.

## Slide 3: Discussion: how to terminate a sensing session
Who may initiate to terminate a pairwise <STA, AP> sensing session?
  STA may initiate to terminate a sensing session, e.g., due to low battery or heavy uplink traffic load.
  AP may also initiate to terminate a sensing session, e.g. due to heavy downlink traffic load.
Implicit termination:
  When an associated STA is disassociated with the BSS, the sensing session is automatically terminated.
  Expiration of a predefined inactivity time may also terminate a sensing session. (TBD)
Explicit termination:
  Either side of a pairwise sensing session can initiate a sensing session termination procedure.

## Slide 4: Discussion: how to terminate a sensing session (Cont.)
After a sensing session for a <STA, AP> pair is terminated, all the measurement setups for the same <STA, AP> pair are also terminated.
  E.g., if session 2 is terminated, measurement setup 1 and 2 for <STA2, AP> pair are also terminated.
Termination of one sensing session does not impact the activity of another sensing session.
  E.g., termination of session 2 does not impact measurement setup 1 and 2 of <STA 3, AP> pair.

## Slide 5: Discussion: Explicit Termination Procedure
F1:
AP initiates sensing session termination as:
STA initiates sensing session termination as:
F2:

## Slide 6: Discussion: Sensing Session Termination Frame Format
Frame dependent fields and elements [2] for sensing session termination frame:
  Reason Code: indicates the reason to terminate this session. (size TBD)

## Slide 7: SP 1
Do you agree to add the following into 11bf SFD?
  When an associated STA is disassociated with the BSS, the corresponding sensing session, if present, is automatically terminated.
  Either side of a pairwise sensing session can initiate a sensing session termination procedure, by sending a sensing session termination frame.
  After a sensing session for a <STA, AP> pair is terminated, all the measurement setups for the same <STA, AP> pair are also terminated.
  Termination of one sensing session does not impact the activity of another sensing session.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 8: SP 2
Do you agree to add the following into 11bf SFD?
  The sensing session termination frame is a Public Action frame with a sensing subtype and a reason code, the format is shown as the figure in slide 6.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 9: Reference
[1] 11-21-0504-03-00bf-specification-framework-for-tgbf
[2] 11-21-1828-02-00bf-mesurement-setup-frame-formats
Chaoming Luo (OPPO)