## Slide 1: Discussion on Measurement Setup ID Setting
Date: 2021-12-27
Authors:
Name | Affiliation | Address | Phone | Email
Pei Zhou | OPPO |  |  | zhoupei1@oppo.com
Chaoming Luo |  |  |  | 
Lei Huang |  |  |  | 
Ning Gao |  |  |  | 

## Slide 2: Background
According to [1] and [2], the following rules/contents are agreed by TGbf:
  The Measurement Setup ID identifies the attributes/parameters agreed upon between the initiator and one or more responders [1].
  The Measurement Setup ID may be used to identify attributes of the sensing measurement instances [2] (Motion 24).
  An optional negotiation process in the sensing measurement setup is defined that allows for a sensing initiator and a sensing responder to exchange and agree on operational attributes associated with a sensing measurement instance [2] (Motion 17, Motion 23, Motion 29). The operational attributes may include initiator’s and responder’s roles, measurement report types, and other operational parameters [2] (Motion 29).

## Slide 3: Issue: Measurement Setup ID Conflict
Assumption: Either STA or AP can act as Sensing Initiator to initiate Measurement Setup(s) within a Sensing Session. Measurement Setup ID is set by Sensing Initiator. The Sensing Initiator and Sensing Responder only use Measurement Setup IDs to identify attributes/parameters.
Issue: The Measurement Setup IDs set by different Sensing Initiators (STAs) may conflict.
Case study: When STA 2 acts as Sensing Initiator to initiate a measurement setup, it doesn’t know the Measurement Setup ID (e.g., x = 3) set by STA 1. Then, STA 2 may set the same Measurement Setup ID (y = 3) with STA 1. From the Sensing Responder (e.g., AP) side, it can not identify the attributes/parameters agreed with the different Sensing Initiators (e.g., STA 1 and STA 2).

## Slide 4: Proposal
The following 2 options are proposed to solve the potential conflict of Measurement Setup IDs:
Option 1: Measurement Setup ID is set by Sensing Initiator, the tuple <Sensing Initiator’s MAC address, Measurement Setup ID> is used to identify a specific Measurement Setup.
Option 2: The Measurement Setup ID is always set by AP, the Measurement Setup ID is used to identify a specific Measurement Setup.
  If STA is Sensing Initiator, it can request the AP (Sensing Responder) to set the Measurement Setup ID through Sensing Measurement Setup Response frame.

## Slide 5: Summary
We highlighted the issue of Measurement Setup IDs conflict, and proposed two possible solutions.
*Note: P2P Sensing may be considered by TGbf later.
Option 1 is preferred since it has better flexibility and supports more sensing scenarios.
 | Pros. | Cons.
Option 1 | Better flexibility: Sensing Initiator (either AP or STA) can set Measurement Setup ID(s) directly. Applicable to P2P Sensing*. | More memory is required to store the Measurement Setup identification.
Option 2 | Measurement Setup ID is enough to identify attributes/parameters. | Less flexibility: Only AP sets Measurement Setup ID(s). Not applicable to P2P Sensing*.

## Slide 6: SP
Do you agree to add the following into the 11bf SFD:
Measurement Setup ID is set by Sensing Initiator, the tuple <Sensing Initiator’s MAC address, Measurement Setup ID> is used to identify a specific Measurement Setup.
How the SBP Requesting STA identifies the sensing measurement is TBD.
Yes/No/Abstain

## Slide 7: Reference
[1] 11-21-1701-01-00bf-measurement-setup-termination.pptx
[2] 11-21-0504-04-00bf-specification-framework-for-tgbf.docx
[3] 11-21-1692-04-00bf-enhancing-client-based-sensing-sensing-by-proxy.pptx