## Slide 1: TGbe Proposed Solution to NSEP Omission
Date: 2021-12-06
Authors:

## Slide 2: Revision History
Revision | Date | Description
0 | 2021-12-06 | Initial version identifying issues and proposing solution

## Slide 3: Abstract
This document identifies an issue with the current NSEP feature description and proposes a solution.

## Slide 4: NSEP Feature Omission
Current NSEP feature definition does not allow AP-initiated teardown
  AP initiated tear down may be required when the non-AP STA that initiated the NSEP priority treatment loses communication with its NSEP AP without issuing a Tear-down request.
  AP initiated tear down may be required if the NSEP AP receives notice that an NSEP non-AP STA has had its NSEP permission revoked.
  If an NSEP AP receives a notification to de-activate its NSEP capability, it is not clearly defined how that AP would handle that situation if NSEP service is active to one or more non-AP STAs.
December 2021

## Slide 5: Current NSEP feature definition does not allow AP-initiated teardown
Issue
Non-AP STAs may lose communication with an NSEP AP while a priority session is active for a number of reasons:
  Battery exhaustion
  Non-AP STA is moved outside of the NSEP AP’s range (drive away)
  Non-AP STA has its communication interfered with (device is taken inside another building)
Current messaging specification does not allow an NSEP AP to terminate a priority session without communication from the non-AP STA that activated the priority session.
Recommendation
Allow an NSEP AP to terminate an NSEP priority session
  The NSEP may support a hysteresis period allowing a brief period of loss of comms with an NSEP non-AP STA before the NSEP AP tears down the session.
  If more than one non-AP STA has authenticated and established NSEP priority sessions with an NSEP AP, the AP may maintain the NSEP priority settings in the other non-AP STAs even if one of the NSEP STAs loses communication with the NSEP AP.
  The NSEP AP may send a termination message to the NSEP non-AP STA in case it is still capable of receiving transmissions to notify it that its session has been terminated

## Slide 6: 1) Current NSEP feature definition does not allow AP-initiated teardown (cont’d)
Issue
AP initiated tear down may be required if the NSEP AP receives notice that an NSEP non-AP STA has had its NSEP permission revoked.
  An NSEP non-AP STA’s authentication may be revoked while that device has an active NSEP session.
  802.11 specification does not address how that authentication is instantiated, but the possibility that an authentication is withdrawn should be addressed.
  Also, the text for the MIB indicates that is read-only but also that it is set by an SME or other higher layer entity.
Current messaging specification does not allow an NSEP AP to terminate a priority session without communication from the non-AP STA that activated the priority session.
Recommendation
Allow an NSEP AP to terminate an NSEP priority session
  If more than one non-AP STA has authenticated and established NSEP priority sessions with an NSEP AP, the AP may maintain the NSEP priority settings in the other non-AP STAs even after being notified that one of the non-AP STAs is not longer authenticated.
  The NSEP AP may send a termination message to the NSEP non-AP STA with a reason code that its authentication has been withdrawn.

## Slide 7: Current NSEP feature definition does not define how an AP (or AP MLD) suspends NSEP service
Issue
If an NSEP AP receives a notification to de-activate its capability, it is not clearly defined how that AP would handle that situation if NSEP service is active to one or more non-AP STAs.
  The capability MIB describes that the MIB may be set or cleared by a higher layer (dot11EHTNSEPPriorityAccessActivated), but the MIB is also marked as ‘read-only’.
  If the capability MIB is cleared, it is not clear how the AP should respond.
Current messaging specification does not allow an NSEP AP to terminate a priority session without communication from the non-AP STA that activated the priority session.
Recommendation
Allow an NSEP AP to terminate an NSEP priority session
  The NSEP AP may send a termination message to any NSEP non-AP STAs that have active priority sessions to notify them that their sessions have been terminated.

## Slide 8: Straw Poll #1
Do you support the addition of a method/message for an NSEP AP with an active NSEP prioritization session to terminate the session without a termination message from the NSEP STA who initiated the prioritization session?