## Slide 1: DMG Passive Sensing
Date: December 27, 2021
Author:

## Slide 2: Agenda
This presentation proposes a method to enable DMG beacon based passive sensing.

## Slide 3: DMG Passive sensing - motivation
In passive sensing, transmissions that are not specifically designed for sensing are used by other devices for sensing.
In DMG, beacons are transmitted regularly, to many directions
  usually, every 100ms
Beacons can be used for passive sensing by other devices

## Slide 4: If we want to use beacons – do we need any spec changes?
Some minor changes are needed to make it more effective:
  The sensing device needs to know in which direction the beacon was transmitted
  The sensing device needs to know the location of the PCP/AP
  The sensing device may benefit from beacons being transmitted at high time accuracy
    use waveform from one beacon to synchronize signals received in another beacon.
  TRN sequences may be added to beacons to enable STAs to sense in several directions (no change is needed)
It is expensive to transmit all this information in the beacon due to large number of bits and low bit rate of the beacon.

## Slide 5: Solution: an information request
The AP uses one bit in the DMG capabilities element to indicate that is supports passive sensing
  it also indicates support of accurate timing of beacons.
A STA that wants to know the direction and location information of the beacon would send an information request to the PCP/AP
The PCP/AP would respond with a frame with an information report.

## Slide 6: PCP/AP Sensing Information report
The Sensing Information report will include:
  location of the PCP/AP
  direction of each sector:
    list of sector ids, azimuth and elevation
The sensing information request and sensing information response are transmitted in data MCS (MCS>0)

## Slide 7: Straw Poll
Do you agree to add to the SFD:
DMG passive sensing is enabled by
  capability bit in the beacon
  Sensing information request and response that will provide information the about the beacon
  Sensing information include:
    azimuth and elevation for each sector id (of beacons)
    location information of the PCP/AP